## Slide 1
AVIATION OPERATIONAL MEASURES FOR FUEL AND EMISSIONS REDUCTION WORKSHOP
ENGINE DETERIORATION
AND
ON-WING PROCEDURES TO RECOVER PERFORMANCE
Robert E. Owens
Manager of Vehicle Systems Analysis
Pratt & Whitney

## Slide 2: Presentation Outline
Engine Deterioration
  Mechanisms
  Effect on Performance
On-Wing Maintenance Actions
  Process and tools
  Potential gains
  Projected savings

## Slide 3: Engine Components Are Affected by Their Operating Environment

## Slide 4: Typical Deterioration Mechanisms
Increased
Tip Clearances
Seal
Leakage
Airfoil Erosion
Dirt
Accumulation

## Slide 5: Typical Engine Performance Deterioration (Un-refurbished)
Cycles or Hours
Specific
Fuel
Consumption
or
Exhaust Gas
Temperature

## Slide 6: EGT to Achieve Thrust is Measure of Deterioration

## Slide 7: Scheduled Refurbishing Recovers SFC and EGT

## Slide 8: Simple Procedures to Recover Performance Between Shop Visits
On-Wing Engine Washing
  addresses dirt accumulation
On-Wing Engine Bleed Rigging
  addresses leakage caused by bleed system wear

## Slide 9: On-Wing Engine Washing Regular Intervals Ensure Fuel Economy
Simple procedure
Special tooling identified
3-4 hours, two mechanics
Payoff :
Up to 1.5%
SFC Benefit
Hand wash fan
and LPC stator vanes

## Slide 10
SFC and EGT Recouped Between Shop Visits with Repetitive Engine Wash
0.0
0.5
1.0
1.5
2.0
2.5
3.0
3.5
4.0
0
1000
2000
3000
4000
5000
6000
500 Cycle-Wash
Deterioration Curve
1000 Cycle -Wash
Deterioration Curve
Un-Washed
Deterioration Curve
Cycles
% Delta TSFC
1000 Cycle Wash
Unwashed
500 Cycle Wash
0.5%
1000 Cycle Wash
Cumulative Benefit
0.75%
500 Cycle Wash
Cumulative Benefit
Sample Impact of Water Wash Frequency

## Slide 11: On-Wing Water Wash Cost - Benefit
Costs
  6-8 man-hours per wash
  waste water disposal
  airplane down time
Benefits (annual per engine)
  fuel savings of $20000 to $30000
  CO2 reduction of 190 to 290 tonnes
  maintenance cost savings of $4000 to $6000
Note: 777 type airplane, 6.5 hr cycle, 620 cycles/yr., $1.00/gallon fuel

## Slide 12: On-Wing Engine Bleed Rigging Repair of Leaking Bleed Valves Saves Fuel
Simple Procedure
Start, Stability, Service Bleeds
Problem Noted from in-flight performance trends
Up to 2.5% SFC Benefit

## Slide 13: On-Wing Engine Maintenance Simple Procedures Can Save Fuel
On-Wing water wash saves fuel and recovers EGT, extending time between shop visits
Attention to bleed system rigging prevents excessive fuel consumption

## Slide 14
AVIATION OPERATIONAL MEASURES FOR FUEL AND EMISSIONS REDUCTION WORKSHOP
Thank you !