## Slide 1
AVIATION OPERATIONAL MEASURES FOR FUEL AND EMISSIONS REDUCTION WORKSHOP
Fuel Advisory Board
Juan Polyméris
Dr. sc. techn. ETHZ
Strategic Projects Flight Operations
& Fuel Advisory Board

## Slide 2: FAB - mission swissair
The Swissair Fuel Advisory Board was established in 2000. Lead: Flight Operations, a committee comprising ten specialists from within the Group.
We identified recurring fuel savings in the order of magnitude of 10+ Mio$ and realized a ‘significant’ budget improvement (Swissair) 2001 of 6+ Mio$.

## Slide 3: FAB - mission swiss
We resumed immediately – spring 2002 – with three people from Swiss Flight Operations and having full support from our management.
We are prepared to implement measures and realize further benefits & quick wins. FAB target is an agreed budget improvement 2002 in the order of magnitude of 1+ Mio$.

## Slide 4: FAB - problem & solution
Problem: Lack of operational-technical facts & figures in order to ‘convince’ our flight crews & management – improve the overall cost & environmental awareness.
Solution: Implementation of the Event Measurement System (Austin Digital Inc.) + additional flight information & ‘intelligence’.
   conclusion: ‘hardware’ + ‘software’ plus continuity.

## Slide 5: FAB - problem & solution
The EMS – a tremendously powerful tool designed for flight operations & maintenance quality assurance – not only detects events, but also measures the engineering & operational parameters of the flight.
It gives us the ability to understand how the aircraft are flying and allows Operations to easily support the information requirements of the various engineering departments.

## Slide 6: FAB - problem & solution
Flight Data Warehouse & Analysis.
Event Detection.
Parameter Measurement & Flight Data Viewer 
  software to detect and measure virtually every aspect of a flight; e.g. average true airspeed during climb in function of climb rate, average machnumber for the first five flighthours after top of climb etc.

## Slide 7: FAB - mission, cont.
The primary goal is to reduce fuel consumption & cost without compromising safety, community noise & emissions and optimize the operational weight of the aeroplane.
For the time being we are forced to minimize our efforts and decided to concentrate our work implementing the EMS and to operational measures for fuel savings in the cruise phase of flight.

## Slide 8: FAB - work done / in progress
Aircraft weight is a major factor in fuel consumption. Apart from the empty weight and the payload (passengers & cargo), the fuel in the tanks and the goods needed for in-flight service contribute to the total weight.
All parties within our Group are constantly seeking to achieve weight reductions;

## Slide 9: FAB - work done / in progress
  e.g. A340-300 introduction / specification & weight guarantees, flexible drinking water replenishment, fitting of a ‘zonal dryer’ system to drive out moisture from the insulation blankets, JAR-OPS fuel policy, ULD weight reduction, excess customer service items, baggage overweight etc.

## Slide 10: FAB - work done / in progress
Our work has shown that weight-saving measures yield the greatest environmental yield (without causing any ‘problematic’ sideeffect).
Cost savings; e.g. enhanced fuel ferry tool – 2+ Mio$ per year recurring cost reduction –, new route comparison tool & overflight charges etc.

## Slide 11: FAB - work in the ‚pipeline‘
Operational measures;
  e.g. further reduction in high speed flying long-haul, ICAO B procedure, enhanced flight plan optimization & variable mach cruise calculation, make use of best available planning assumptions; e.g. actual zero fuel weight & last minute OFP, reduction of the remaining fuel on board landing at the home destination etc.

## Slide 12: FAB - work in the ‚pipeline‘
Technical items;
  e.g. A340-300 / CFMI performance retention guarantees, MD11 engine wash (A320/A330 done, A340-300 planned), enhanced CG calculation (A340), APU running time etc.,
  fuel additives in order to reduce emissions on ground etc.

## Slide 13: FAB - reduction in high speed flying
‘The idea’: Our MD11 fuel (1999) audit showed an average HSC far above 40% of which half could be reduced to normal speed resulting in an agreed annual saving of at least 3+ Mio$ (cargo penalty not quantified). .
Facts & figures re. cruise – above FL 290 – with speeds higher than ‘normal cruise’ – machnumber > 0.83 or > 0.82:

## Slide 14: FAB - reduction in high speed flying
MD11 (2000) > 0.83:
  ~ 30% to above 50%
   less than 20% (2001)
A330-200 (2000) > 0.82:
  ‘best guess’ > 30%
   less than 10% (2001)
Goal: Assure best practice & transparency re. fuel consumption, punctuality etc.

## Slide 15: FAB - reduction in high speed flying
Introduction of a High Speed Policy (A320/A330/A340 & MD11 Aircraft Operating & Route Manual):
Priority 1 Flight – according to TOI – High Speed Procedures apply whenever possible.
Priority 2 Flight – High Speed only if so dictated to meet operational requirements given to the crew via telex, TOI, ACARS or other means.

## Slide 16: FAB - reduction in high speed flying
“As the use of High Speed procedures leads to an increased fuel consumption, every decision to fly with speeds higher than Normal Cruise shall be made only after careful consideration of all factors.
The partial application of high speed procedures (e.g. variable cost index, only high speed climb or high speed descent etc.) may often be sufficient to meet the above requirements”.

## Slide 17: FAB - reduction of remaining fuel
‘The idea’: Our analysis – A330-200 remaining fuel on board at touch down, before and after introduction of the JAR-OPS fuel policy – showed an average reduction of 500 kg per long-haul flight resulting in an agreed annual saving of at least 500’000+ $.
An MD11 survey showed an average extra fuel amount for NAT-flights in the order of magnitude of 2.5 t with ‘good’ & stable forecast conditions.

## Slide 18: FAB - reduction of remaining fuel
It clearly shows that additional savings of approx. 500’000+ $ can be reached fleetwide specifically through a reduction of 2.5 t to 1.8 t extra fuel (MD11 fleet).
Our analysis re. A330 remaining fuel ex. DEL & DXB showed a median equal to 8’400 kg & 9’200 kg fuel on board at touch down – incl. 1.5 t company fuel – with less than 5% having less than 6.4 tons remaining.

## Slide 19: FAB - reduction of remaining fuel
We expect a significant improvement after RVSM (Reduced vertical separation Minima) implementation.
Reliable facts & figures required in order to identify operational measures and corresponding benefits for fuel savings in the cruise phase reducing the weight of the – extra – fuel in the tanks no further recommendations done for the moment.

## Slide 20: FAB - quantitative goals
Statistical & operational analysis tool:
we keep a close eye on fuel consumption, aided by improvements in our fuel information system, fuel & weight monitoring, keeping track on performance guarantees & deterioration in specific range, providing figures in order to compare our fuel efficiency with other airlines, fuel budget process improvement etc.

## Slide 21: FAB - some facts / order of magnitude
+1% fuel consumption A330 fleet 
  1+ Mio$ / y recurring costs.
+1% fuel consumption A340 fleet 
  1+ Mio$ / y recurring costs.
+100kg weight increase A340 
  500’000+ $ per year recurring costs (complete A340 fleet; fuel & cargo).

## Slide 22: FAB - some facts / order of magnitude
+1kg weight increase MD11 
  400+ $ per A/C & year
  (recurring costs fuel & cargo).
+/- 1/100 machnumber A340-300 (0.82  0.83) 
  +/- 0.7 min per flighthour 
  +/- 5% fuel burn.

## Slide 23
AVIATION OPERATIONAL MEASURES FOR FUEL AND EMISSIONS REDUCTION WORKSHOP
muchissimas gracias !