## Slide 1
AVIATION OPERATIONAL MEASURES FOR FUEL AND EMISSIONS REDUCTION WORKSHOP
Fuel Conservation
Airframe Maintenance for Environmental Performance
Rob Root
Flight Operations Engineer
Boeing Commercial Airplanes

## Slide 2
Maintenance Personnel
  Airframe maintenance
  Systems maintenance
Opportunities for fuel conservation:
Notes: - Managing "condition" of the airplane is different from managing the "operation." A new airplane is the best it's going to get. mantainence is there to keep it from deteriorating.
- Systems: ECS leaks, re-circ fans, FAMV's, anything in the MMEL that incurs a fuel-burn penalty.

## Slide 3: Excess Drag Means Wasted Fuel
1% Drag in Terms of Gallons per Year
737  15,000
727  30,000
757  25,000
767  30,000
777  70,000
747  100,000
Notes: <number>
<footer>
<header>
<date/time>
8
8
8

## Slide 4
Compressible Drag  Drag due to Mach
  Shock waves, separated flow
Induced (Vortex) Drag  Drag due to Lift
  Wing, trim drag
Parasite Drag  Drag NOT due to Lift
  Shape of the body, skin friction, leakage, interference between components
  Parasite Drag Includes EXCRESCENCE drag
Total Drag Is Composed Of:

## Slide 5
Contributors to Total Airplane Drag
Drag due to
airplane size
and weight
(unavoidable)
~ 90%
Pressure, trim and interference drag (optimized in the wind tunnel) ~ 6%
Excrescence drag (this can increase)
~ 4%
Notes: - Due to A/P size is just physics; can't do too much about it. (Skin friction drag and induced drag).
- Boeing tries to minimize excrescence in the A/P design

## Slide 6: What Is Excrescence Drag?
The additional drag on the airplane due to the sum of all deviations from a smooth sealed external surface
Proper maintenance can prevent an increase in excrescence drag
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7
Most Important in Critical Areas
Forward portion of fuselage and nacelle
Leading areas of wings and tail
Local Coefficient of Pressure (Cp) is highest
747 CRUISE DRAG SENSITIVITIES
All spoilers up 3.75” = 2% drag
Outboard aileron up 4” = 1% drag
Rudder deflection 4.5 degrees
(offset 9.5” at base) =2% drag
1” tall ridge on wing 75 ft. long = 2% drag

## Slide 8: Discrete Items
Antennas, masts, lights
Drag is a function of design, size, position
Notes: <number>
<footer>
<header>
<date/time>
19
19
16
- Have to put these on the airplane, and try to minimize drag in their design.
- Damage to these items can increase their drag; although damage usually results in requirement to replace them.

## Slide 9: Mismatched Surfaces
Steps at skin joints, around windows, doors, control surfaces, and access panels
Frame
Skin
Notes: <number>
<footer>
<header>
<date/time>
20
- Repairs can end up causing these mismatches.
- No step, but separated surfaces would be a gap.

## Slide 10: Internal Airflow
Leaks through gaps, holes, and seals
Airflow
Notes: <number>
<footer>
<header>
<date/time>
22
22
18
- Aerodynamic seals are those used to improve the aerodynamic characteristics of the airplane, other than prevent cabin pressurization leaks. They are mainly there to prevent air at high pressure from leaking to an area of low pressure, disturbing the airflow & creating drag.

## Slide 11: Roughness (Particularly Bad Near Static Sources)
  Non-flush fasteners, rough surface
  Waviness, gaps
  Deteriorated paint and decals
Non Flush Rivet
Rough Surface
Gaps
Waviness
Notes: <number>
<footer>
<header>
<date/time>
24
24
21
- Want to make repairs as smooth as possible
- A/Ps deliver in their best condition, improper maintenance will make drag increase

## Slide 12: Average Results of In-Service Drag Inspections
  Total Airframe Drag Deterioration ~ 0.65%
    Control Surface Rigging  0.25%
    Deteriorated Seals  0.20%
    Misfairs  0.1%
    Roughness  0.05%
    Other  0.05%
  A well maintained airplane should
  never exceed 0.5% drag increase
  from its new airplane level
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: Regular Maintenance Minimizes Deterioration
Rig flight controls
Misalignments and mismatches
Maintain seals
Maintain surface finish
OEW control
Instrument calibration
Notes: - And, systems maintenance.

## Slide 14
OEW Control
Operating empty weight grows on average 0.1 to 0.2% per year, leveling off at about 1% after 5 years
Mainly due to moisture and dirt
Notes: - Mainly due to dirt and moisture.
- Maybe .1 to .2% per year at first, but seems to level off after 5 to 10 years.
- Residual moisture in an aircraft depends on time spent on the ground for turnarounds, local climate, load factor, and duration of the flight (average passenger exhales ~ 100 grams of water every hour, or about 1 litre per person in a 10-hour flight).

## Slide 15
Instrument Calibration
Speed measuring equipment has a large impact on fuel mileage
If speed is not accurate the airplane may be flying faster or slower than intended
Flying 0.01M faster can increase fuel burn by 1%

## Slide 16
Airspeed System Error Penalty
Calibrate airspeed system
Airspeed reads 1% low, you fly 1% fast
About 2% drag penalty in a 747
Notes: - Includes pitot probes, pitot-static probes, pressure transducers, static ports, and alpha-vanes on airplanes with static ports.

## Slide 17
Conclusions It Takes the Whole Team to Win
  Large fuel (and emissions) savings can result from the accumulation of many smaller fuel-saving actions and policies
  Flight operations, flight crews, maintenance, and management all need to contribute
  Program should be tailored to your airline
  Boeing offers Fuel Conservation module as part of the “Performance Engineer Training – Operations Course”
Notes: <number>
<footer>
<header>
<date/time>
34
34
26
- There is no one big item that will save tremendous amounts of fuel. It is by combining many practices tha you start to obtain big savings.
- Any program needs to be tailored to each airline's policies on ETOPs, reserves, redispatch, etc.

## Slide 18
Conclusions It Takes the Whole Team to Win
  Questions?
Notes: <number>
<footer>
<header>
<date/time>
34
34
26
- There is no one big item that will save tremendous amounts of fuel. It is by combining many practices tha you start to obtain big savings.
- Any program needs to be tailored to each airline's policies on ETOPs, reserves, redispatch, etc.