## Slide 1
AVIATION OPERATIONAL MEASURES FOR FUEL AND EMISSIONS REDUCTION WORKSHOP
Fuel Conservation
Operational Procedures for Environmental Performance
Rob Root
Flight Operations Engineer
Boeing Commercial Airplanes

## Slide 2
Operational Procedures to Reduce Fuel Burn and Emissions
CO2 emissions are directly proportional to fuel burn
Practicing fuel conservation will also reduce CO2
Reduction in other emissions depends on the specific procedure

## Slide 3: What is Fuel Conservation?
Fuel conservation means managing the operation and condition of an airplane to minimize the fuel used (and emissions) on every flight
Notes: - never sacrifice safety to save fuel
- Is anybody assigned as a fuel conservation focal/mgr to establish policies at your airline?

## Slide 4
How Much is a 1% Reduction in Fuel Worth?
Airplane Fuel Savings
Type Gal/Year/Airplane
737 15,000
727 30,000
757 25,000
767 30,000
777 70,000
747 100,000
*
(* Assumes typical airplane utilization rates)
Notes: - Assumes 'typical' airplane utilization rates. Your operations may use more or less.

## Slide 5: Saving Fuel Requires Everyone’s Help
  Flight Operations
  Dispatchers
  Flight Crews
  Maintenance
  Management
Notes: - Also requires Airline Management. They have to buy into and support fuel conservation policies.
- These are general areas of responsibility; they do overlap in practice.
- First two manage the operation of the A/P
- Maintenance mainly manages the condition of the A/P

## Slide 6
Operational Practices for Fuel Conservation

## Slide 7: Flight Operations / Dispatchers
  Landing weight
  Fuel reserves
  Airplane loading
  Flap selection
  Altitude selection
  Speed selection
  Route selection
Opportunities for fuel conservation:

## Slide 8
737-3/4/500
737-6/7/800
757-200/-300
767-200/300
777-200/300
747-400
.7%
.6%
.5%
.3%
.2%
.2%
Effect of Reducing Landing Weight
%Block Fuel Savings per 1000 LB ZFW Reduction
Notes: - This is a fixed delta wt, not a % change.
- Values are different between models because1000 LB makes a larger effect on a 737 than it does on a 747.
- You can determine your own values by running flight planning data for a range of ZFW's and comparing the results.
- Tankering increases LDG wt

## Slide 9: Reducing OEW Reduces Landing Weight
Items to consider:
  Passenger service items
  Passenger entertainment items
  Cargo and baggage containers
  Emergency equipment
  Potable water
Notes: - Reduction in OEW or ZFW also reduces reserve fuel, which leads to a larger reduction in LDG wt. Therefore, %savings per 1000 LB OEW or ZFW is greater than 1000 LB LDG wt.
- OEW reductions lower the LDG wt, and avg wt, on every flight whereas lowering LDG fuel load is different on every flt.
-Pass Serv Items: Meal & beverage items & equipment
- Gear req'd for overwater operations weights 1000 to 2000 LB; not req'd if plane placed in domestic service (maybe seasonal change).
- Extra potable water is extra wt! (8.3 lb/gal; 3.8 kg/gal; 1.0 kg/liter).
- Ideas from airlines?
- Cargo and baggage containers: maybe consider pallet or bulk loading in place of containers if possible.

## Slide 10: Reducing Unnecessary Fuel Reduces Landing Weight
Flight plan by tail numbers
Practice cruise performance monitoring
Carry the appropriate amount of reserves to ensure a safe flight
(Extra reserves are extra weight)
Notes: - Each airplane has its own deterioration value. Don't use the worst A/P in the fleet to determine required fuel for all. Load the right amount of fuel.
- Wt LDG = OEW + P/L + Res + fuel loaded but not used.
- Limit discretionary fuel (easier if you plan the right amount)
- Monitor the performance of your A/Ps to ID deterioration for each tail number.
- APM program can help (discussion of this in another section of Ops course)
- (DRAG ITEM, NOT LDG WT REDUCTION!) Aft loaded A/P requires less downward force from tail, so wing produces less lift. Unnecessary lift causes unnecessary drag and fuel flow (cargo loading guidelines)

## Slide 11: Fuel Reserves
  Regulatory requirements
  Choice of alternate airport
  Use of redispatch
  Company policies on reserves
  Discretionary fuel
The amount of required fuel reserves depends on:
Notes: - What amount of reserves should you carry?
- See FCN Apr-Jun '82 for discussion of Reserve policies
- redispatch a.k.a. reclearance or refile
- company policies - including known increases for specific airports which have known delays, etc. Increased taxi, maneuver, holding times, higher contingency.
- reserves are wt; must burn fuel to carry wt; carrying more reserves than necessary burns extra fuel
- Discretionary; captain increases for a particular route if in his/her opinion extra fuel is necassary to safely complete the flight without diversion or en-route landing. Based on past experience with the route, dest airport, or particular A/P.
- Lowering ZFW lowers Reserves.

## Slide 12
Airplane Loading Maintain c.g. in the Mid to Aft Range
WT (fwd c.g.)
Lift tail (fwd c.g.)
Lift wing (fwd c.g.)
Lift wing (aft c.g.)
WT (aft c.g.)
Lift tail (aft c.g.)
<
=
Is less negative than
At aft c.g. the lift of the tail is less negative than at forward c.g.
due to the smaller moment arm between Liftwing and WT.
Less angle of attack, , is required to create the lower Liftwing
required to offset the WT plus the less negative Lifttail.
Same Lifttotal, but lower Liftwing and therefore lower a required.

## Slide 13
Airplane Loading
Examples of change in drag due to c.g. can be found in the various Performance Engineer’s Manuals
737-700
777-200
CG RANGE
CD TRIM
8% TO 12%
13% TO 18%
19% TO 25%
26% TO 33%
+2%
+1%
0
-1%
.78M Trim Drag
CG RANGE
CD TRIM
14% TO 19%
19% TO 26%
26% TO 37%
37% TO 44%
+2%
+1%
0
-1%
.84M Trim Drag

## Slide 14: Flap Setting
Choose lowest flap setting that will meet performance requirements:
  Less drag
  Better climb performance
  Spend less time at low altitudes, burn less fuel
Notes: - Choose lowest cleanup height (minimize exposure to flaps-down drag)
- see FCN Apr-Jun '82 for discussion of Flap retraction & extension schedules
- see FCN Jan-Feb '82 for discussion of Takeoff procedure effect on fuel burn.
- Flap retraction/extension schedules choosen for:
1) Schedule simplicity
2) maneuver margin of 30 deg. + 15 overshoot (i.e., 45 total) capability at all times
3) Close to optimum climb or acceleration capability
4) Stay within flap limit speeds
5) Compatible with flap retraction/extension times (EO usually longer times)

## Slide 15: Altitude Selection
Optimum altitude:
  Pressure altitude for a given weight and speed schedule that gives the maximum mileage per unit of fuel
Notes: - Boeing A/P's provide a wide range of usable alts & speeds within limits imposed by thrust limits, buffet margins, & max operating speeds. Proper choice of alt & speed can greatly impact fuel economy.
- Opt alt increases as weight decreases.
- how is this determined? (next slide)

## Slide 16: Step Climb
= Off optimum operations
Optimum Altitude
4000 FT
2000 FT
Step Climb
Notes: - Make the next step if fuel req'd to complete the mission with the step is less than without the step.
- RVSM allow A/Ps to fly closer to optimum & therefore conserve fuel
- Try to step where FM at the current & next altitude are equivalent. Earlier, & initially FM worse & manueuver and Fn margins lessoned. Late, & get immediate benefit, but burned more beforehand.
- Wt at which to step from 33 to 37 is virtually the same as the optimum wt for 35
- 1000 ft steps may be as good as climbing cruise
- If RVSM certified can use 2000 ft steps
- Not easy to say how much time must be spent at the higher alt, but in general @ least 30 min to 1 hr to see the benefit.

## Slide 17
Off-Optimum Fuel Burn Penalty
Optimum Altitude
+ 1.5%
+ 1.5%
4000 FT Step vs. No Step Over a 4-hour Cruise
1000 FT
+ 0.5%
+ 3.0%
+ 0%
+ 4.5%
+ 0.5%
+ 6.5%
+ 1.5%
+ 8.5%
4-hour Average
+ 0.6%
4-hour Average
+ 4.8%
Notes: - Comparison of flying constant altitude vs. 2000 ft. step.
- Fuel used in 4,000 ft step is approx. airplane wt/1000. Some of this is offset by the later descent such that over a 4K step cycle (4-5 hrs) net climb plus descent is approx. 0.25% of the total fuel burn.
- Penalty goes up dramatically as you move further from opt.
- Usually can assume approx. 1,000 ft/hr change in Opt alt.
- Fly at opt alt adjusted for winds actually.
- See FC&ON Apr-Jun '86 " Step Climb" and Jan-Mar '86 "Opt Cruise Alt."
- Early climb to above opt is preferred to remaining below opt for too long since above opt the penalty decreases with time while below opt the penalty is always becoming worse. (Be aware of stability effects & reduced maneuver margin if going much higher than 2,000 above opt).

## Slide 18: Speed Selection - LRC vs MRC
NAM/Pound Fuel
MACH Number
0.12
0.11
0.10
0.09
0.08
0.07
0.06
0.60
0.64
0.68
0.72
0.76
0.80
0.84
0.05
Increasing Weight
LRC
MRC
MMO
MRC = Maximum Range Cruise
LRC = Long Range Cruise
Notes: - If flying CI then speed would be for lowest cost not necessarily lowest fuel. For CI = 0 the speeds will be for minimum trip fuel (MRC).
- Dramatic FM penalty for going much faster than LRC.
- LRC buys you a good time decrease for a small fuel increase.
- see FC&ON Apr-Jun'85 "The effect of speed on cruise performance."
- LRC was an arbitrary choice providing the speed increase with a "theoretical" fuel mileage loss of 1%. Not really experienced in practice because of MRC speed/thrust instability.
- Flying within +- 4000 ft of opt, LRC can be approximated quite closely by a constant Mach.

## Slide 19
LRC
777-200
747-400
777-200
747-400
LRC (777)
LRC (747)
Flying Faster Than MRC?
 Fuel for Flying Faster than MRC
 Time for Flying Faster than MRC
5000 NM cruise
Notes: - 1st 1% FM decrease gains ~ 12 & 17 minutes. Next 10 minute gain costs much more: 4 and 5%.
- If pilots increase speed to make up time, there can be a large fuel burn increase.

## Slide 20
Speed Selection - Other Options
  Cost Index = 0 (maximize ngm/lb; = MRC)
  Selected Cost Index (minimize costs)
  Maximum Endurance (maximize time/lb)
CI =
Time Cost ~ $/hr
Fuel Cost ~ cents/lb
Notes: - Selected CI would be chosen to match your airline's cost structure. CI = cost of time/cost of fuel. We have a complete class on CI.
- Examples of using max endurance would be for holding (minimum fuel burn for a given amount of holding time; not going anywhere), or for a military operation circling on station.

## Slide 21: Route Selection
  Choose the most direct route possible
  ‘Great Circle’ is the shortest distance between 2 points on the earth’s surface
  Great circle may not be the shortest air distance when winds are included
Notes: - Great circle is the shortest ground distance. What is really desired is the shortest air distance. With no wind, great circle is the shortest air distance.

## Slide 22
Sample Taxi and APU Fuel Burns
Condition
727
737
747
757
767
777
Taxi (lb/min)
60
25
100
40
50
60
APU (lb/min)
5
4
11
4
4
9
Notes: - Limit taxiing and use of APU

## Slide 23: ETOPS
  ETOPS allows for more direct routes
  Shorter routes = less fuel required
New York
Montreal
St. Johns
Goose Bay
Iqaluit
Kangerlussuaq
Reykjavik
Shannon
Paris
120 min
60 min
3148
3461
Using 120 min ETOPS leads to a 9% savings in trip distance!
Notes: - If flying a twin-engined A/P you want to take advantage of ETOPS routings.
- Have a section of the course which covers ETOPs in great detail. At this point, just want to point out the more direct routing aspect of ETOPS.
- shorter distance = less time and less fuel

## Slide 24: Flight Crew
Opportunities for Fuel Conservation:
  Practice fuel economy in each phase of flight
  Understand the airplane’s systems - Systems Management
Notes: - now let's discuss practices which are more specific to the flight crew
- flight crews must buy into your fuel consv efforts because they can greatly impact the success of the program
- FMC provides speed & alt info for optimization. One of the most important tools to mimimize costs

## Slide 25: Engine Start
  Start engines as late as possible, coordinate with ATC departure schedule
  Take delays at the gate
  Minimize APU use if ground power available
Notes: - Fuel burned at the gate provides zero miles per pound of fuel (take delays at the gate or at some designated area with the engines shut down).
- use APU instead of engines, but use ground cart instead of APU.
- This applies as well to any airplane movement/engine use on the ground such as during maintenance, and when moving airplanes from maintenance facility to the gate (tow if possible).

## Slide 26: Taxi
  Take shortest route possible
  Use minimum thrust and minimum braking
Notes: - If safety consideration can be met, then it may save fuel to taxi with less than all engines operating
- see Jan 1991 article, and Airliner Jul-Sep '81
- Make assessment based on fuel conservation & safety considerations.
- Make intersection takeoffs if possible (and the crew has the adjustments for the shorter runway).
- Savings depends on if the remaining engine(s) has to be operated at higher than idle thrust (high wts, uphill, etc.) not just dividing taxi wf by two. Savings can only be estimated. Also, depends on taxi times.
- Some airlines use single-engine taxi as std procedure.

## Slide 27
Taxi - One Engine Shut Down Considerations
  After-start & before-takeoff checklists delayed
  Reduced fire protection from ground personnel
  High weights, soft asphalt, taxi-way slope
  Engine thermal stabilization - warm up & cool down
  Pneumatic and electrical system requirements
  Slow/tight turns in direction of operating engine(s)
  Cross-bleed start requirements
  Balance Fuel Conservation and Safety Considerations

## Slide 28: Takeoff
  Retract flaps as early as possible
  Using full rated thrust will save fuel relative to derated thrust (but will increase overall engine maintenance costs)
Notes: - Discuss this with the class
- Fuel is reduced for that one takeoff, but 1) maintenance costs increase 2) may speed up engine deterioration which affects all phases of flight
- this is hard to quantify
- Old presentation said it saved 25 to 250 lb of fuel to use full rate
- Retract flaps as early as possible: consistent with ATC and safety.
- Minimize maneuvering with flap & gear down.

## Slide 29
Climb
  Cost Index = 0 minimizes fuel to climb and cruise to a common point in space.
Distance
Altitude
Initial Cruise Altitude
Cost Index
Increasing
A
B
CI = 0 (Min fuel)
Min time
Max Gradient
Notes: - CI = 0 can be thought of as maximizing AVERAGE nautical ground miles per lb of fuel between A and B. As such, it includes the effects of both speed and fuel flow for a given takeoff weight.
- Max Rate of Climb speed ONLY looks at what fixed speed will give minimum time to climb between two altitudes.

## Slide 30: Cruise
  A plane flying in steady, level flight may require some control surface inputs to maintain lateral-directional control
  Use of the proper trim procedure minimizes drag
  Poor trim procedure can result in a 0.5% cruise drag penalty on a 747
Lateral - Directional trim procedure:
Notes: - Causes for trim requirements: Fuel imbalance; thrust imbalance; internal load distribution; imperfect rigging after maintenance
- 1 deg of sideslip increases fuel burn 3/4 to 1% depending on A/P, for trimmed sideslip controlled by rudder and wheel (see FCN Oct-Dec '81).
- Maintain planned speed (remember penalty mentioned earlier).

## Slide 31
Cruise
  A/C packs in high flow typically produce a 0.5 - 1 % increase in fuel burn
  Do not use unnecessary cargo heat
  Do not use unnecessary anti-ice
  Maintain a balanced fuel load
Systems management:
Notes: - With one or more re-circ fans switched off the A/C packs operate in a high-flow mode drawing more bleed from the engines. Estimated fuel increase for each pack at high flow: ~.3% (i.e., 2 packs ~.6%)
- 737-300/400/500 ~ .5%/pack
- Changes in electrical power loads are considered negligible on fuel consumption
- maintain balanced thrust on A/P's where you are setting thrust manually

## Slide 32
Cruise
  Wind may be a reason to choose an “off optimum” altitude
  Want to maximize ground miles per gallon of fuel
  Wind-Altitude trade tables are provided in Operations Manual
Winds:
Notes: - see Airliner Apr-Jun '82
- cruise speed ~500 ktas; if Wf 2% higher 4000 ft below, but tailwind 10 knots higher, then Vg up 2% and you break even. If tailwind >10 ktas then every 5 kt will gain 1% in FM
- Better nautical ground miles with headwind or tailwind?
- FM = VT/Wf = Vg/Wf; off-optimum alt will increase Wf, but increase in Vg may more than offset it so you get an overall FM benefit.

## Slide 33: Descent
  Penalty for early descent - spend more time at low altitudes, higher fuel burn
  Optimum top of descent point is affected by wind, ATC, speed restrictions, etc…
  Use information provided by FMC
  Use idle thrust (no part-power descents)
Notes: - High-speed descent minimizes descent fuel, but not trip fuel. For min fuel, the descent should be spread over the longest distance possible. As descent speed is reduced, distance will increase until a max value is achieved around min drag.
- No part-power descents.
- Avoid early descents since considerably more fuel is burned glying the distance at low altitude (can look at penalty for each one minute early in descent).

## Slide 34
Descent
Distance
Altitude
Final Cruise Altitude
Cost Index
Increasing
A
B
CI = 0 (Min fuel)
Min time
  Cost Index = 0 minimizes fuel between a common cruise point and a common end of descent point.
Notes: - As with climb, CI=0 maximizes nautical ground miles per pound. Generally, covering the most ground at min idle thrust will produce the lowest fuel burn between A and B.
- CI = 0 will increase the fuel burned DURING descent, but minimizes the fuel burned from a common point in cruise.
- Generally, want to maximize the time spent at idle thrust between points A and B.

## Slide 35: Approach
  Do not transition to the landing configuration too early
  Fuel flow in the landing configuration is approximately 150% of the fuel flow in the clean configuration
Notes: - Delay flap and gear extension as long as possible, consistent with establishing a stabilized approach, targeting to be in the LDG config & at the Ref LDG speed early in the final approach.
- As always, never sacrifice safety. Factors such as visibility, ceiling, daylight, precipitaion, windshear, & turbulence should all be considered, lest the A/P arrives at the decision pt unstabilized on speed an power.

## Slide 36: Summary of Operational Practices
  Minimize landing weight
  Do not carry more reserve fuel than required
  Use lowest flap setting required
  Target optimum altitude (wind-corrected)
  Target LRC (or cost index)
  Choose most direct routing
Flight Operations / Dispatchers:

## Slide 37
  Minimize engine/APU use on ground
  Fly the chosen Cost Index speeds
  Use proper trim procedures
  Understand the airplane’s systems
  Don’t descend too early
  Don’t transition to landing config too early
Summary of Operational Practices
Flight Crews:

## Slide 38
  Questions?
Summary of Operational Practices