AERONAUTICAL INFORMATION MANAGEMENT (AIM) IP-5 AIRAC ADHERENCE

Aeronautical information is constantly changing: airspace structures and routes are revised, navigation aids change, SIDs and STARs are amended, runway and taxiway information changes. It is essential, for both efficiency and safety, that Pilots, Air Traffic Controllers, Air Traffic Flow Managers, Flight Management Systems and Aviation Charts all have the same data set. This can only be achieved by following the AIRAC. What is AIRAC? AIRAC stands for Aeronautical Information Regulation And Control and steps from the Annex 15 - Aeronautical Information Services (AIS) document and defines a series of common dates and an associated standard aeronautical information publication procedure for States. In short it defines that in all instances, information provided under the AIRAC system shall be published in paper copy form and shall be distributed by the AIS unit at least 42 days in advance of the effective date with the objective of reaching recipients at least 28 days in advance of the effective date. Whenever major changes are planned and where additional notice is desirable and practicable, a publication date of at least 56 days in advance of the effective date should be used. Three dates are to be remembered from this: Effective Date Date at which changes take effect. Publication Date Date at which the AIS organization sends out the information. –> Should be at least 42 days (56 for major changes) before effective date. Reception Date Date at which the user should receive the publications. –> Should be at 28 days before the effective date. The two weeks between Publication date and Reception date is basically to allow for postal distribution of the (mostly) paper publications. The AIRAC cycle The AIRAC cycle was adopted in 1964 and further improved over the years. Key are the worldwide effective dates with 28 days intervals (e.g. 4 August 2005, 1 September 2005, 29 September 2005, ...). Effective days are always on a Thursday. It may look indeed like a long period, 28 days, or even 56, but it should be understood that aeronautical information changes (mostly published through so called AIRAC Amendments) require Changes to local systems which includes interpreting, re-typing and re-coding the information. Verification and Correction as publications are unfortunately seldom perfect. Validation against other data; Flight Plans are just one example. Re-distribution. Hereby think of Charts and Flight Management Systems to a fleet which can be anywhere in the world. The AIRAC effective dates The AIRAC effective dates are published in ICAO Doc 8126, the Aeronautical Information Services Manual, 'Table 2-1. Schedule of AIRAC effective dates'. They are also referred to in most national AIPs when providing the data delivery dates for data originators. 2009 2010 2011 2012 2013 15 January 14 January 13 January 12 January 10 January 12 February 11 February 10 February 9 February 7 February 12 March 11 March 10 March 8 March 7 March 9 April 8 April 7 April 5 April 4 April 7 May 6 May 5 May 3 May 2 May 4 June 3 June 2 June 31 May 30 May 2 July 1 July 30 June 28 June 27 June 30 July 29 July 28 July 26 July 25 July 27 August 26 August 25 August 23 August 22 August 24 September 23 September 22 September 20 September 19 September 22 October 21 October 20 October 18 October 17 October 19 November 18 November 17 November 15 November 14 November 17 December 16 December 15 December 13 December 12 December 'Freeze' dates Each recipient has an internal date, called 'freeze' date or Cut-off date, before the effective date after which he can not accept changes anymore. For example, Aircraft Flight Management Systems need the data often 20 days before the effective date to allow for the information re-coding, information uploading and distribution. Note that these freeze dates are strictly speaking the recipients own business, however they become important in the context of AIRAC Non-adherence as illustrated on the following timeline: Christmas and New Year ICAO Annex 15 - Chapter 6 is clear: "The use of the date in the AIRAC cycle which occurs between 21 December and 17 January inclusive should be avoided as an effective date for the introduction of significant changes under the AIRAC system". And in ICAO Doc 8126 – Chapter 4, because of reduced staffing and increased postal delays, "it is recommended that the AIRAC cycle date occurring in the 28-day period from 21 December to 17 January (both dates included) no longer be used as an AIRAC effective date for the introduction of significant operational changes. States experiencing similar problems during other holiday periods may wish to adopt a comparable system". For additional information, please contact: Mr. David Lewtas Chief, Aeronautical Information Unit Air Navigation (ANB) Bureau Telephone: +1 514-954-8163 Fax: +1 514-954-6077 E-mail: dlewtas@icao.int