## Slide 1
2019 World Radiocommunication Conference Agenda Item 9.1.4
Stations on-Board Sub-Orbital Vehicles
(Spaceplanes)
John Mettrop
UK CAA
ICAO Regional Preparatory Group meeting
Johannesburg, South Africa 4-5 September 2018

## Slide 2
  to conduct studies to identify any required technical and operational measures, in relation to stations on board sub-orbital vehicles, that could assist in avoiding harmful interference between radiocommunication services;
    to conduct studies to determine spectrum requirements and, based on the outcome of those studies, to consider a possible future agenda item for WRC‑23;
resolves to invite the ITU Radiocommunication Sector
Agenda Item 9.1.4 – Resolution 763

## Slide 3
  How will planes be operated including a description of the various phases of flight?
  During which phases of flight described in decides 1, will, if at all, need to be supported by air traffic control systems and what sort of systems are expected?
  What radio links will be required to support planes operations and under what radiocommunication service definition will they fall?
decides that the following Questions should be studied
ITU-R Question 259/5

## Slide 4
Space tourism
Satellite launch
Hypersonic travel
Scientific research
Technology testing
Remote sensing
Space Plane Applications

## Slide 5
Aircraft or Spacecraft?
Aircraft: Any machine that can derive support in the atmosphere from the reactions of the air other that the reactions of the air against the Earth’s surface (ICAO)
spacecraft: A man-made vehicle which is intended to go beyond the major portion of the Earth's atmosphere. (ITU)

## Slide 6
Issues with Respect to Aeronautical Spectrum
45,000 ft
120 km
522 NM
1,544 NM
6,500 km/hr
1,000 km/hr
Height
Radio Horizon
  Link Budget
  Time in Sector
Speed
  Doppler Shift
Incompatible with current planning rules
Aeronautical system Capabilities e.g. ADS-B max
  Velocity 4096 knots
  Height 131,072 ft

## Slide 7
Radiocommunication
Mobile Service
Radiodetermination
Amateur
Broadcasting
Fixed
Meteorological aids
Standard frequency & time signal
Mobile-satellite
Radiodetermination-satellite
Amateur
Broadcasting-Satellite
Fixed-Satellite
Earth exploration-satellite
Standard frequency & time signal-satellite
Inter-satellite
Safety
Special
Space research
Radio astronomy
Space operation
Aeronautical mobile
Aeronautical mobile (R)
Aeronautical mobile (OR)
Land mobile
Maritime mobile
Port operations
Ship movement
Radiolocation
Radionavigation
Aeronautical radionavigation
Maritime radionavigation
Meteorological-satellite
Aeronautical mobile-satellite (R)
Aeronautical mobile-satellite
Land mobile-satellite
Maritime mobile-satellite
Radiolocation-satellite
Aeronautical radionavigation-satellite
Maritime radionavigation-satellite
Radionavigation-satellite
Aeronautical mobile-satellite (OR)
Which Radio Service?
Aeronautical mobile
Aeronautical mobile-satellite
Mobile Service
Radiodetermination
Aeronautical mobile (OR)
Aeronautical mobile-satellite (OR)
Mobile-satellite
Radiodetermination-satellite
Aeronautical mobile (R)
Aeronautical mobile-satellite (R)
Aeronautical radionavigation-satellite
Radionavigation-satellite
Safety
Radionavigation
Aeronautical radionavigation
Special
Space operation
Safety
Mobile-satellite

## Slide 8: Current Proposals within the ITU
  Identifies the phases of flight for single & multistage suborbital vehicles
  Types of applications
  Spectrum requirement
    Communication
    Navigation
    Surveillance
    Telemetry
    Telecommand
  Identifies radio spectrum issues
WDPDN Report ITU-R M.[Suborbital Vehicles] (https://www.itu.int/dms_ties/itu-r/md/15/wp5b/c/R15-WP5B-C-0538!N24!MSW-E.docx)
  No Change to the Radio Regulations is proposed for WRC-19. Further operational, technical and regulatory issues may need to be addressed, which require continuing studies, in particular of the status of the station aboard suborbital vehicles and type of applications, through the appropriate mechanism. No action has been taken with respect to retention, revision or suppression of Resolution 763 (WRC-15).
Draft CPM text on WRC-19 AI 9.1, issue 4 (https://www.itu.int/dms_ties/itu-r/md/15/wp5b/c/R15-WP5B-C-0538!N08!MSW-E.docx)

## Slide 9: ICAO Position
To support the studies called for by Resolution 763 (WRC-15) noting that those studies need to be completed during this study cycle.
If the results of studies indicate that additional spectrum and/or other regulatory measures are required, seek an agenda item for WRC-23.

## Slide 10
Summary
How Much Spectrum is Required?
Which Service?
Sufficient Spectrum Available?
Impact on Existing Aeronautical Services
  Standards
  Planning rules
  Sector Size
Support the need for a WRC-23 Agenda Item
Support ICAO/ITU Studies

## Slide 11
Questions