## Slide 1: Inter-American Telecommunication Commission (CITEL) Permanent Consultative Committee II Mike Biggs, FAA
Status of Preparations for WRC-19

## Slide 2: Working Group - PCC.II “Working Group for the Preparation of CITEL for Regional and World Radiocommunication Conferences”
Chair: Carmelo Rivera, United States
(carmelo.rivera@noaa.gov)
Vice-Chairs: Victor Martinez, Mexico
(victor.martinezv@ift.org.mx)
Martha Suarez, Colombia
(martha.suarez@ane.gov.co)

## Slide 3: WRC Working Group Structure
Sub WG | Title | Agenda items | Coordinator
SGT1 | Mobile & Fixed | 1.11, 1.12, 1.13, 1.14, 1.15, 1.16, 9.1 (Issues 9.1.1, 9.1.2, 9.1.5, 9.1.6, 9.1.8) | Luciana CAMARGOS (Brazil) lcamargos@gsma.com Jose COSTA (Canada) Jose.costa@ericsson.com
SGT2A | Radiolocation, Amateur, Maritime & Aeronautical | 1.1, 1.8, 1.9, 1.10, 9.1 (Issue 9.1.4) | Mike RAZI (Canada) mrazi@storm.ca
SGT2B | Space Science | 1.2, 1.3, 1.7 | Glenn Feldhake (USA) glenn.s.feldhake@nasa.gov
SGT3 | Satellite Regulatory | 1.4, 1.5, 1.6, 9.1 (Issue 9.1.9) 7, 9.1 (Issues 9.1.3, 9.1.7), 9.2 (satellite), 9.3 | Brandon MITCHELL (USA) bmitchell@ntia.doc.gov Chantal BEAUMIER Chantal.beaumier@canada.ca
SGT4 | General Regulatory, Future Work & Other | 2, 4, 8, 9.2 (non-satellite), 10 | Victor MARTINEZ (Mexico) victor.martinezv@ift.org.mx Martha SUAREZ Martha.suarez@ane.gov.co

## Slide 4: Inter – American Proposals : Definitions
PRELIMINARY VIEWS (PV): a Member State’s initial view of an Agenda Item, indicating its view of a future proposal or position.
DRAFT INTER-AMERICAN PROPOSAL (DIAP): a Preliminary Proposal that has been supported by at least one other Member State, but not the number of Member States required for an Inter-American Proposal.
PRELIMINARY PROPOSAL (PP): Member State proposal that has yet to be supported by another Member State.
INTER-AMERICAN PROPOSAL (IAP): a Member State(s) proposal supported by at least six Members States and not opposed by more than 50% of the number of supports obtained (i.e., 8 support, 4 oppose = IAP; 8 support, 5 or more oppose = “not IAP”.

## Slide 5: WRC-19 – Issues of Primary Interest to Aviation
Agenda Item 1.10 – Global Aeronautical Distress and Safety System (GADSS) – Draft Inter-American Proposal*
Agenda Item Issue 9.1.4 – Stations on Board Sub-Orbital Vehicles – Preliminary View and Proposal Proposal (Mexico)*
Agenda Item 1.8 – Introduction of Additional Satellite Systems into the Global Maritime Distress and Safety System (GMDSS) – Inter-American Proposal*
* Status Upgraded

## Slide 6: Agenda Item 1.10: GADSS
Draft Inter-American Proposal (elevated from Preliminary View status)
Canada, Mexico, United States of America
Proposal includes several modifications to Chapter VII Distress and Safety Communications of the Radio Regulations to:
  identify articles and numbers associated with GADSS;
  introduce GADSS into the Radio Regulations;
  link the functional requirements of GADSS to the Convention of International Civil Aviation; and,
  introduce a new Article 34A is proposed that describes GADSS and precludes systems contributing to GADSS from operating under Article 4.4.
  * This is similar to the existing link in Article 30 between GMDSS and the International Convention for the Safety of Life at Sea (SOLAS) under the responsibility of the International Maritime Organization.
Issue Coordinator: Luís Fernando (B) lfsouza@embraer.com.br
Alt Coordinator: Sandra Wright (USA) sandra.a.wright@faa.gov

## Slide 7: Agenda Item 1.10: GADSS – Proposals
Draft Inter-American Proposals
CAN/MEX/USA
Article 5 – Section IV – Table of Frequency Allocations
NOC DIAP/1.10/1
Reason: There is no requirement for additional spectrum allocations for GADSS.
Issue Coordinator: Luís Fernando (B) lfsouza@embraer.com.br
Alt Coordinator: Sandra Wright (USA) sandra.a.wright@faa.gov

## Slide 8: Agenda Item 1.10: GADSS – Proposals
Draft Inter-American Proposals
CAN/MEX/USA
Article 30 – Chapter VI – Distress and Safety Communication
MOD DIAP/1.10/2
30.1 § 1 Nos 30.4 - 30.13, and Articles 31, 32, 33 and 34 of this Chapter contain the provisions for the operational use of the global maritime distress and safety system (GMDSS), whose functional requirements, system elements and equipment carriage requirements are set forth in the International Convention for the Safety of Life at Sea (SOLAS), 1974, as amended. These Nos and Articles also contain provisions for initiating distress, urgency and safety communications by means of radiotelephony on the frequency 156.8 MHz (VHF channel 16). (WRC‑19)
Reason: Identifies the specific articles and numbers associated with GMDSS, to allow for an additional article and numbers to address GADSS as part of Chapter VII.

## Slide 9: Agenda Item 1.10: GADSS – Proposals
Draft Inter-American Proposals
CAN/MEX/USA
Article 30 – Chapter VI – Distress and Safety Communication
ADD DIAP/1.10/3
30.1A Article 34A of this Chapter contains the provisions for the global aeronautical distress and safety system (GADSS), whose functional requirements are set forth in the Annexes to the Convention on International Civil Aviation, as amended. (WRC‑19)
Reason: Includes GADSS as part of Chapter VII Distress and safety communications.

## Slide 10: Agenda Item 1.10: GADSS – Proposals
Draft Inter-American Proposals
CAN/MEX/USA
ADD DIAP/1.10/4
Article 34A – Global aeronautical distress and safety system
Reason: Initiates a new article to establish a regulatory framework for GADSS.

## Slide 11: Agenda Item 1.10: GADSS – Proposals
Draft Inter-American Proposals
CAN/MEX/USA
Article 34A – Global aeronautical distress and safety system
ADD DIAP/1.10/5
34A.1 The global aeronautical distress and safety system (GADSS) determines performance requirements for the radiocommunication systems utilized for conducting functions such as aircraft tracking, autonomous distress tracking, and post flight localization and recovery. (WRC-19)
Reason: Initiates a new article to establish a regulatory framework for GADSS.

## Slide 12: Agenda Item 1.10: GADSS – Proposals
Draft Inter-American Proposals
CAN/MEX/USA
Article 34A – Global aeronautical distress and safety system
ADD DIAP/1.10/6
34A.2 The type of radiocommunication service(s) to be used by systems contributing to the GADSS depend(s) on the requirements of the specific GADSS function. Systems contributing to the GADSS shall not be operated under the provisions of No. 4.4. (WRC-19)
Reason: Radiocommunication services to be used by systems contributing to GADSS should be operated in accordance with the Table of Frequency Allocations.

## Slide 13: Agenda Item 1.10: GADSS – Proposals
Draft Inter-American Proposals
CAN/MEX/USA
Article 34A – Global aeronautical distress and safety system
SUP DIAP/1.10/7
RESOLUTION 426 (WRC-15)
Studies on spectrum needs and regulatory provisions for the introduction and use of the Global Aeronautical Distress and Safety System
Reason: Resolution 426 is no longer necessary.

## Slide 14: Agenda Item 1.10: GADSS – CITEL Draft-Inter-American Proposal

## Slide 15: Issue 9.1.4: Stations on board sub-orbital vehicles
Preliminary Proposal (elevated from Preliminary View status)
Mexico
NOC PP/9.1/9.1.4/1
Radio Regulations, Volumes 1, and 2
Reason: It is deemed unnecessary to introduce any changes in the Radio Regulations or to take any regulatory measure under this Agenda Item
SUP PP/9.1/9.1.4/2
RESOLUTION 763 (WRC-15) – Stations on board sub-orbital vehicles
Reason: Resolution 763 is no longer necessary.
Issue Coordinator: Sandra Wright (USA) sandra.a.wright@faa.gov

## Slide 16: Agenda Item 9.1.4: Sub-Orbital Vehicles – Preliminary Proposal

## Slide 17: Agenda Item 1.8: GMDSS (additional satellite systems – issue “B”)
Inter-American Proposal (elevated from Preliminary View status)
Bahamas, Canada, Chile, Ecuador, Panama, United States of America
Noting the 99th Meeting of the Maritime Safety Committee (MSC 99) adopted Resolution MSC.451(99), “Statement Of Recognition Of Maritime Mobile Satellite Services Provided By Iridium Satellite LLC”, the above countries support a new CITEL IAP to modify Article 5, Article 33, and Appendix 15 to reflect in the Radio Regulations IMO’S recognition of a new provider capable of operating in the band 1616-1626.5 MHz.
Issue Coordinator: Michael Razi (CAN) mrazi@parscom
Alt Coordinator: Christopher Casarrubias (MEX) chirstopher.casarrubias@accesspartnership.com

## Slide 18: Agenda Item 1.8: GMDSS additional satellite systems (1 of 9)
Inter-American Proposal
Bahamas, Canada, Chile, Ecuador, Panama, United States of America
MOD IAP/1.8B/1
Article 5 – Section IV – Table of Frequency Allocations
1610-1613.8 MHz Regions 1, 2 and 3 MOD 5.368
1613.8-1626.5 MHz Regions 1, 2 and 3 MOD 5.364 and 5.368
Reason: To reference in the Table of Frequency Allocations to add new footnote 5.GMDSS to recognize the availability of frequencies within the band 1613.8-1626.5 MHz for GMDS and to reflect proposed modifications to 5.364 and 5.368 to support the introduction of an additional satellite system into the GMDSS in accordance with Resolution 359 (Rev.WRC-15).

## Slide 19: Agenda Item 1.8: GMDSS additional satellite systems (2 of 9)
Inter-American Proposal
Bahamas, Canada, Chile, Ecuador, Panama, United States of America
MOD IAP/1.8B/2
Article 5 – Section IV – Table of Frequency Allocations
1610-1626.5 MHz Regions 1, 2 and 3 MOD 5.368
5.GMDSS The band 1616-1626.5 MHz may also be used for the provision of distress, urgency, and safety communications of the Global Maritime Distress and Safety System (GMDSS). (See Table 15-2 of Appendix 15, No. 33.50 and No. 33.53 of Article 33).
Reason: To identify the band 1616-1626.5 MHz as being available for the provision of GMDSS by mobile-satellite service systems. Also to align with the Method B1 in the Draft CPM Text.

## Slide 20: Agenda Item 1.8: GMDSS additional satellite systems (3 of 9)
Inter-American Proposal
Bahamas, Canada, Chile, Ecuador, Panama, United States of America
MOD IAP/1.8B/3
5.364 The use of the band 1 610-1 626.5 MHz by the mobile-satellite service (Earth-to-space) and by the radiodetermination-satellite service (Earth‑to‑space) is subject to coordination under No. 9.11A. A mobile earth station operating in either of the services in this band shall not produce a peak e.i.r.p. density in excess of ‑15 dB(W/4 kHz) in the part of the band used by systems operating in accordance with the provisions of No. 5.366 (to which No. 4.10 applies), unless otherwise agreed by the affected administrations. In the part of the band where such systems are not operating, the mean e.i.r.p. density of a mobile earth station shall not exceed –3 dB(W/4 kHz). Except when used for distress and safety purposes in the band 1 616-1 626.5 MHz by satellite networks in the mobile-satellite service using the same channel in the Earth‑to‑space and space-to-Earth directions, sStations of the mobile-satellite service shall not claim protection from stations in the aeronautical radionavigation service, stations operating in accordance with the provisions of No. 5.366 and stations in the fixed service operating in accordance with the provisions of No. 5.359. Administrations responsible for the coordination of mobile-satellite networks shall make all practicable efforts to ensure protection of stations operating in accordance with the provisions of No. 5.366. (WRC-19)
Reasons: To provide adequate protection for GMDSS operations in this band.

## Slide 21: Agenda Item 1.8: GMDSS additional satellite systems (4 of 9)
Inter-American Proposal
Bahamas, Canada, Chile, Ecuador, Panama, United States of America
MOD IAP/1.8B/4
5.368 With respect to the radiodetermination-satellite service and the mobile-satellite services the provisions of No. 4.10 do not apply in the band 1 610-1 616* MHz, with the exception of the aeronautical radionavigation-satellite service.
Reason: To recognize that in the necessary parts of the frequency band 1 610-1 626.5 MHz the mobile-satellite service is used for the provision of aeronautical and maritime safety services. Consequently, No. 4.10 would apply to these safety services within the appropriate frequency bands.
*the modification is to change the upper band limit from 1626.5 MHz to 1616 MHz.

## Slide 22: Agenda Item 1.8: GMDSS additional satellite systems (5 of 9)
Inter-American Proposal
Bahamas, Canada, Chile, Ecuador, Panama, United States of America
MOD IAP/1.8B/5
33.50 § 26 Maritime safety information may be transmitted via satellite in the maritime mobile-satellite service using the bands 1 530-1 545 MHz and 1 616-1 626.5 MHz. (see Appendix 15). (WRC‑19)
Reasons: To include the necessary parts of the frequency band 1 610-1 626.5 MHz as being available for transmitting maritime safety information via satellite.

## Slide 23: Agenda Item 1.8: GMDSS additional satellite systems (6 of 9)
Inter-American Proposal
Bahamas, Canada, Chile, Ecuador, Panama, United States of America
MOD IAP/1.8B/6
33.53 § 28 Radiocommunications for safety purposes concerning ship reporting communications, communications relating to the navigation, movements and needs of ships and weather observation messages may be conducted on any appropriate communications frequency, including those used for public correspondence. In terrestrial systems, the bands 415-535 kHz (see Article 52), 1 606.5-4 000 kHz (see Article 52), 4 000-27 500 kHz (see Appendix 17), and 156‑174 MHz (see Appendix 18) are used for this function. In the maritime mobile-satellite service, frequencies in the bands 1 530-1 544 MHz, 1616-1626.5 MHz, and 1 626.5-1 645.5 MHz are used for this function as well as for distress alerting purposes (see No. 32.2). (WRC‑0719)
Reason: To apply No. 33.53 to the necessary parts of the frequency band 1 610-1 626.5 MHz for use by mobile-satellite service systems approved by the International Maritime Organization to participate in the Global Maritime Distress and Safety System.

## Slide 24: Agenda Item 1.8: GMDSS additional satellite systems (7 of 9)
Inter-American Proposal
Bahamas, Canada, Chile, Ecuador, Panama, United States of America
MOD IAP/1.8B/7
APPENDIX 15 (REV. WRC-19)
1616-1626.5 | SAT-COM | In addition to its availability for routine non-safety purposes, the band 1 616‑1 626.5 MHz is used for distress and safety purposes in the Earth-to-space and space-to-Earth directions in the maritime mobile-satellite service. GMDSS distress, urgency and safety communications have priority over non-safety communications within a satellite system (see No. 5.GMDSS).

## Slide 25: Agenda Item 1.8: GMDSS additional satellite systems (8 of 9)
Inter-American Proposal
Bahamas, Canada, Chile, Ecuador, Panama, United States of America
MOD IAP/1.8B/7 (cont.)
APPENDIX 15 (REV. WRC-1519)
TABLE 15-2 (WRC-1519)
1616-1626.5 | SAT-COM | In addition to its availability for routine non-safety purposes, the band 1 616‑1 626.5 MHz is used for distress and safety purposes in the Earth-to-space and space-to-Earth directions in the maritime mobile-satellite service solely by satellite networks using the same channel in both directions. GMDSS distress, urgency and safety communications have priority over non-safety communications within a satellite system.
Reason: To add the necessary parts of the frequency band 1 610-1 626.5 MHz to Appendix 15 as being available for distress and safety communications for the Global Maritime Distress and Safety System (GMDSS).

## Slide 26: Agenda Item 1.8: GMDSS additional satellite systems (9 of 9)
Inter-American Proposal
Bahamas, Canada, Chile, Ecuador, Panama, United States of America
SUP IAP/1.8B/8
33.50 § 26 Maritime safety information may be transmitted via satellite in the maritime mobile-satellite service using the bands 1 530-1 545 MHz and 1 616-1 626.5 MHz. (see Appendix 15). (WRC‑19)
Reasons: To include the necessary parts of the frequency band 1 610-1 626.5 MHz as being available for transmitting maritime safety information via satellite.

## Slide 27: Agenda Item 1.8: GMDSS Issue B – CITEL Inter-American Proposal

## Slide 28
Other Agenda Items
Inter-American Proposals: 1.1, 1.11, 1.12, 9.1.2, 9.1.3, 9.1.8
Draft Inter-American Proposals: 1.9.1, 1.9.2, 1.13 (Band A), 1.14, 1.16, 7 Issues B, C1, C5, D, and G,
Preliminary Proposals: 1.2, 1.3, 1.4, 1.9.1, 1.13 (Bands C, D, E), 1.14, 1.15, 1.16, 7 Issues E, I, and K, 9.1.1, 9.1.4, 9.1.5, 9.1.6, 9.1.7, 10
Preliminary Views: 1.5, 1.6, 1.7, 9.1.1

## Slide 29
INTER-AMERICAN PROPOSALS
(IAP)
INTER-AMERICAN PROPOSAL (IAP): DIAP for which the PCC II has ended its consideration and discussion, has been supported by at least six Members States and is not opposed by more than 50% of the number of supports obtained.

## Slide 30: Agenda Item 1.1: Consideration of the band 50-54 MHz to the amateur service in Region 1 (1 of 2)
Inter-American Proposal
Argentina, Brazil, Bahamas, Canada, Colombia, [Paraguay],[United States of America, Uruguay
NOC IAP/1.1/1
Reasons: WRC-19 agenda item 1.1 is a Region 1 issue. Any changes made to the Radio Regulations under WRC-19 agenda item 1.1 must not impact the existing allocation to the Amateur Service in 50-54 MHz in Region 2, nor subject Region 2 to any changed procedural or regulatory provisions.
Coordinator: Flávio A. B. Archangelo (B) flavio.archangelo@ties.itu.int
Alt. Coordinator: Jonathan Siverling (USA) jsiverling@arrl.org
Issue Coordinator: Flávio ARCHANGELO (B) Flavio.archangelo@labre.org.br

## Slide 31: Agenda Item 1.1: Consideration of the band 50-54 MHz to the amateur service in Region 1 (2 of 2)
Inter-American Proposal
Argentina, Brazil, Bahamas, Canada, Colombia, [Paraguay],[United States of America, Uruguay
IAP/1.1/2
Reasons: Given that WRC-19 agenda item 1.1 is a Region 1 issue. No change is proposed for Region 1. Furthermore, any changes made to the Radio Regulations under WRC-19 agenda item 1.1 must not impact the existing allocation to the Amateur Service in 50-54 MHz in Region 2, nor subject Region 2 to any changed procedural or regulatory provisions.
Coordinator: Flávio A. B. Archangelo (B) flavio.archangelo@ties.itu.int
Alt. Coordinator: Jonathan Siverling (USA) jsiverling@arrl.org
Issue Coordinator: Flávio ARCHANGELO (B) Flavio.archangelo@labre.org.br

## Slide 32
IAP
Argentina, Brazil, Canada, Colombia, United States of America, Ecuador, Guatemala, Mexico, Panama, Uruguay
NOC IAP/1.11/1
Radio Regulations Volumes 1 & 2
Reason: The Administrations believe it is unnecessary to identify spectrum specifically for railway radiocommunication systems. Regional and global harmonization can be satisfied by developing applicable ITU-R Reports and Recommendations. Therefore, no change to the Radio Regulations or regulatory action is required under this agenda item.
SUP IAP/1.11/2
RESOLUTION 236 (WRC-15)
Railway radiocommunication systems between train and trackside
Reasons: The studies towards regional and global harmonization can be satisfied through ITU-R Recommendations and Reports.
Issue Coordinator: David TEJEDA (Mexico) david.tejeda@ift.org.mx
Agenda Item 1.11: Railway Train and Trackside

## Slide 33: Agenda Item 1.12: ITS Harmonization
Inter-American Proposal
Brazil, Canada, Colombia, Ecuador, Guatemala, Mexico, Panama, United States
NOC DIAP/1.12/1
Radio Regulations Volumes 1 & 2
Reason: It is unnecessary to identify spectrum specifically for Intelligent Transport Systems. Regional and global harmonization can be satisfied by developing applicable ITU-R Reports and Recommendations. Therefore, no change to the Radio Regulations or regulatory action is required under this agenda item.
SUP DIAP/1.12/2
RESOLUTION 237 (WRC-15)
Intelligent Transport Systems applications
Issue Coordinator: TBD Argentina
Alt Issue Coordinator: Francisco Soares (B) fsoares@qti.qualcomm.com

## Slide 34: Issue 9.1.2: Compatibility of IMT and broadcasting-satellite service (sound) in the frequency band 1 452-1 492 MHz in Regions 1 and 3
IAP
Argentina, Brazil, Canada, Colombia, Ecuador, Mexico, United States of America, Guatemala, Uruguay
NOC IAP/9.1.2/1
Article 5 – Section IV – Table of Frequency Allocations
Reasons: WRC-19 issue 9.1.2 is limited to technical and regulatory studies of the mobile (IMT) and broadcasting satellite (sound) services in the band 1452-1492 MHz in Regions 1 and 3 only. Therefore, there is no basis for any changes to the Radio Regulations that would impact the services in the frequency band1452-1492 MHz in Region 2 under this issue. Therefore, NOC is proposed with respect to any change to Article 5 that could impact Region 2 services in the frequency band 1452-1492 MHz.
Issue Coordinator: Luciana Camargos (B) lcamargos@gsma.com

## Slide 35: Issue 9.1.3: Technical and operational issues and regulatory provisions for new NGSO systems in the 3 700-4 200 MHz, 4 500-4 800 MHz, 5 925-6 425 MHz and 6 725-7 025 MHz bands allocated to FSS
IAP
Brazil, Canada, Guatemala, Nicaragua, United States, Uruguay
NOC IAP/9.1/9.1.3/1 – ARTICLE 21
NOC IAP/9.1/9.1.3/2 – ARTICLE 22
SUP IAP/9.1/9.1.3/3 – RESOLUTION 157 (WRC-15)
ITU-R studies show that it would be very difficult to operate a non-GSO circular-orbit system for the purposes of a global broadband network in the 6/4 GHz frequency bands. Therefore, CITEL administrations support no revision to Article 21, Table 21-4 for non-GSO FSS satellites in the frequency band 3700-4200 MHz (space-to-Earth) and no modifications to Article 22 epfd limits applicable to non-GSO systems in the bands 3700-4200 MHz (space-to-Earth) and 5925-6425 MHz (Earth-to-Space). Similarly, CITEL administrations propose no change to the bands 4500-4800 MHz (space-to-Earth) and 6725-7025 MHz (Earth-to-space).
Issue Coordinator: [Hugo Mario Trivino (CLM) trivino@mintic.gov.co ]
[Manoel Almeida (B) manoel.almeida@intelsat.com ]
Alt. Issue Coordinator: Marcella Ost (Canada) marcella.s.ost@boeing.com

## Slide 36: Issue 9.1.8: Narrowband and broadband machine-type communication infrastructures (1 of 2)
IAP
Argentina, Brazil, Canada, Colombia, Dominican Republic, Ecuador, United States, Guatemala, Mexico, Panama, Uruguay
NOC IAP/9.1 Issue 9.1.8/1
Radio Regulations Volumes 1 & 2
Reason: Analysis of the current and future spectrum use for narrowband and broadband machine type communications (MTC), also known as machine-to-machine (M2M) or Internet of Things (IoT), concluded that there is no need to identify specific spectrum for those applications. Therefore, no change to the Radio Regulations or regulatory action is required.
Issue Coordinator: Sergio Marquez (Mexico) sergio.marquez@ift.org.mx
Alt. Issue Coordinator: Jayne Stancavage (USA) jayne.stancavage@intel.com

## Slide 37: Issue 9.1.8: Narrowband and broadband machine-type communication infrastructures (2 of 2)
IAP
Argentina, Brazil, Canada, Colombia, Dominican Republic, Ecuador, United States, Guatemala, Mexico, Panama, Uruguay
SUP IAP/9.1 Issue 9.1.8/2
ANNEX TO RESOLUTION 958 (WRC-15)
Urgent studies required in preparation for the 2019 World Radiocommunication Conference
3) Studies on the technical and operational aspects of radio networks and systems, as well as spectrum needed, including possible harmonized use of spectrum to support the implementation of narrowband and broadband machine-type communication infrastructures, in order to develop Recommendations, Reports and/or Handbooks, as appropriate, and to take appropriate actions within the ITU Radiocommunication Sector (ITU-R) scope of work.
Reason: Analysis of the current and future spectrum use for narrowband and broadband machine type communications (MTC), also known as machine-to-machine (M2M) or Internet of Things (IoT), concluded that there is no need to identify specific spectrum for those applications. Therefore, no change to the Radio Regulations or regulatory action is required. No changes also apply to RR Volume 3, apart from the suppression proposed to parts of Resolution 958 (WRC-15).
Issue Coordinator: Sergio Marquez (Mexico) sergio.marquez@ift.org.mx
Alt. Issue Coordinator: Jayne Stancavage (USA) jayne.stancavage@intel.com

## Slide 38
DRAFT INTER-AMERICAN PROPOSALS
(DIAP)
DRAFT INTER-AMERICAN PROPOSAL (DIAP): PP that has been supported by at least one other Member State.

## Slide 39: Agenda Item 1.9.1: Regulatory actions within the frequency band 156-162.05 MHz for autonomous maritime radio devices to protect the GMDSS and automatic identifications system (AIS), in accordance with Resolution 362 (WRC-15)
DIAP
Bahamas, Canada
Issue Coordinator: Robert Denny – rdenny@ntia.doc.gov

## Slide 40: Agenda Item 1.9.2: Modifications of the Radio Regulations, preferably within the frequency bands 156.0125-157.4375 MHz and 160.6125-162.0375 MHz, to enable a new VHF data exchange system (VDES) satellite component
DIAP
Bahamas, Mexico
Issue Coordinator: Robert Denny – rdenny@ntia.doc.gov

## Slide 41: Agenda Item 1.14: High Altitude Platform Systems
DIAP
Bahamas, Brazil, Ecuador
Issue Coordinator: Ana Valadares (B) avaladares@fb.com
Alt Coordinator: Vassilios Mimis (Canada) vmimis@primus.ca

## Slide 42: Agenda Item 1.16: WAS/RLANs in 5 GHz
DIAP
Canada, Mexico
Issue Coordinator: [Jose Francisco Lozano] [CLM] [jose.lozano@ane.gov.co]
Alt Coordinator: Jayne Stancavage (USA) jayne.stancavage@intel.com

## Slide 43: Agenda Item 7: Changes in response to Resolution 86 – Satellite network regulatory procedures –Issue B
DIAP
Brazil, Canada
Coordinator: bmitchell@ntia.doc.gov

## Slide 44: Agenda Item 7: Changes in response to Resolution 86 – Satellite network regulatory procedures –Issue C1
DIAP
Brazil, Canada, Mexico
Coordinator: bmitchell@ntia.doc.gov

## Slide 45: Agenda Item 7: Changes in response to Resolution 86 – Satellite network regulatory procedures –Issue C2
DIAP
Brazil, Mexico
Coordinator: bmitchell@ntia.doc.gov

## Slide 46: Agenda Item 7: Changes in response to Resolution 86 – Satellite network regulatory procedures –Issue C3
DIAP
Brazil, Mexico
Coordinator: bmitchell@ntia.doc.gov

## Slide 47: Agenda Item 7: Changes in response to Resolution 86 – Satellite network regulatory procedures – Issue C5
DIAP
Brazil, Canada, Mexico
Coordinator: bmitchell@ntia.doc.gov

## Slide 48: Agenda Item 7: Changes in response to Resolution 86 – Satellite network regulatory procedures – Issue D
DIAP
Brazil, Canada, Mexico
Coordinator: bmitchell@ntia.doc.gov

## Slide 49: Agenda Item 7: Changes in response to Resolution 86 – Satellite network regulatory procedures – Issue G
DIAP
Brazil, United States of America
Coordinator: bmitchell@ntia.doc.gov

## Slide 50
PRELIMINARY PROPOSALS
(PP)
PRELIMINARY PROPOSAL (PP): Member State proposal that has yet to be supported by another Member State.

## Slide 51: Agenda Item 1.2: ​To consider in-band power limits for earth stations operating in the mobile-satellite service, meteorological-satellite service and Earth exploration-satellite service in the frequency bands 401-403 MHz and 399.9-400.05 MHz
Preliminary Proposal
Mexico
Issue Coordinator: [Glenn Feldhake]

## Slide 52: Agenda Item 1.3: Possible upgrading met satellite service (space-to-Earth) to primary status and a possible primary allocation to the EESS (space-to-Earth) in the band 460-470 MHz
Preliminary Proposal
United States of America
Issue Coordinator: James Mentzer (USA) jmentzer@doc.gov

## Slide 53: Agenda Item 1.4: Review, and revise if necessary, the limitations mentioned in Annex 7 to Appendix 30
Preliminary Proposal
United States of America
Issue Coordinator: TBD

## Slide 54: Agenda Item 1.9.1: Maritime autonomous devices
Preliminary Proposal
Mexico
Issue Coordinator: Robert Denny (USA) rdenny@ntia.doc.gov
Alt Coordinator: Waldon Russell (BAH) wrussell@urcabahamas.bs

## Slide 55: Agenda Item 1.13: IMT in the frequency range 24.25 GHz to 86 GHz
Preliminary Proposal – Band CDE
Brazil
Issue Coordinator: Camilo ZAMORA – COL - camilo.zamora@ane.gov.co

## Slide 56: Agenda Item 1.13: IMT in the frequency range 24.25 GHz to 86 GHz (2 of 2)
Preliminary Proposal – Band J
Brazil
Issue Coordinator: Camilo ZAMORA – COL - camilo.zamora@ane.gov.co

## Slide 57: Agenda Item 1.14: High Altitude Platform Systems
Preliminary Proposal
Mexico
Issue Coordinator: Ana Valadares (B) avaladares@fb.com
Alt Coordinator: Vassilios Mimis (Canada) vmimis@primus.ca

## Slide 58: Agenda Item 1.15: To consider identification of frequency bands for use by administrations for the land-mobile and fixed services applications operating in the frequency range 275 450 GHz
Proposal
United States of America
Issue Coordinator: José COSTA – CAN - jose.costa@ericsson.com

## Slide 59: Agenda Item 1.16: WAS/RLANs in 5 GHz
Preliminary Proposal
Mexico, Brazil (B/1.16/1 only)
Issue Coordinator: [TBD]
Alt. Coordinator: Jayne Stancavage (USA) jayne.stancavage@intel.com

## Slide 60: Agenda Item 7: Changes in response to Resolution 86 – Satellite network regulatory procedures
ISSUE E: Harmonization of RR Appendix 30B with RR Appendices 30 and 30A
Preliminary Proposal
United States of America
NOC USA/7/E/1
APPENDIX 30B (REV. WRC-15)
Reason: With respect to provision (§ 4.1.24) of Appendices 30 and 30A for Regions 1 and 3:
4.1.24 No assignment in the List shall have a period of operation exceeding 15 years, counted from the date of bringing into use, or 2 June 2000, whichever is later. Upon request by the responsible administration received by the Bureau at the latest three years before the expiry of this period, this period may be extended by up to 15 years, on condition that all the characteristics of the assignment remain unchanged.
This provision is limited to satellite networks serving Regions 1 and 3 only and there is no such provision in RR AP30/30A for networks serving Region 2. Therefore, any changes to RR AP30B should not be applicable to Region 2. Moreover, there is no linkage between RR AP30/30A, which was created for the broadcasting-satellite service, and RR AP30B, which was created for the fixed-satellite service. Each of these appendices have its own set of conditions and procedures. Consequently, there is no need for harmonization amongst those plans. Those plans were established for two different satellite services for different purposes.
Coordinator: Brandon Mitchell (USA): bmitchell@ntia.doc.gov

## Slide 61: Agenda Item 7: Changes in response to Resolution 86 – Satellite network regulatory procedures
ISSUE I: Additional RR Appendix 4 data items to be provided for non-geostationary satellite systems with multiple orbital planes
Preliminary Proposal
Canada
Coordinator: Brandon Mitchell (USA): bmitchell@ntia.doc.gov

## Slide 62: Agenda Item 7: Changes in response to Resolution 86 – Satellite network regulatory procedures
ISSUE K: Difficulties for Part B examinations under § 4.1.12 or 4.2.16 of RR Appendices 30 and 30A and § 6.21 c) of RR Appendix 30B
Preliminary Proposal
United States
Coordinator: Brandon Mitchell (USA): bmitchell@ntia.doc.gov

## Slide 63: Issue 9.1.1: Terrestrial and Satellite Components of IMT in 2 GHz
Preliminary Proposal
United States of America
Issue Coordinator: TBD
Alt Coordinator: Olmo Ramirez (Mexico) olmo.ramirez@ift.org.mx

## Slide 64: Issue 9.1.4: Terrestrial and Satellite Components of IMT in 2 GHz
Preliminary Proposal
United States of America
Issue Coordinator: TBD
Alt Coordinator: Olmo Ramirez (Mexico) olmo.ramirez@ift.org.mx

## Slide 65: Issue 9.1.7: Unauthorized operation of earth station terminals
Preliminary Proposal
United States of America
Issue Coordinator: Hugo Mario TRIVIÑO (Colombia) htrivino@mintic.gov.co

## Slide 66: Issue 9.1.7: Unauthorized operation of earth station terminals
Preliminary Proposal
United States of America
Issue Coordinator: Hugo Mario TRIVIÑO (Colombia) htrivino@mintic.gov.co

## Slide 67: Agenda Item 10: Agenda Items for WRC-23
Preliminary Proposal – the use of the frequency bands 17.7-20.2 GHz and 27.5-29.1 GHz and 29.5-30.0 GHz by earth stations on mobile platforms communicating with non-geostationary space stations in the fixed-satellite service
CANADA
Coordinator: Martha SUAREZ – CLM – martha.suarez@ane.gov.co

## Slide 68: Agenda Item 10: Agenda Items for WRC-23
Preliminary Proposal
Brazil – proposal to include a WRC-23 agenda item that deals of the space weather sensors in accordance of the Resolution 657 (WRC-15).
Coordinator: Martha SUAREZ – CLM – martha.suarez@ane.gov.co

## Slide 69: Agenda Item 10: Agenda Items for WRC-23
Preliminary Proposal
Brazil – administrative items relating to Resolution 810 (WRC-15).
Coordinator: Martha SUAREZ – CLM – martha.suarez@ane.gov.co

## Slide 70
PRELIMINARY VIEWS (PV)
PRELIMINARY VIEWS (PV): a Member State’s initial view of an Agenda Item, indicating its view of a future proposal or position.

## Slide 71: Agenda Item 1.5: The use of the frequency bands 17.7-19.7 GHz (space-to-Earth) and 27.5-29.5 GHz (Earth-to-space) by earth stations in motion
Preliminary Views of Brazil, Canada, Mexico and USA
Coordinator: Brandon MITCHELL – bmitchella@ntia.doc.gov
Notes: Agenda Item 1.5: To consider worldwide/regional harmonization of spectrum for electronic news gathering (ENG), taking into account the results of ITU-R studies, in accordance with Resolution 954 (WRC-07)
Issues
To review the needs of ENG systems, to decide if harmonization is possible, and in what potential bands such harmonization is appropriate. This issue may also lead to requests from administrations for consideration of additional spectrum allocations.
Preliminary views
CAN
Canada supports ongoing efforts in the ITU-R to study this issue.
USA
The United States supports reviewing the requirements developed in WP 6A to determine if harmonization is feasible on a regional/global basis for ENG systems. The United States supports studies on technologies for ENG that maximize efficient and flexible use of frequencies at the national level in lieu of global/regional identification of frequency bands. If studies demonstrate that such harmonization is required and feasible, the United States supports focusing on studying the impact of identifying in the Radio Regulations harmonized spectrum for ENG systems on the existing services.

## Slide 72
Preliminary Views of Brazil, Canada, Mexico, USA
Coordinator: Brandon MITCHELL – bmitchella@ntia.doc.gov
Agenda Item 1.6: To consider regulatory framework for non-GSO FSS satellite systems that may operate in the frequency bands 37.5-39.5 GHz (space-to-Earth), 39.5 42.5 GHz (space-to-Earth), 47.2-50.2 GHz (Earth-to-space) and 50.4-51.4 GHz (Earth-to-space).

## Slide 73: Agenda Item 1.7: Non-GSO satellites with short duration missions
Preliminary views of Canada, Mexico, and USA
Coordinator: Glen Feldhake – USA - glenn.s.feldhake@nasa.gov

## Slide 74: Agenda Item 2: ITU-R Recommendations incorporated by reference (Resolutions 27 and 28)
Preliminary Views
TBD
Notes: Agenda Item 2: Revise ITU-R Recommendations incorporated by reference in the Radio Regulations.
Issues
Monitor the development of new and revised ITU-R Recommendations and determine whether these should be incorporated by reference in the Radio Regulations.
Preliminary Views:
Some administrations believe that:
Resolutions 27 and 28 provide clear guidance on the principles and application for incorporating by reference ITU-R Recommendations in the Radio Regulations. Consequently, no revisions to these Resolutions are necessary at this time.
WRC-07 should follow the incorporation by reference process in Resolution 27 (Rev.WRC-03) and Resolution 28 (Rev.WRC-03).
Administrations should, in accordance with Resolution 28, review those revised ITU-R Recommendations listed by the Director to the CPM and communicated by the RA to the WRC to determine whether the updated version should be incorporated by reference in the R.R. in place of the previous version.

## Slide 75: Agenda Item 4: Review of Resolutions and Recommendations (Resolution 95)
Preliminary Views
TBD

## Slide 76: Agenda Item 7: Changes in response to Resolution 86 – Satellite network regulatory procedures
Preliminary Views
ISSUE A:
Canada
Canada is of the view that the current seven-year period may not be enough to deploy a “mega” non-GSO constellation. In trying to address this issue, it is important to adopt a balanced approach, taking into account the financial, technological and planning challenges posed by the multiple launches required to deploy this type of constellation but also the need to prevent any abuse that may lead to spectrum reservation. In this context, a milestone approach appears to be an appropriate solution.
Issue Coordinator: Michelle Caldeira (B) Michelle.caldeira@ses.com
Alt Coordinator: Angeles Gallego (Mexico) mgallego@satmex.com

## Slide 77: Agenda Item 7: Changes in response to Resolution 86 – Satellite network regulatory procedures
Preliminary Views
ISSUE C6
Canada
Canada supports allowing notifying administrations to submit simultaneously the Appendix 4 data elements for the purposes of entering the frequency assignments in the List (§6.17) and recording them (§8.1)
Issue Coordinator: Michelle Caldeira (B) Michelle.caldeira@ses.com
Alt. Coordinator: Angeles Gallego (Mexico) mgallego@satmex.com

## Slide 78: Agenda Item 7: Changes in response to Resolution 86 – Satellite network regulatory procedures
Preliminary Views
ISSUE E
Canada
These administrations support extending the current Bureau identification and publication of the satellite networks or systems to be considered when effecting coordination under No. 9.7 and 9.7A to other types of coordination, namely coordination under No. 9.12, 9.12A or 9.13 as appropriate.
Issue Coordinator: Michelle Caldeira (B) Michelle.caldeira@ses.com
Alt Coordinator: Angeles Gallego (Mexico) mgallego@satmex.com

## Slide 79: Agenda Item 8: Deletion of country footnotes, deletion of country names from footnotes (Resolution 26)
Preliminary Views
TBD
Issue Coordinator: TBD

## Slide 80: Issue 9.1.9: Studies relating to spectrum needs and possible allocation of the frequency band 51.4-52.4 GHz to the fixed-satellite service (Earth-to-space)
Preliminary Views of Canada, Mexico, and USA
Issue Coordinator: Jennifer Manner (USA) jennifer.manner@echostar.com

## Slide 81: Agenda Item 9.2: Difficulties and inconsistencies encountered in the application of the Radio Regulations
Preliminary Views
TBD
Issue Coordinator: Marc Dupuis (Canada) marc@oneweb.net

## Slide 82: Agenda Item 9.3: On action in response to Resolution on action in response to Resolution 80 (Rev.WRC‑07)
Preliminary Views
TBD
Issue Coordinator: TBD

## Slide 83: Next PCCII meeting Brasilia, Brazil December 3 – 6, 2018

## Slide 84: Additional PCCII Information at:
https://www.citel.oas.org/en/Pages/PCCII/default.aspx

## Slide 85
Thank you very much for your attention
Mike Biggs
http://www.citel.oas.org
citel@oas.org