## Slide 1: WRC-19 – Agenda Items for Other Issues
Andrew Roy - ASRI

## Slide 2: Scope
1.7 - Non-GSO satellites
1.8 - Global Maritime Distress Safety Systems (GMDSS)
1.9 – Maritime Automatic Identifications System (AIS) and VHF data exchange system (VDES)
1.11 - railway radiocommunication systems
1.12 - Intelligent Transport Systems (ITS)
1.13 – New IMT between 24.25 and 86 GHz
1.14 - High-altitude platform stations (HAPS)
1.16 - Radio local area networks 5150 MHz and 5925 MHz
9.1.3 - Non-geostationary-satellite orbit systems in C-band
9.1.6 - Wireless Power Transmission (WPT)
10 – Future agenda items

## Slide 3: Supporting Info
Final ICAO WRC-19 position document (approved June 2017)
  https://www.icao.int/safety/FSMP/Documents
  See folder ‘ITU-WRC19’
ITU-R list of WRC-19 Agenda Items
  http://www.itu.int/en/ITU-R/study-groups/rcpm/Pages/wrc-19-studies.aspx
  Identifies lead ITU-R study group for each item
  Links to latest study group work (requires ITU TIES account)

## Slide 4: Agenda Item 1.7
To study the spectrum needs for telemetry, tracking and command in the space operation service for non-GSO satellites with short duration missions
Assess the suitability of existing allocations to the Space Operation Service (SOS)
If necessary, to consider new SOS allocations
Resolution 659 (WRC 15).

## Slide 5: Agenda Item 1.7 - Commentary
WRC-19 studies will determine if existing SOS allocations are sufficient
  If not, will consider new allocations within the frequency ranges 150.05-174 MHz and 400.15-420 MHz.
  Studies need to conclude if Space-to-Earth transmission in the 150 MHz range will effect VDLM 2 Common Signaling Channel (CSC) at 136.975 MHz.
Additional concern of the affect on COSPAS SARSAT (EPIRB) in 406.1 MHz
Space planes may want to use SOS spectrum
  Need to ensure flexibility for any space plane use of SOS spectrum

## Slide 6: Agenda Item 1.7 - Updates
Draft CPM text available
  Studies for adjacent channel interference from proposed NGSO SD satellite system to COSPAS-SARSAT would exceed threshold
    Mitigation is to employ 100 kHz guard bands above 406.1 MHz and below 406 MHz for NGSO SD space-to-Earth transmissions
    NGSO SD satellite earth stations would implement guard bands 1 MHz below 406 MHz and 900 kHz above 406.1 MHz to protect spaceborne receiver
3 Proposed Methods to satisfy agenda item
  Method A
    No Change
  Method B
    Allocate 403- 406 MHz to space operation service, in either 403-404 MHz or 404-405 MHz
  Method C
    Use 137-138 MHz for downlink and the band 148-149.9 MHz for uplink and to provide appropriate associated regulatory provisions
    Remove coordination of 9.21 in RR No. 5.218 for 148-149.9 MHz

## Slide 7: Agenda Item 1.7 - ICAO Position
To oppose any new allocations to the space operations service unless agreed ITU-R studies have proven sharing and compatibility with aviation systems. In particular, oppose consideration of possible allocation to the space operation service in the frequency range 405.9 – 406.2 MHz unless agreed ITU-R studies have proven aviation use of the EPIRBs operating in the frequency band 406 - 406.1 MHz is protected in accordance with Resolution 205 (rev. WRC-15) and RR No. 5.267.
To ensure that any change to the regulatory provisions and spectrum allocations resulting from this agenda item do not preclude the use of SOS allocations for space planes if this service is deemed appropriate for such use.

## Slide 8: Agenda Item 1.8
Regulatory actions to support Global Maritime Distress Safety Systems (GMDSS) modernization
To support the introduction of additional satellite systems into the GMDSS
Resolution 359 (Rev.WRC 15)

## Slide 9: Agenda Item 1.8 - Commentary
Search and rescue aircraft are an integral part of the global maritime distress and safety system
  Need to ensure no adverse impact on the capability of search and rescue aircraft
If AMS(R)S system which already carries such communications is identified to also carry GMDSS
  Any AMS(R)S use must comply with priority requirements contained in ICAO SARPS

## Slide 10: Agenda Item 1.8 – CPM Text
Issue A: GMDSS Modernization – Resolve 1 of Resolution 359 (Rev. WRC-15) – WP 5B
  Method A1
    No Change
  Method A2
    MF navigational data (NAVDAT)
      Identify 500 kHz band for MF NAVDAT , remove radiotelegraphy for region 2
    HF NAVDAT
      Modify Appendix 17 to allow certain frequency bands in M.2058, and develop proper regulatory provisions
      WRC-23 will consider modernization after IMO work concluded
  Draft CPM Text

## Slide 11: Agenda Item 1.8 – CPM Text
Issue B: Additional satellites systems - Resolve 2 of Resolution 359 (Rev. WRC-15) – WP 4C
  6 Methods available
  Issues arise from secondary status in MSS (space-to-Earth) Direction
    Methods include upgrading band 1 621.35-1 626.5 MHz to primary allocation

## Slide 12: Agenda Item 1.8 - ICAO Position
To ensure that any change to the regulatory provisions and spectrum allocations resulting from this agenda item do not adversely impact on the capability of search and rescue aircraft to effectively communicate with vessels during disaster relief operations.
To ensure that any regulatory provisions in response to this agenda item do not adversely impact SARPS compliance of aeronautical mobile-satellite (route) service satellite systems.

## Slide 13: Agenda Item 1.9 (incl 1.9.1 & 1.9.2)
1.9.1 - Regulatory actions within the frequency band 156-162.05 MHz for autonomous maritime radio devices (AMRD) to protect the GMDSS and automatic identifications system (AIS)
  Classified into 2 different groups:
    Group A: AMRD that enhance the safety of navigation
    Group B: AMRD that do not enhance the safety of navigation
1.9.2 - Modifications of the Radio Regulations, including new spectrum allocations to the MMSS (E-s & s-E)
  Preferably within the frequency bands 156.0125-157.4375 MHz and 160.6125-162.0375 MHz of Appendix 18
  Enable a new VHF Data Exchange System (VDES) satellite component
  Do not degrade the current terrestrial VDES components or AIS
  Resolution 360 (Rev.WRC 15)

## Slide 14: Agenda Item 1.9 - Commentary
Search and rescue aircraft are an integral part of the global maritime distress and safety system
  Need to ensure no adverse impact on the capability of search and rescue aircraft

## Slide 15: Agenda Item 1.9.1 - Updates
1.9.1 – Draft CPM text updated
  AMRD Group A (safety of navigation)
    Modify footnote for RR Appendix 18.
  AMRD Group B
    3 methods
      Break down frequency bands and type by footnote in Appendix 18

## Slide 16: Agenda Item 1.9.2 - Updates
1.9.2 – Draft CPM Text
  5 Methods available
  Methods include new primary or secondary allocation to MMSS (Earth to space and space-to-Earth)

## Slide 17: Agenda Item 1.9 - ICAO Position
To ensure that any change to the regulatory provisions and spectrum allocations resulting from this agenda item do not adversely impact aviation systems, including the capability of search and rescue aircraft to effectively communicate with vessels during disaster relief operations.

## Slide 18: Agenda Item 1.11
Railway radiocommunication systems between train and trackside
  Actions to facilitate global or regional harmonized frequency bands within existing mobile service allocations
Resolution 236 (WRC-15)

## Slide 19: Agenda Item 1.11 - Commentary
Evolving rail operations requiring additional communications between train and trackside systems
  Meeting the needs of a high-speed railway environment
  New functions may not be supported by the current narrowband railway radiocommunication systems
Existing railway communication bands include 140-150 MHz, 330 – 360 MHz, 410 – 420 MHz and 450 – 460 MHz
  328.6 – 335.4 MHz an ARNS allocation for ILS glide slope
Aeronautical mobile service is a subset of the mobile service
  Need to protect existing aviation allocations

## Slide 20: Agenda Item 1.11 - Updates
Draft CPM Text available
  3 Methods available
    NOC
    New Resolution specifying frequency ranges within resolution or using recommendation

## Slide 21: Agenda Item 1.11 - ICAO Position
To ensure, on the basis of agreed ITU-R studies, that any regulatory actions within existing mobile-service bands do not impact existing aeronautical systems operating in accordance with the Radio Regulations.

## Slide 22: Agenda Item 1.12
Evolution of Intelligent Transport Systems (ITS)
  Consider possible global or regional harmonized frequency bands for implementation
  Use existing mobile-service allocations
Resolution 237 (WRC 15).

## Slide 23: Agenda Item 1.12 - Commentary
New technologies can be integrated in a vehicle system to provide Intelligent Transport Systems (ITS)
  Improving traffic management and assisting safe driving
Harmonization of existing frequency bands for ITS not worldwide
Current frequencies being considered:
  5 855- 5 925 MHz (dedicated short range communications)
  63 – 64 GHz (integrated systems for ITS)
    Close proximity communication
Aeronautical mobile service is a subset of the mobile service
  Need to protect existing aviation allocations

## Slide 24: Agenda Item 1.12 - Updates
3 methods available
  Method A: No change to the Radio Regulations because ITS continue to operate within existing mobile service allocations and the required harmonization of frequencies for ITS can be achieved through ITU‑R Recommendations and Reports.
  Method B: No change to the table of frequency allocations in the Radio Regulation, and add a new WRC Resolution to encourage administrations to use globally and regionally harmonized frequency bands for ITS applications.
  Method C: No change to the table of frequency allocations in the Radio Regulation, and add a new WRC Resolution to encourage administrations to use globally and regionally harmonized frequency bands for ITS applications by referring to the most recent version of Recommendation ITU-R M.[ITS_FRQ].
  Draft CPM Available

## Slide 25: Agenda Item 1.12 - ICAO Position
To ensure, on the basis of agreed ITU-R studies, that any regulatory actions within existing mobile-service bands do not impact existing aeronautical systems operating in accordance with the Radio Regulations.

## Slide 26: Agenda Item 1.13
International Mobile Telecommunications (IMT) above 24 GHz
  Requires identification of frequency bands for the future development
Resolution 238 (WRC 15)
Responsibility of TG 5/1
  Last meeting 2-11 May
“Gentle” agreement at last plenary that no new technical would be submitted to the next meeting, except where no studies have been received

## Slide 27: Agenda Item 1.13 – Commentary
A number of frequency bands/ranges between 24.25 and 86 GHz have been identified for IMT (terrestrial)
8 bands already have a primary MS allocation
  24.25-27.5 GHz, 37-40.5 GHz, 42.5-43.5 GHz, 45.5-47 GHz, 47.2-50.2 GHz, 50.4-52.6 GHz, 66-76 GHz and 81-86 GHz
3 bands may require additional primary MS allocations
  31.8-33.4 GHz, 40.5-42.5 GHz and 47-47.2 GHz
24.25-24.65 GHz & 31.8-33.4 GHz bands are identified for Airport Surface Detection Equipment (ASDE)
  31.8-33.4 GHz also used for embedded systems that generate navigation information/video for pilots

## Slide 28: Agenda Item 1.13 - Commentary Cont.
76-81 GHz is allocated to the radiolocation service
  Planned for non safety-critical, advisory applications on the airport surface such as wing-tip radar
  Band excluded from studies, but will need to be protected from adjacent band emissions either side
43.5-47 GHz and 66-71 GHz have allocations to the RNS and/or RNSS
  No aeronautical systems have currently been identified as operating in those frequency bands
Agenda Item work being developed in separate ITU-R Task Group 5/1
  Meeting collocated with ITU Working Parties 5A, 5B & 5C
  Draft CPM Text

## Slide 29: Agenda Item 1.13 - ICAO Position
To oppose any identification of a frequency band for IMT that could impact aviation systems, within a new or existing allocation to the mobile service in the frequency range 24.25 GHz to 86 GHz, unless agreed ITU-R studies demonstrate no adverse impact to those systems.

## Slide 30: Agenda Item 1.14
Appropriate regulatory actions for high-altitude platform stations (HAPS)
  Within existing fixed-service allocations.
Resolution 160 (WRC 15)

## Slide 31: Agenda Item 1.14 - Commentary
High altitude platform stations (HAPS) stations located on an object at an altitude of 20-50 km
  Operate at a specified, nominal, fixed point relative to the Earth
Reviewing current RR identifications for HAPS
  6 440-6 520 MHz, 6 560-6 640 MHz, 27.9-28.2 GHz, 31.0-31.3 GHz, 47.2-47.5 GHz and 47.9-48.2 GHz
Additional spectrum possible in other FS bands
  38-39.5 GHz globally
  21.4-22 GHz and 24.25-27.5 GHz in Region 2

## Slide 32: Agenda Item 1.14 – Commentary Cont
Future aviation may wish to incorporate the use of HAPS
  Global air ground communication network
  Alternative to VSAT ground networks
Additional concerns regarding the platform on which the HAPS resides
  Radio links used for the HAPS communications service function do not impact any radio links used for safe operation (e.g., command and control links or see-and-avoid) of those platforms

## Slide 33: Agenda Item 1.14 – Updates
Draft CPM Text
Method A – No change
Method B – Designation of bands for HAPS, in accordance with Resolution 160 (WRC-15) with options
  Method B1 – Revision of the regulatory provisions for HAPS in the fixed service (FS) with a primary status in bands already designated for HAPS.
  Method B2 – Add new designation(s) for HAPS in bands already allocated to the FS with a primary status.
  Method B3 – Add a primary allocation to the FS and a new designation for HAPS in the band 24.25-25.25 GHz (Region 2) not already allocated to the FS.
Method C – Suppress the existing HAPS designation, pursuant to resolves 3 of Resolution 160 (WRC-15).

## Slide 34: Agenda Item 1.14 - ICAO Position
If agreed ITU-R studies demonstrate there is no adverse impact on aeronautical systems including those used for the safe operation of the platform on which the HAPS resides, then support the use of fixed service allocations for HAPS provided that any regulatory actions taken within the existing allocations to the fixed service noted in Resolution 160 (WRC-15) do not constrain the potential future use of those HAPS fixed links as part of aeronautical communication systems (e.g., VSAT enhancement).

## Slide 35: Agenda Item 1.16
Consider wireless access systems, including radio local area networks (WAS/RLAN)
  5 150 MHz and 5 925 MHz
Take the appropriate regulatory actions, including additional spectrum allocations to the mobile service
Resolution 239 (WRC 15)

## Slide 36: Agenda Item 1.16 - Commentary
5 150-5 250 MHz
  Use of WAS/RLAN in this band is currently limited to indoor systems
  Intent to show compatibility between incumbent services and outdoor WAS/RLAN systems
  Allocated worldwide on a primary basis to the ARNS & FS
    AMS allocation in Region 1 (some countries) and Brazil
  possible UAS sense and avoid collision awareness systems
    Designed to operate independently of Aircraft Collision Avoidance Systems (ACAS)
  Frequency band below 5 150 MHz allocated for ARNS, AMS(R)S, and AM(R)S
    Includes AeroMACS system

## Slide 37: Agenda Item 1.16 – Commentary Cont
5 350-5 470 MHz
  Allocated worldwide on a primary basis to the ARNS
    Airborne weather radars
    Previous ITU-R studies indicated that sharing with WAS/RLAN was not feasible
  Autonomous UAS sense and avoid system described for the 5 150-5 250 MHz band above, is also being designed to be capable of operating in this frequency band
5 850-5 925 MHz
  Primary mobile allocation in all three regions
  Some countries in Region 2 have an AMS allocation in 5925-6700 MHz
    Does not preclude the use of this band by other mobile service applications
  FSS usage (E-s) by VSATs for critical aeronautical and meteorological information
Notes: if existing WAS/RLAN mitigation measures limited to the regulatory provisions of Resolution 229 (Rev.WRC-12) were used

## Slide 38: Agenda Item 1.16 - Updates
Draft CPM Text
5150 – 5250 MHz
  4 Methods
  NOC; Enable Outdoor with new EIRP Limit; Enable outdoor with same conditions for 5 250- 5 350;Enable in Vehicle use
5 725-5 850 MHz
  3 Methods
  NOC & SUP Resolution 239; New Worldwide or Regional Primary MS Allocation & MOD Res 229; Accommodate WAS/RLAN in an existing or new footnote
Other Frequencies
  NOC

## Slide 39: Agenda Item 1.16 - ICAO Position
To ensure, on the basis of agreed ITU-R studies, that any new provisions, or changes to existing regulatory provisions, in the frequency bands/ranges 5 150 -5 250 MHz, 5 350 – 5 470 MHz and 5 850 – 5 925 MHz do not adversely impact aviation systems.

## Slide 40: Agenda Item 9.1.3
Study of technical and operational issues and regulatory provisions for non-geostationary-satellite orbit systems
  Existing frequency bands allocated to the fixed-satellite service
  3 700 – 4 200 MHz, 4 500 -4 800 MHz, 5 925 – 6 425 MHz and 6 725 – 7 025 MHz
Resolution 157 (WRC-15)

## Slide 41: Agenda Item 9.1.3 - Commentary
3 700 – 4 200 MHz and 5 925-6 425 MHz are the main bands for VSAT transmissions used for aeronautical ground-ground communications
  Often used in remote areas
Adjacent to ARNS and AM(R)S band 4 200 – 4 400 MHz
  Both radio altimeter and Wireless Avionics Intra-Communication (WAIC) system

## Slide 42: Agenda Item 9.1.3 - Updates
Draft CPM Text available
  One study indicates that circular-orbit non-GSO FSS operations in the 6/4 GHz band could result in large exceedances of the GSO protection criteria
  Another study suggested to envisage the establishment of aggregate epfd limits that would be verified through multilateral meetings.

## Slide 43: Agenda Item 9.1.3 - ICAO Position
To oppose any new or changes to existing regulatory provisions in Article 21 of the ITU Radio Regulations for the frequency bands 3 700 – 4 200 MHz and 5 925-6 425 MHz unless it has been demonstrated through agreed ITU-R studies that there will be no impact from the potential introduction of new non-geostationary-satellites on aviation use in those bands.
To oppose introduction of new non-geostationary-satellites in frequency bands near to the frequency band 4 200 – 4 400 MHz unless aviation use of that band is ensured through agreed ITU-R studies.

## Slide 44: Agenda Item 9.1.6
Studies for Wireless Power Transmission (WPT) for electric vehicles (EV)
  Preparation for WRC-19
Resolution 958 (WRC-15)

## Slide 45: Agenda Item 9.1.6 - Commentary
WPT being considered in ISM bands in the low and very low frequency ranges, as well as MF band
  19 – 21 kHz, 59 – 61 kHz, 79 – 90 kHz, 100 – 300 kHz, 6 765 – 6 795 kHz
  Power limits of up to 100kW for charging electric vehicles
  100 – 300 kHz, 6 765 – 6 795 kHz used for mobile device charging
Majority of work conducted externally to ITU-R standards organizations
Broader bandwidth with more complex modulation mechanisms than existing WPT technology
  Potentially leaking large amounts of power into adjacent band
  HF bands at potential risk

## Slide 46: Agenda Item 9.1.6 - Updates
Draft CPM text
  Loran-C compatibility feasible with Electric Vehicle Wireless Power Transmission in 81.38-90 kHz
  WPT-EV operation in 55-65 kHz will cause harmful interference to Standard Frequency and Time Signals (SFTS) up to 60 kHz
    Appropriate Frequency Separation needs to be studied.

## Slide 47: Agenda Item 9.1.6 - ICAO Position
To ensure that the protection of aeronautical systems is appropriately taken into account during the studies called for in response to Resolution 958 (WRC-15).

## Slide 48: 10 – Future agenda items
?

## Slide 49: Supporting Info
Final ICAO WRC-19 position document (approved June 2017)
  https://www.icao.int/safety/FSMP/Documents
  See folder ‘ITU-WRC19’
ITU-R list of WRC-19 Agenda Items
  http://www.itu.int/en/ITU-R/study-groups/rcpm/Pages/wrc-19-studies.aspx
  Identifies lead ITU-R study group for each item
  Links to latest study group work (requires ITU TIES account)

## Slide 50: Questions?