## Slide 1: RTCA MOPS for Unmanned Aircraft Systems (UAS) Control and Non-Payload Communications (CNPC)
C2 LINK
ICAO
Don Nellis
8/29/2016

## Slide 2: RTCA UAS and Frequency Spectrum
CNPC/C2 Link MOPS Phase 1 (Final approval pending)
CNPC/C2 Link MOPS Phase 2
  due 2018 Satcom
  due 2020 Terrestrial update/network
DAA MOPS Phase 1 (Due Winter 2016)
DAA MOPS Phase 2 (Future)

## Slide 3: RTCA C2 MOPS Phase 1
Minimum Operating Performance Standards (MOPS) For Unmanned Aircraft Systems (UAS) Control and Non-Payload Communications (CNPC) (Terrestrial Only)

## Slide 4: UAS Concept of Operations
Phase 1 TOR focus
Phase 1 MOPS also supports terrestrial networks (based on proprietary handover functionality) but does not address any industry standard handover capability, which will be addressed in Phase 2.

## Slide 5: Intended Function of CNPC Link Systems
The CNPC Link Systems addressed in the RTCA’s MOPS shall provide CNPC Link capabilities supporting the UAS information exchanges that allow the pilot to safely control, monitor, and manage the UA (often called the control and communication, C2, function of the UAS).
Depending on the intended operations, the systems and equipment shall also provide CNPC Link System capabilities supporting one or more of the following functions:
Air Traffic Control voice and data relay
Detect and avoid data exchange
Weather radar data exchange
Video data exchange
The CNPC Link System shall not cause a hazard to other users of the National Airspace System.

## Slide 6: CNPC Information Flows between Pilot and UA

## Slide 7: Basic Internal and External Non-Payload Information Flows of a UAS

## Slide 8: Security Considerations
Higher layer security considerations, can either be implemented inside the CNPC Link System or within the remaining UAS System.
CNPC Link System user plane and control plane security controls shall provide:
Mutual peer entity authentication between the Airborne Radio System and the Ground Radio System
Access control to authorize the Airborne Radio System access to the Ground Radio System
Data origin authentication of user and control plane traffic between the Airborne Radio System and the Ground Radio System
Data integrity for user and control plane traffic between the Airborne Radio System and the Ground Radio System
Confidentiality when sensitive user and control plane traffic is exchanged between the Airborne Radio System and Ground Radio System
The security controls shall additionally be implemented with the following characteristics:
Using cryptographic algorithms with algorithm strength and key length sufficient to protect data in transit
Using formally validated cryptographic modules

## Slide 9: Terrestrial Link Radio Systems
CNPC is an internal interface within the applicant’s system. It is not an external interface to ATS (Air Traffic Services) operational infrastructure (e.g. XPDR, ADS-B, CPDLC, Voice Comm)
Interoperability between radios or systems is not a requirement, only electromagnetic compatibility.
Under the current TOR (Terms of Reference) RCTA SC-228 covers the MOPS Validation Baseline as well as Manufacturer Specific radio specifications.
  Since the market is still maturing and different UAS will require different performance both MOPS Validation Baseline CNPC Link System and Manufacturer-Specific CNPC Link Systems are addressed in the MOPS
  MOPS Validation Baseline does not provide low level details to allow manufacturers to replicate an interoperable system but was primarily intended to validate the MOPS.
  Manufacturer-Specific designs are allowed and can use the flight test data from MOPS validation flight tests with deterministic scaling of performance (within prescribed limits)
Initial implementation is expected to be stand- alone LOS (Line-of-Sight) systems to support limited geographic area.
CNPC Link System Components

## Slide 10: Specifications
Frequency bands:
  C-Band: 5030-5091 MHz
  L-Band: 1040-1080 MHz
  1104-1150 MHz
Power (max):
  C-Band:10W (Pavg: 18.6 dBm/kHz)
  L-Band: 32mW (Pavg: -3.4 dBm/kHz) limited to protect incumbent services
Transmitter Bandwidth:
Maximum Bandwidth is 250kHz
Also: In-Flight Emergency Video Channel of 500kHz
Two Takeoff and Landing Video Channel of 250kHz
The needed spectrum bandwidth will vary over time and location.

## Slide 11: Specifications (cont.)
MOPS Validation Baseline Transmitter Data Class Bandwidth:
  Data Class 1 62.5 kHz(C2 only)
  Data Class 2 125 kHz (C2 + 1 enhancement)
  Data Class 3 187.5 kHz (C2 + 2 enhancements)
  Data Class 4 250 kHz (C2+ 3 enhancements)
Manufacture-Specific Transmitter Data Class Bandwidths are flexible within in the maximum 250kHz allowed*
  Inefficient use of spectrum will be discouraged through various mechanisms
The bandwidth is determined by the needed data for a specific flight phase/scenario (e.g. C2 only, C2 with A/G comm, C2 with radar data, etc.).
*Note: the occupied bandwidth can vary, from one user to another and at one time to another (in 5kHz increments).

## Slide 12: Specifications (cont.)
For the CNPC terrestrial MOPS we are using TDD instead of FDD to separate transmission from reception due to inefficient use of spectrum (diplexer cross over band) and the size and weight of the filters required in the aircraft.
DOWNLINK SUBFRAME
TDD structure is based on TDD frames lasting 50 milliseconds each
Uplink TDD subframe is lasting 24.3 milliseconds and the subsequent Downlink TDD subframe is lasting 25.7 milliseconds
Uplink TDD subframe includes 1.3 milliseconds of guard time to account for propagation delays and timing errors
Downlink TDD subframe includes 2.7 milliseconds of guard time to account for propagation delays and timing errors
TDD FRAME 50ma
CNPC TDD Frame Structure

## Slide 13: Emission Limits for CNPC Transmitters in Specific Bands
Band (MHz) | Systems in Band | Maximum CNPC Link System Power Spectral Density Allowed in Band a, b, c |  | Remarks
 |  | CNPC Link System Ground Radios | CNPC Link System Airborne Radios | 
0.009–0.15 | LORAN | –36 dBm/kHz | –36 dBm/kHz | Same as VDL Mode 2/3 MOPS
0.15–30 | ADF, AM Broadcast & HF COM | –36 dBm/10 kHz | –36 dBm/10 kHz | Same as VDL Mode 2/3 MOPS
30–108 | Military VHF, FM & TV Broadcast | –36 dBm/100 kHz | –36 dBm/100 kHz | Same as VDL Mode 2/3 MOPS
108–118 | VHF NAV | –36 dBm/100 kHz | –36 dBm/100 kHz | Same as VDL Mode 2/3 MOPS if no on board VHF NAV
 |  |  | –64 dBm/100 kHz | Protects on board VHF NAV with same level of protection VHF NAV is given by VDL Mode 2/3 MOPS
118–137 | VHF COM | –36 dBm/100 kHz | –36 dBm/100 kHz | Same protection as adjacent VHF NAV band if no on-board VHF COM Relay
 |  |  | –64 dBm/100 kHz | Protects on board VHF COM Relay with same level of protection VHF COM is given by other MOPS
137–960 | Military UHF, Land Mobile & Marine UHF Radio, Cellular/ Wireless | –36 dBm/100 kHz | –36 dBm/100 kHz | Same as VDL Mode 2/3 MOPS

## Slide 14: Emission Limits for CNPC Transmitters in Specific Bands (Cont.)
960–976 | CNPC, TACAN, JTIDS | +20 dBm/kHz, averaged over CNPC Link System transmitter channel | +20 dBm/kHz, averaged over CNPC Link System transmitter channel | Includes fundamental emissions in CNPC Link System tuning range. CNPC Link System mask envelope applies. Frequency/distance/altitude management needed to coexist with TACAN.
976–980 | UAT, ramp testers, JTIDS | –62.2 dBm/MHz | –43.2 dBm/MHz | Protects UAT. See Appendix G for rationale.
 |  |  | –81 dBm/MHz | Protects co-located UAT. See Appendix G.
980–1020 | CNPC, DME, TACAN, JTIDS | +20 dBm/kHz, averaged over CNPC Link System transmitter channel | +20 dBm/kHz, averaged over CNPC Link System transmitter channel | Includes fundamental emissions in this optional CNPC Link System tuning range. CNPC Link System mask envelope applies. Frequency/distance/altitude management needed to coexist with DME and TACAN.
1020–1027 | DME, TACAN | –62.2 dBm/MHz | –37.2 dBm/MHz | Protects Y-Mode DME interrogators. See Appendix G.
 |  |  | –61.2 dBm/MHz | Protects DME beacons. See Appendix G.
 |  |  | –81 dBm/MHz | Protects co-located DME and TACAN interrogators. See Appendix G.
1027–1033 | SSR, TCAS | –46.2 dBm/MHz | –21.2 dBm/MHz | Protects transponders and TCAS. See Appendix G.
 |  |  | –65 dBm in any 1 MHz | Protects co-located transponders and TCAS. See Appendix G.
1033–1087 | DME, TACAN, JTIDS | Same as for 1020–1027 MHz | Same as for 1020–1027 MHz | Same as for 1020–1027 MHz.

## Slide 15: Emission Limits for CNPC Transmitters in Specific Bands (Cont.)
1087–1093 | TCAS, | –56.2 dBm/MHz |  | Protects TCAS and Mode S ES on aircraft.
 | Mode S ES |  | –47.2 dBm/MHz | Protects offboard SSR interrogators and Mode S ES.
 |  |  | –65 dBm/MHz | Protects co-located TCAS.
 |  |  | –75 dBm in any 1 MHz | Protects co-located Mode S ES.
1093–1164 | DME, TACAN, JTIDS | Same as for 1020–1027 MHz | Same as for 1020–1027 MHz | Same as for 1020–1027 MHz.
1164–1197.6 | GNSS, JTIDS | –84.8 dBm in any 1 MHz | –86.5 dBm in any 1 MHz | CNPC Link System Ground Radio maximum is ITU-R Res. 417 AM(R)S EIRP density limit, minus assumed maximum CNPC Link System antenna gain. CNPC Link System Airborne Radio maximum is RTCA DO-235B limit of –146.5 dBW/MHz at GNSS receiver input, minus assumed 30 dB isolation.
1197.6–1215 | GNSS, JTIDS | –84.8 dBm in any 1 MHz | –86.4 dBm in any 1 MHz | ITU-R Res. 417 AM(R)S EIRP density limits, minus assumed maximum L-band CNPC Link System antenna gain.
1215–1300 | GNSS, radars | –84.8 dBm in any 1 MHz | –86.4 dBm in any 1 MHz | Same limits as those for 1197.6–1215 MHz band are assumed necessary here as well, to protect GPS L2 and other GNSS signals in this band.
1559–1605 | GNSS (GPS L1, Galileo E1, GLONASS, Beidou) |  | –86.5 dBm in any 1 MHz | RTCA DO-235B limit of –146.5 dBW/MHz at GNSS receiver input, minus assumed 30 dB isolation.

## Slide 16: Emission Limits for CNPC Transmitters in Specific Bands (Cont.)
5010–5030 | GNSS, AeroMACS | –113 dBW/MHz | –90 dBW/MHz | International Radio Regulations Footnote 5.443C AM(R)S EIRP density limit, minus assumed maximum C-band CNPC antenna gain.
5030–5091 | CNPC | +20 dBm/kHz, averaged over CNPC transmitter channel | +20 dBm/kHz, averaged over CNPC transmitter channel | Includes fundamental emissions in CNPC Link System tuning range. CNPC Link System mask envelope applies.
5091–5150 | AeroMACS | –68 dBm/MHz | –44 dBm/MHz | Protects AeroMACS.
 |  |  | –79 dBm/MHz | Protects co-located AeroMACS.

## Slide 17: Operational Limitations for C Band
For a CNPC Link System radio C Band, when at or less than 10NM from any takeoff and landing operation the Ground Stations:
  Must only be used for takeoff and landing operations.
  Must not be located closer than 500 ft to the takeoff and landing or taxiway location.
For a CNPC Link System radio C Band, the installed CNPC link system airborne power control must be used.
For a CNPC Link System radio C Band, when at or less than 10NM from any takeoff and landing operation the Airplanes:
  Must use high transmit power mode above 500 ft AGL.
  Must use low transmit power mode at or below 500 ft AGL.
  Must be operated above 3,000 ft AGL if not taking off or landing.
For a CNPC Link System radio C Band, when more than 10NM from any takeoff and landing operation the Ground Stations must only be used for enroute operations.
For a CNPC Link System radio C Band, when more than 10NM from any takeoff and landing operation the Airplanes:
  Must use high transmit power mode above 3,000 ft AGL.
  Must use low transmit power mode at or below 3,000 ft AGL.
  Must not be operated below 500 ft AGL.
Operational limitations are required to protect Airborne and Ground receivers under adverse near-far conditions

## Slide 18: Operational Limitations for L Band
For a CNPC Link System radio L Band the Ground Stations:
Must not be operated within a certain standoff distance of a navigation receiver (distance measuring equipment (DME), tactical air navigation (TACAN), automatic dependent surveillance –broadcast (ADS-B), Mode S, traffic collision avoidance system (TCAS), etc.).
For operation at any geographic location, demonstrate that the CNPC link system can adequately protect the currently operational ground and airborne equipment from interference.
For a CNPC Link System radio L Band the Airplanes:
Must not be operated above 3,000 ft above ground level (AGL).
Must not be operated within a certain standoff distance of a navigation receiver (DME, TACAN, ADS-B, Mode S, TCAS, etc.).
For operation at any geographic location, demonstrate that the CNPC link system can adequately protect the currently operational ground and airborne equipment from interference.
Operational limitations are required to protect Airborne and Ground receivers under adverse near-far conditions and Incumbent Services

## Slide 19: Future CNPC MOPS (Phase 2)
  SATCOM
    Ka
      10.95-11.2 GHz
      11.45-11.7 GHz
      11.7-12.2 GHz
      14.0-14.47 GHz
    Ku
      19.7-20.2 GHz
      29.5-30.0 GHz
    L
      1.5-1.6 GHz AMS(R)S *
      C
        5030-5091MHz **
  Networked terrestrial
  C-Band Terrestrial – Update
  * Note: Looking for, but do not want to impose changes to current requirements.
  ** Note: A long term solution. No SAT currently exists

## Slide 20: Detect-and-Avoid (DAA) MOPS
Frequency bands available for airborne Detect-and Avoid operations are (Phase 1):
    4.2-4.4 GHz (radio altimeter band)
    5.15-5.25 GHz
    5.35-5.47 GHz (aircraft weather radars)
    9.3-9.5 GHz (aircraft weather radars)
    13.25-13.4 GHz (helicopter station keeping radars)
    15.4-15.7 GHz
    24.450 -24.65 GHz
    32.30 – 33.4 GHz
Frequency bands for ground based Detect-and-Avoid operations are (Phase 2):
    1.24-1.37 GHz
    2.7-2.9 GHz
    9.0-9.2 GHz
For more info see: Report ITU-R M.2204