## Slide 1: SARPs and Manual on C2 Links for RPAS - Status Update -
– RPAS Panel WG2 –
FSMP WG/13-IP/01 – Agenda 3c
21-25 February, 2022

## Slide 2: ICAO Responsibilities regarding AI 1.8, WRC-23
ITU-R is looking to ICAO to provide SARPs that complement the ITU-R Resolution and, in particular for the FSS, provide for the equivalent safe operation elements in the absence of an AMS(R)S allocation
The ICAO SARPs, covering FSS and other C2 Link technologies, are being developed within the RPAS Panel
  Part I (Procedures) adopted in February 2021 and are now effective
  Part II (Systems) are underdevelopment and are anticipated to be adopted in Q1 2025
    Will be in State Letter review by WRC-2023

## Slide 3: C2 Link SARPs and Manual - Background
    Because the C2 Link is, for several reasons, very different to other aeronautical communication systems the C2 Link SARPs are contained in their own volume (Volume VI) of Annex 10
    Part I of Annex 10, Volume VI, contains the already adopted and effective Procedures associated with C2 Links
      Many additions also to Annex 6 “Operation of Aircraft” in support of the C2 Link Procedures
    RPASP WG2 is now developing the Systems SARPs for, Volume VI, Part II and the accompanying Manual on C2 Links for RPAS
      Planning Informal and Formal coordination between RPASP 18 (October 2021) and WGWHL/2 (October 2022)
        CP, CP-DCIWG, CP-OPDWLG, FLIRECSWG, FSMP, NSP, SASP, SMP, SP
      Planning to request RPASP approval to send the SARPs and Manual to the ANC at RPASP WGWHL/2, October 2022
      Planning that the ANC will hold a Preliminary Review of these SARPs in Q4 2022
      Anticipated adoption of SARPs in Q1 2025

## Slide 4: C2 Link SARPs and Manual - Background
    The C2 Link is a “black box” connecting the RPS and the RPA
      Supports all remote pilot activities required to safely manage the RPA
      Supports external management of its operation by the RP/RPS and RPA
    Neither “end“ of the C2 Link needs to be standardized in SARPs
      The C2 Link is entirely inside the RPAS and does not need to directly connect with other standardized aeronautical systems
    Many technical solutions are possible some already know, some to be discovered
      Currently RPASP WG2 is considering several terrestrial and satellite solutions, including the FSS
      No interoperability between solutions is required
      Compatibility between solutions sharing the same frequency band is required
Graphic from the SARPs

## Slide 5: C2 Link SARPs and Manual - Background
    RPASP WG2 and RTCA have developed the Required Link Performance (RLP) concept for the C2 Link User Data
      Same RLP for all RPAS/C2 Links operating in the same airspace/phase of flight
      All RPAS are equally “safe” irrespective of their design or their C2 Link design
    The C2 Link is Managed by the RP/RPS and RPA
      Currently only how and how well the C2 Link responds to C2 Link Control Data is part of the proposed SARPs and Manual on C2 Links for RPAS
      How the C2 Link itself is managed by the RP/RPS and RPA is outside the scope of the RPASP WG2
        Will be part of the Type Certification of the RPAS
Graphic from the SARPs

## Slide 6: C2 Link SARPs and Manual – RLP Context
    The required performance of a C2 Link is highly dependent on
      The Target Level of Safety in the airspace = RLP
      The phase of flight = RLP
      The pilot activity it is supporting = RLP
      The level of automatic capability in the RPA and RPS = C2 Link Specification
        Too many different levels of RPAS automatic capability to cover in the RLP/SARPs
    The RLP is developed by Aviation Safety Regulators
      The RPAS Designer then specifies the, RPAS design dependent, C2 Link Specification
      The RPAS Operator then contracts, through a Service Level Agreement with the C2CSP, for a QoSR for their planned operation

## Slide 7: C2 Link SARPs – Strategy
    The Annex 10, Volume VI, Part II Systems SARPs
      Contain high level technical requirements that can be applied to any current or future C2 Link technology
        SARPs will not need to change every time the technical solution changes or a new technology is introduced
        SARPs provide a framework for any new technology concept
      SARPs standardize any C2 Link’s
        Performance
          Performance based RLP, high level concept and process, actual values in Manual
        Management
          Performance based, response to commands to Establish/Terminate, Switchover, Handover and Report Status, actual values in Manual
        Compatibility
          Performance based, management of interference and protection of systems, actual values in Manual
        Security
          Performance based security controls, actual values in Manual

## Slide 8: SARPs on C2 Links for RPAS
Foreword
Part I – C2 Link Procedures
  Chapter 1. Definitions
  Chapter 2. Specifications
  Chapter 3. Procedures
Part I I – C2 Link Systems
  Chapter 1 Definitions
  Chapter 2 Systems
  2.1 System description
  2.2 Interfaces
    2.3 Frequency Spectrum
    2.4 System Characteristics
    2.5 User Data Transmission Characteristics
    2.6 C2 Link User Data Performance Requirements
    2.7 C2 Link Control Data Response Characteristics and Performance Requirements
    2.8 Security
    2.9 Records
    2.10 C2 Link Communications Service Providers
Part I SARPs already adopted/effective
WG2 internal review completed Informal and Formal coordination with other Panels underway

## Slide 9: Manual on C2 Links for RPAS - Strategy
    The Manual on C2 Links for RPAS will evolve as ICAO, its member states, and the RPAS industry learn more about the certification and operation of C2 Links
      Regular updates to the Manual on C2 Links for RPAS are anticipated
    The first version of the Manual on C2 Links for RPAS will focus on setting up the foundations and methods that States will use to develop C2CSP certification and management as well as the development of specific RLP types (grouped values of RLP parameters for certain phases of flight and airspaces)
      Chapter 1. Introduction to C2 Links for RPAS
      Chapter 2. The C2 Link Service Provision and Communication Service Providers
      Chapter 3. RLP description, method to develop etc. with worked examples
        RLP values are not currently planned to be in the initial version of the Manual on C2 Links for RPAS, but it is anticipated that they will be added as they become available

## Slide 10: Manual on C2 Links for RPAS - Strategy
    WG2 has a challenge
      Without RLP, it is not possible to assess the suitability of a C2 Link technology
      Without C2 Link technologies it is not possible to gather experience and data to enable RLP to be determined and validated
    The Manual on C2 Links for RPAS will encourage States to contribute to the development of RLP at a national level and then bring their findings to ICAO
    Since specific RLP values are not available currently it is not possible to indicate the suitability of any technical solution in the first version of the Manual on C2 Links for RPAS
    To ensure States do get guidance and work towards international harmonization, the Manual on C2 Links for RPAS will describe the “Candidate” C2 Link technologies that are being considered at this time
    Future versions of the Manual on C2 Links for RPAS will contain RLP values for various airspaces and phases of flight
    Future versions of the the Manual on C2 Links for RPAS will contain suitable C2 Link technologies and the performance they can achieve

## Slide 11: C2 Link SARPs – Next Steps outside the RPASP
1) Panels provide “informal coordination” comments to rapporteurs by February 11th.
2) Rapporteurs prepare proposed “informal coordination” comment resolutions and circulate to WG2 by March 4th.
3) WG2 resolves all “informal coordination” comments prior to or during RPASP 19 by March 25th.
4) Rapporteurs prepare clean version of SARPs text and request WG2 consensus to send the SARPs text to the secretariat by April 15th.
5) ICAO secretariat requests concurrence of the RPASP to conduct the “formal coordination” process by May 2nd.
6) ICAO secretariat starts the “formal coordination” process with Panels by May 16th.
7) Panels provide “formal coordination” comments by July 15th.
8) Rapporteurs and WG2 resolve “formal coordination” comments by September 28th (deadline for papers to WGWHL/2).