## Slide 1
2019 World Radiocommunication Conference Agenda Item 9.1.4
Stations on-Board Sub-Orbital Vehicles
(Spaceplanes)
John Mettrop
UK CAA
ICAO Regional Preparatory Group meeting
Bangkok, Thailand, 27 – 28 March 2017

## Slide 2
resolves to invite the ITU Radiocommunication Sector
  to conduct studies to identify any required technical and operational measures, in relation to stations on board sub-orbital vehicles, that could assist in avoiding harmful interference between radiocommunication services;
  to conduct studies to determine spectrum requirements and, based on the outcome of those studies, to consider a possible future agenda item for WRC‑23;
Agenda Item 9.1.4 – Resolution 763

## Slide 3
decides that the following Questions should be studied
  How will planes be operated including a description of the various phases of flight?
  During which phases of flight described in decides 1, will, if at all, need to be supported by air traffic control systems and what sort of systems are expected?
  What radio links will be required to support planes operations and under what radiocommunication service definition will they fall?
ITU-R Question 259/5

## Slide 4
Space tourism
Satellite Launch
Hypersonic Travel
Space Plane Applications

## Slide 5
Aircraft or Spacecraft?
Aircraft: Any machine that can derive support in the atmosphere from the reactions of the air other that the reactions of the air against the Earth’s surface (ICAO)
spacecraft: A man-made vehicle which is intended to go beyond the major portion of the Earth's atmosphere. (ITU)

## Slide 6
Issues with Respect to Aeronautical Spectrum
45,000 ft
120 km
522 NM
1,544 NM
6,500 km/hr
1,000 km/hr
Height
Radio Horizon
  Link Budget
  Time in Sector
Speed
  Doppler Shift
Incompatible with current planning rules

## Slide 7
Radiocommunication
Mobile Service
Radiodetermination
Amateur
Broadcasting
Fixed
Meteorological aids
Standard frequency & time signal
Mobile-satellite
Radiodetermination-satellite
Amateur
Broadcasting-Satellite
Fixed-Satellite
Earth exploration-satellite
Standard frequency & time signal-satellite
Inter-satellite
Safety
Special
Space research
Radio astronomy
Space operation
Aeronautical mobile
Aeronautical mobile (R)
Aeronautical mobile (OR)
Land mobile
Maritime mobile
Port operations
Ship movement
Radiolocation
Radionavigation
Aeronautical radionavigation
Maritime radionavigation
Meteorological-satellite
Aeronautical mobile-satellite (R)
Aeronautical mobile-satellite
Land mobile-satellite
Maritime mobile-satellite
Radiolocation-satellite
Aeronautical radionavigation-satellite
Maritime radionavigation-satellite
Radionavigation-satellite
Aeronautical mobile-satellite (OR)
What Radio Service?

## Slide 8
Summary
How Much Spectrum is Required?
Which Service?
Sufficient Spectrum Available?
Impact on Existing Aeronautical Services
  Standards
  Planning rules
  Sector Size
Support ICAO/ITU Studies

## Slide 9
Questions