## Slide 1
Radio Interference
John Mettrop
The Invisible Threat

## Slide 2: What do we mean by Interference?
Oxford English Dictionary
  The action or fact of interfering or intermeddling (with a person, etc., or in some action)
  The mutual action of two waves or systems of waves, in reinforcing or neutralizing each other, when their paths meet or cross.
Radio Regulations
  interference: The effect of unwanted energy due to one or a combination of emissions, radiations, or inductions upon reception in a radiocommunication system, manifested by any performance degradation, misinterpretation, or loss of information which could be extracted in the absence of such unwanted energy.
    permissible interference: Observed or predicted interference which complies with quantitative interference and sharing criteria contained in these Regulations or in ITU-R Recommendations or in special agreements as provided for in these Regulations.
    accepted interference: Interference at a higher level than that defined as permissible interference and which has been agreed upon between two or more administrations without prejudice to other administrations.
    harmful interference: Interference which endangers the functioning of a radionavigation service or of other safety services or seriously degrades, obstructs, or repeatedly interrupts a radiocommunication service operating in accordance with Radio Regulations

## Slide 3: Sources of Interference
Interference
Man Made
Natural
Space Weather
Solar Flares
Propagation
Weather
Reflections
Refraction
Obstructions
Intentional
Radiators
Unintentional
Radiators
Microwave ovens
RF Driers
Power line
communication
LED Lighting
Predictable
Unpredictable
New Allocations
Sharing
MoD Jamming
Test & Development
Deliberate
Inadvertent
Jamming
Ignoring Licence
Illegal use
Equipment failure
Equipment
modification
Anti-Tracking
Video
Surveillance
Phone
Jammers

## Slide 4: Factors Affecting Susceptibility to Interference
Power
  Received signal
  Interference source
Receiver Design
  Filtering
  Antenna directivity
Transmitter Spurious Emissions
Separation Distance
Terrain

## Slide 5: How to Interference Detect?
Direction
Finding
Triangulation
Deductive
Reasoning

## Slide 6: Relative Minimum Signal Levels
Grapefruit
Shot
Put
Cricket
Ball
Tennis
ball
Pool
Ball
Marble
Bicycle Wheel
DME
ILS
Marker
ILS
Localiser
ILS
Glideslope
VOR
VHF
Comms
GNSS

## Slide 7: Case Study 1: LED Interference
Scenario:
  Intermittent Interference
  Affected frequencies 119.975, 127.8, 306.2 & 353.5 MHz
  Minimum wanted signal -93dBm
Reason for Interference:
  Microwave site ≈2.5 km away
  LED , florescent tube replacement
Solution:
  Replace light bulb

## Slide 8: Case Study 2: Mobile Phones vs S-Band Radar
Scenario
  2 500 – 2 690 MHz identified for International Mobile Telecommunications in 2007
  2 700 – 2 900 MHz allocated to Aeronautical Radionavigation (Airport Radar)
  2 690 – 2 700 MHz allocated to Radio Astronomy
  2008 Ofcom testing Impact of Radar to Mobile Phones
Reason for Interference:
  Lack of Radar filtering
  Power of the mobile base stations
  Manufacturers lack of regulatory due diligence
Solution:
  Options
    Block implementation of 4G mobile phone deployment
    Procedural approaches only (15 movements/hour)
    Delay implementation of 4G mobile deployment & Modification of the Radar receiver
  Cost £150m
  4 Year programme
Chart: Watchman Susceptibility to Adjacent Band Interference
| 0 | -10 | -12 | -25 | -30 | -45 | -50 | -100 | -150 | -400
 | -79 | -47 | -45 | -45
Chart: Watchman Susceptibility to Adjacent Band Interference
| 0 | -10 | -30 | -45 | -150 | -400
 | 2 | 2 | 2 | 2 | 2

## Slide 9: Case Study 3: Mobile Phones vs Rad Alt
Scenario
  Proposed use of the frequency bands 3 700 – 4 200 & 4 400 – 4 600 MHz by mobile phones
  Radio altimeters operate in the frequency band 4 200 – 4 400 MHz
  Radio altimeter performance defined in M.2059 “ Operational and technical characteristics and protection criteria of radio altimeters….” (2014)
Potential Issue
  Adjacent band interference
  Study based on supplied mobile phone characteristics & M.2059
  Airport protected surfaces

## Slide 10: Case study 3: Results

## Slide 11: Case Study 3: Cause & Implications
Cause
  Radio Altimeter filtering
  Insufficient rejection of adjacent band signals
  Not currently an issue (Satellite downlinks, Point to point radio links)
Implications
  Cannot guarantee signal integrity on approach within 4.5 km of an airport
  Ban mobile use within 4.5 km of an airport
  Preclude Cat II & III landings
  Modification of current Radio Altimeters
  Cost ???
  Risk low

## Slide 12: Case Study 4: GPS
Low level signal (virtually in the noise floor)
Frequencies under military control (Except L5/E5)
Common mode failure point
  Communications
  Navigation
  Surveillance
Potential Threats
  Natural
    Space Weather
    Obstruction
  Man Made
    Adjacent band interference (Ligado USA)
    Deliberate or inadvertent jamming
    Spoofing

## Slide 13: Case Study 4: Who wants to Jam
State sponsored Jamming
  2013 North Korea
    50 Watts
    Disrupted mobile phone network in Seoul 50 miles away
  MoD Jamming trials
Criminal Jamming
  Vehicle & high value asset theft
  Evasion of covert tracking
  Defeating GPS based electronic tags
  Defeating Geo-fencing
Civil Jamming
  Avoidance of fleet tracking
  Commercial advantage
  Unintended consequence of resolving personal aggravation

## Slide 14: Case Study 4: Examples of GPS Jammers
Low Power
Power: 2W
Bands Affected: GPS L1
Price: £38
Medium Power
Power: 5W
Bands Affected: GPS L1-5
3G
GSM
Price: £170
High Power
Power: 12W
Bands Affected: GPS L1-5
3G/4G
GSM/WiMAX
Wifi
Price: £170

## Slide 15: Case Study 4: Personal Aggravation

## Slide 16: Case Study 4: White Van Man Oct 12 – Dec13

## Slide 17: Conclusions
Interference is a real threat
  Need for addition spectrum
  Poor aeronautical receiver design
  Susceptible to adjacent channel interference
CAA Response
  Predictable Interference
    Maintain safety
    Find mitigation solutions
    Economic impact
    Flow rates
  Un-intention/Unpredictable Interference
    Work with Ofcom to
      Trace source
      Resolve
      Avoid in future
    Seek tightening of international standards where appropriate
Probability Low
Impact High

## Slide 18
Questions