## Slide 1: Aircraft Tracking GADSS Update
FSMP
September 2016
Miguel Marin
A/Chief Operational Safety
ICAO
Notes: Notes:
Congratulations, you are now in Module 2a of Amendment 1 to Annex 19.

## Slide 2: Topics

## Slide 3
Normal Aircraft Tracking SL
AN 11/1.1.29-15/12
Aircraft Tracking Normal Operations
Aircraft Tracking Abnormal Operations
Autonomous Distress Tracking
Retrieval of CVR and FDR Data

## Slide 4: Normal Tracking SARPs
Timelines
January 2015
  Preliminary review by ICAO ANC
March 2015
  State Letter
October 2015
  Final review by ICAO ANC
November 2015
  Adopt
March 2017
  Effective
November 2018
  Applicable
Performance-based Standards and recommended practices for normal flight tracking




  No change to ATC procedures
  Not technology-specific
  Establish operator responsibility to track
  Recommendation to track where ATC gets position information at more than every 15 min
    27 000 Kg and more than 19 Seats
  Standard to track in oceanic areas where ATC gets position information at more than every 15 min
    45 500 Kg and more than 19 Seats
  Data retention for last aircraft location purposes


## Slide 5: Graphical Representation
Requirement to track
Recommendation to track at 15 minute intervals
Requirement to track at 15 minute intervals

## Slide 6
Timelines
January 2015
  Preliminary review by ICAO ANC
May 2015
  State Letter
October 2015
  Final review by ICAO ANC
March 2016
  Adopted
July 2016
  Effective
January 2021
  Applicable
Performance-based Standards and recommended practices for distress flight tracking
Distress Tracking SARPs





  Not technology-specific
  Location of an accident site within 6 NM
  Active
    On flight behaviors that can lead to an accident
    Manually from the air
  Power and position information autonomous from other a/c systems
  Applies to new aeroplanes from 2021
  Incentive for early adoption as an alternative to second ELT
Notes: For Distress Tracking, these SARPs:
Will again be not limited to any specific technology
Will help identify the location of an accident site within 6 NM
Will be activated automatically based on flight behaviour, or manually from the air or the ground
Will use technology that have power and position information that are autonomous from other aircraft systems
Will apply to new aeroplans from 2021
Will provide incentive to early adopters by being an alternative to the second ELT
In terms of timelines, the ANC has already conducted its preliminary review back in January, and ICAO will issue a State letter regarding these proposed amendments by April of this year. By next year March, the SARPs will hopefully be adopted, and will then be applicable by January 2021

## Slide 7
DISTRESS TRACKING
 Automatic
 Manual
AUTONOMOUS
RESCUE COORDINATION CENTER
Adopted SARP
Aircraft behavior event that if left uncorrected, can result in an accident.
6 NM
Squawk at
one minute intervals
Notes: Triggers for the transition to autonomous tracking may be activated automatically, manually, or through actions taken on the ground. Trigger examples include Unusual attitudes, speed or acceleration as well as
Failure of aircraft surveillance and tracking systems, Complete Loss of engine power or Alerts such as ground proximity warnings. Under distress tracking, the frequency of position reports increases to approximately 1 minute intervals to ensure that the location of an accident site can be determined to a degree of accuracy within 6 NM.

## Slide 8
  Rescue Coordination Center
  Rescue Coordination Center
DISTRESS TRACKING
AUTONOMOUS
 Automatic
 Manual
Distress Tracking Concept
GADSS CONCEPT
  Mission
  Control
  Center
  Local User Terminal
4D/1 Position information

## Slide 9
  Rescue Coordination Center
  Rescue Coordination Center
DISTRESS TRACKING
AUTONOMOUS
 Automatic
 Manual
Distress Tracking Concept
GADSS CONCEPT
  Mission
  Control
  Center
ATC
Other
Satellites
  Ground
  Station
  Control
  Center
Airline
4D/1 Position information

## Slide 10
Continuous 4D/1 tracking
Abnormal situation .
ADT DATA REPOSITORY
(To be defined)
4D/1 Data
Rescue Coordination Centers RCCs
ADT DATA RETENTION LOCATION AND ACCESS
Potential distress 1
ACCESS TO ADT DATA
Operator retained information2
ADT 4D/1 Data
Notes.
ADT systems may initiate 4D/1 data transmissions prior to the distress conditions specified in ED-237 to ensure compliance with the requirement.
Aircraft tracking data under normal or abnormal conditions is retained by the operator. In the event of an incident or accident, this data may need to be provided to SAR and/or incident/accident investigators. To facilitate the RCC’s access to all aircraft tracking data it should be made available in the ADT Data Repository upon request.
Distress
EUROCAE ED-237
Submit data upon request 2.
SAR assets
6 NM radius

## Slide 11
ACCESS TO ADT DATA
ADT DATA REPOSITORY
4D/1 Data
Rescue Coordination Centers RCCs
ADT DISTRESS ALERTING
Distress
EUROCAE ED-237
Potential distress
ADT alerting process
> Automatic on-board trigger
> Process in place to initiate alert
> Automatic on-board trigger (ELT compatible)
Current alerting process
> ATS
> ELT activated
> Operator
> External source
SAR assets
6 NM radius
ALERT

## Slide 12: What to Expect
GADSS Advisory Group
  Updating the CONOPS
    SL comments and suggestions
    Latest developments in technology
  Identification additional provisions
    Other Annexes
    PANS
  Next version of GADSS (Ver 6.0)
    Expected to be published end of 2016