## Slide 1: Use of the Fixed Satellite Service for RPAS C2 link (ITU Resolution 155 (WRC-15))
Martin WEBER
REGIONAL PREPARATORY GROUP MEETING FOR WRC-19
Bangkok, Thailand

## Slide 2: Overview
Fixed Satellite Service Systems for RPAS
WRC-19 Decision
Safety
Future Work
  in ITU-R
  In ICAO
Notes: RPAS Remotly Piloted Aircrafts Systems
WRC-19 World Radiocommunication Conference 2019
ITU-R Radiocommunications Sector of the International Telecommunications Union

## Slide 3: Fixed Satellite Service Systems for RPAS
a constant Link between Pilot and RPA is needed
  (Idealy 100% of the time)
for long distant flights (over oceans) terrestrial networks are difficult/impossible  Satellite
Space Station
1
2
3
Satellite orbit
4
RPA
Remote Pilot
RPS
LOS
BLOS
LOS – Radio line-of-sight
BLOS – Beyond LOS
VHF - AM
ATC
Notes: RPA - Remote Piloted Aircraft
RPS - Remote Pilot Station

## Slide 4: Fixed Satellite Service Systems for RPAS
Which Radiocommunication Service?
RPA are mobile  Mobile Satellite Service (MSS)
  Problem: MSS systems are designed for shorter communication (phonecalls, time shared data communication) RPAS require a continuous connection between RPS and RPA.
Possible solution:
Fixed Satellite Service (FSS)
  FSS systems are design to give each user a dedicated Channal for permanent use.
    Problem here: FSS communication is restricted to stations at fixed points.
    An exception from this rule has been agreed by a WRC15
Notes: Radiocommunication Service - Term used in the ITU grouping radio stations into categories based on the pupose and natur of the communication

## Slide 5: WRC-19 Decision
Resolution 155 (WRC-15)
Specific Frequency bands may be used for C2 links
Conditions:
  in accordance with SARPs
  fully coordinated Networks/Assingments
  use for RPAS is registered in the ITU Database
  Earth station on board RPA have the same status as ordinary Earth stations
  terrestrial services need to be protected
Notes: Resolution 155(WRC-15)
…
Resolves
1 that assignments to stations of geostationary FSS satellite networks operating in the frequency bands 10.95-11.2 GHz (space-to-Earth), 11.45-11.7 GHz (space-to-Earth), 11.7-12.2 GHz (space-to-Earth) in Region 2, 12.2-12.5 GHz (space-to-Earth) in Region 3, 12.5-12.75 GHz (space-to-Earth) in Regions 1 and 3 and 19.7-20.2 GHz (space-to-Earth), and in the frequency bands 14-14.47 GHz (Earth-to-space) and 29.5-30.0 GHz (Earth-to-space), may be used for UAS CNPC links in non-segregated airspace*, provided that the conditions specified in resolves below are met;

## Slide 6: Safety
In general:
interruption can only be tolerated over short periods of time (max. several seconds)
but no radio system without interference

## Slide 7: Safety
Traditionally:
  Safety Service
    special provisions in the RR
  4.10 special measures to ensure freedom of harmful interference
  15.36/15.37 special treatment of international reports on harmful interference when safety services are affected
  time of solving a case of harmful interference to a safety service is reduce, but still expected to be in the order of up to several days
In case of FSS:
  The overall rules of Article 15 apply
Notes: RR Radio Regulations: Agreement between the ITU Adminstration on a framework on the use of the radio spectrum
RR 4.10 Member States recognize that the safety aspects of radionavigation and other safety services require special measures to ensure their freedom from harmful interference; it is necessary therefore to take this factor into account in the assignment and use of frequencies.
RR 15.36 § 28 When a safety service suffers harmful interference the administration having jurisdiction over the receiving station experiencing the interference may also approach directly the administration having jurisdiction over the interfering station. The same procedure may also be followed in other cases with the prior approval of the administration having jurisdiction over the transmitting station whose service is being interfered with.
RR15.37 § 29 An administration receiving a communication to the effect that one of its stations is causing harmful interference to a safety service shall promptly investigate the matter and take any necessary remedial action and respond in a timely manner. (WRC 2000)

## Slide 8: Safety
How could safety be ensured while using FSS?
robust modulation reducing the required S/N
use of multiple satellites networks on different frequencies
In general the likelihood of “interference” need to be taken into account when the system is designed

## Slide 9: Future Work in ITU
WRC-19
protection of terrestrial services
WRC-23
special coordination rules for Earth stations on-board RPA?
notification of this Earth stations
adaption of Resolution to the results of ICAO’s work on RPAS regulations

## Slide 10: Future Work in ICAO
To help ITU in finding workable solutions
develop performance requirement for C2 Links
develop a better understanding of the operation of C2 Links
In addition a terrestrial component is needed
only the frequency band 5 030 – 5 091 MHz is available
SARPs are needed

## Slide 11: Thank you
Martin WEBER
+49 941 4626 230
Martin.Weber@BNetzA.de

## Slide 12: UA/RPAS BLOS/LOS Funkinfrastruktur
Space Station
1
2
3
Satellite orbit
4
RPA
Remote Pilot
RPS
LOS
BLOS
LOS – Radio line-of-sight
BLOS – Beyond LOS
VHF - AM
ATC