## Slide 1: Aerospace Vehicle Systems Institute Update on AVSI WAIC-Radio Altimeter Coexistence Testing Texas A&M Engineering Experiment Station
Dr. David Redman, AVSI
FOURTH WORKING GROUP MEETING OF THE FREQUENCY SPECTRUM MANAGEMENT PANEL (FSMP – WG/4)
29 March – 7 April 2017 ICAO APAC, Bangkok, Thailand

## Slide 2: Purpose
The AVSI WAIC Team asks the Meeting to consider preliminary testing of radio altimeter susceptibility to WAIC signal interference for the purpose of
Providing an update on the current status of the work supporting the Radar Altimeter and WAIC job cards submitted in February 2016, and
Providing an opportunity for the Meeting to comment on the suitability of the proposed method.

## Slide 3: Outline
A brief history of WAIC at AVSI that leads us to here…
Description of tests investigating WAIC interference on radio altimeters
Future plans for additional testing
This work represents the collective efforts of the entire AVSI WAIC Team.

## Slide 4: The Aerospace Vehicle Systems Institute
AVSI is an industry-centric applied research cooperative founded in 1998 at Texas A&M University that facilitates pre-competitive collaborative research projects (“AFE’s”).

## Slide 5: AVSI Membership Represents the Industry
Full Members
Airbus
Boeing
DoD
Embraer
GE Aviation
Honeywell
Rockwell Collins
Rolls Royce
Saab
Thales
United Technologies
Liaison Members
FAA
NASA
Aerospace Valley
SEI
Associate Members
ATI Wah-Chang
HarcoSemco
Rafael D. S.
SAES-Getters
Lufhansa Technik
Zodiac
Current membership includes a cross-section of aerospace industry stakeholders, including aircraft producers, system suppliers, regulatory bodies, government and trade organizations, and academia.
Past and present WAIC participants in bold

## Slide 6: WAIC Journey
2006
2007
2013
2014
2015
2016
2017
2018
2019
2009
2010
2011
2012
2008
AFE 56
AFE 73 (through s3)
AFE 76
AFE 76s1
First “dedicated” spectrum workshop
First document submission to ITU
First ITU Report on WAIC
Agenda Item
on WAIC
Final ITU Report on WAIC
Protected Spectrum
Approved at WRC-15
RTCA-EUROCAE MOPS Process Initiated
MOPS Process Completed
AFE 14 (2001)
AFE 23 (2003)
ICAO SARP Process
Notes: Pre-History
AFE 14 – completed 2001
Wireless Communication for Aircraft Systems
Focus on:
  Generic characterization of future on-board wireless systems: throughput, latency, data losses, etc
  Prospective suitability of COTS components
Conclusion: “Wireless communication in one form or another may be suitable at least for some aircraft applications”
AFE 23 – completed 2003
Certification Guideline for Wireless Communication in Aircraft
Focus on:
  Installed systems communicating with PEDs but also with other installed wireless
  Non-essential applications, but not excluding higher criticality
Overview of certification processes and issues to be addressed
These two foundational studies prepared the ground for WAIC

## Slide 7: AVSI Testing
New project members in January 2016 expressed strong interest in supporting testing and provided additional resources
Introduction of WAIC-related ICAO FSMP-WG/4 job cards specifically called for analyses proving safe coexistence of WAIC systems and radio altimeters (RA’s) installed on different aircraft and this accelerated the need for supporting experimental date
Initiation of MOPS development activity under the joint RTCA SC-236 / EUROCASE WG-96 committee also added to the urgency to obtain test data to support analysis of single aircraft coexistence

## Slide 8: Coexistence Scenarios with RA’s
Interference between WAIC and RA’s onboard aircraft equipped with WAIC.
Interference between WAIC and RA’s onboard other aircraft within interference range
The latter is expected to arise during flight phases “Standing”, “Pushback/Towing”, “Taxi-Out”, “Take Off”, “Landing” and “Taxi-in”.

## Slide 9: WAIC Roadmap

## Slide 10: WAIC Electronics Test Rack (WETR)

## Slide 11: Laboratory Testing
Vector Signal Generator
Spectrum Analyzer
RA #1
Fiber Optic Delay Line
RA #2
RA #3
Tx
Tx
Tx
Rx
Rx
Rx
16 dB Directional Couple
ARINC
429
GPIB
Flight
Test
Rack

## Slide 12: Radio Altimeters Used for Testing
Rockwell Collins LRA-2100 | 
Dimensions | L = 15.6”, W = 3.64”, H = 7.7”
Weight | 8.47 lb nominal (8.8 lb max.)
Input Power | 115 V AC ±10%, 360 to 800 Hz
Mounting | ARINC 600
Software | DO-178A
Rockwell Collins LRA-900 | 
Dimensions | L = 15.6”, W = 3.64”, H = 7.7”
Weight | 9.6 lbs
Input Power | 115 V AC ±10%, 380 to 420 Hz
Mounting | ARINC 600
Software | DO-178A
Thales ERT-530 | 
Dimensions | L = 15.6”, W = 3.64”, H = 7.7”
Weight | 8.47 lb nominal (8.8 lb max.)
Input Power | 115 V AC ±10%, 360 to 800 Hz
Accuracy | 1 ft over runway surface
Thales ERT-530 | 
Dimensions | L = 15.6”, W = 3.64”, H = 7.7”
Weight | 9.6 lbs
Input Power | 115 V AC ±10%, 380 to 420 Hz
Mounting | ARINC 600
Honeywell ALA-52B | 
Dimensions | L = 15.6”, W = 3.64”, H = 7.7”
Weight | 8.6 lb
Input Power | +28 VDC
Mounting | ARINC 600
Software | DO-178B, LA
(1)
(2)
(3)
(4)
(5)

## Slide 13: Radio Altimeter Test Scenarios
For constant AGL: Record the effect of WAIC interference on each of 5 RadAlts at 5 altitudes.
  4 waveform types will be evaluated:
    2 Constant Envelope Signals (MSK)
    2 Orthogonal Frequency Division Multiplexing Signals (OFDM)
  Waveform transmit power will be increased in 15 (1dB) steps with signal power ON and OFF (to measure true altitude) for each step.
  Specific events to be noted:
    First instance of radio altimeter output to differ between the ON and OFF state.
    Altimeter accuracy just meets DO-155 specification for that altitude.
    Altimeter loses lock (Null Acquisition Mode)

## Slide 14: Testing Scenarios
Height |  | WAIC Waveforms |  |  |  |  |  |  |  |  |  |  | 
 |  | Single Carrier |  |  | Dual Carrier MSK |  |  | Single Channel OFDM |  |  | Dual Channel OFDM |  | 
 |  | 4.3 GHz | 4.24 GHz | 4.36 GHz | 4.3 GHz | 4.24 GHz | 4.36 GHz | 4.3 GHz | 4.24 GHz | 4.36 GHz | 4.3 GHz | 4.24 GHz | 4.36 GHz
500 ft. | Threshold |  |  |  |  |  |  |  |  |  |  |  | 
 | Out of Spec |  |  |  |  |  |  |  |  |  |  |  | 
 | Loss of Lock |  |  |  |  |  |  |  |  |  |  |  | 
1500 ft. | Threshold |  |  |  |  |  |  |  |  |  |  |  | 
 | Out of Spec |  |  |  |  |  |  |  |  |  |  |  | 
 | Loss of Lock |  |  |  |  |  |  |  |  |  |  |  | 
3000 ft. | Threshold |  |  |  |  |  |  |  |  |  |  |  | 
 | Out of Spec |  |  |  |  |  |  |  |  |  |  |  | 
 | Loss of Lock |  |  |  |  |  |  |  |  |  |  |  | 
5000 ft. | Threshold |  |  |  |  |  |  |  |  |  |  |  | 
 | Out of Spec |  |  |  |  |  |  |  |  |  |  |  | 
 | Loss of Lock |  |  |  |  |  |  |  |  |  |  |  | 
8000 ft. | Threshold |  |  |  |  |  |  |  |  |  |  |  | 
 | Out of Spec |  |  |  |  |  |  |  |  |  |  |  | 
 | Loss of Lock |  |  |  |  |  |  |  |  |  |  |  | 
Per RA Model

## Slide 15: Signal Generation for Injection
MATLAB OFDM and MSK simulated baseband signals loaded into vector signal generator.
OFDM based on the IEEE 802.11 parameters; 52 subcarriers, 312.5 kHz carrier separation, 20 MHz bandwidth and 16 MHz occupied bandwidth, 20 Msps (3.2 µs data symbol duration with a 0.4 µs guard length).
Center frequencies – Center of band, 4.3 GHz, +/- 60 MHz
OFDM
Dual Channel OFDM
Dual MSK
Notes: Two MSK signals at 5 MHz apart (+/- 2.5 MHz offsets from center), each with 2 Msymbol/s. MSK, continuous phase frequency shift keying
OFDM signals (exact same signal) 20 MHz apart (+/-10 MHz offsets). Each signal should have about 16-17 MHz bandwidth. The VSG power setting is -30 dBm. The peak SA’s readings are much lower as shown due to the low resolution bandwidth setting. I think the total integrated power should be -30 dBm. Also, if there is only signal, the peaks are higher than with two signals.

## Slide 16: Data Collection Automation
For each 1 of 5 altitudes
  For each 1 of 5 test altimeters
      Manually select RA under test
      For each 1 of 4 waveforms
        Load/Select VSG Waveform
        For each 1 of 15 power levels
          Read & record altitude without interference power for 10 seconds
          Turn on interference signal
          Read and record altitude with selected int. power for 10 seconds
          Turn off interference signal
The same control and data acquisition software will be used in both the laboratory and in planned flight testing to step through a full set of measurements with minimal operator interaction

## Slide 17: Flight Testing Overview
Flight Test Objectives
  Validate the laboratory test apparatus and method.
  Analyze the the effects of terrain on WAIC/RA interference characteristics
  Provide real-world data supporting development of standards under ICAO and RTCA.
  Provide real-world data supporting development of WAIC technical characteristics, including waveform modulations, protocols and con-ops, being developed under an AVSI project.
Two Flight Test Campaigns
  Phase 1: Direct injection of representative WAIC signals into RadAlt receive antenna. (WAIC on RA)
  Phase 2: Distributive representative WAIC transmitters about the aircraft. (RA on WAIC / WAIC on WAIC)
Note: Additional RadAlt ground scattering tests are also in preparation

## Slide 18: Flight Test Aircraft: Gulfstream G3
Business jet developed by Gulfstream Aerospace.
Equipped with 2 Radio Altimeters.
  Primary  Thales ERT-530A
  Secondary  Thales ERT-530A
https://www.nasa.gov/centers/armstrong/multimedia/imagegallery/G-III_Aerodynamics/index.html
Notes: Antenna 9.5 dBi gain

## Slide 19: Gulfstream 3 – Tail #808 Floor Plan
15” 37” 26”
78”
Gulfstream 3 Floor Plan with WAIC Test Rack.
WAIC Test Rack replaces aircraft seat on the starboard side.
RadAlt #2 disconnected, antennas used with WAIC test rack.

## Slide 20: Flight Test Profile
Start
Fly to start point: Set altimeter 1, waveform 1 ~15 minutes
Each Altitude:
  Altimeter 1
    For 4 Waveforms: (1.5 minutes*4) + (10 sec. waveform switch*3) = 6.5 Min.
    Turn, switch to waveform 1, switch to altimeter 2 = 3 Min.
  Altimeter 2
    For 4 Waveforms: (1.5 minutes*4) + (10 sec. waveform switch*3) = 6.5 Min.
    Turn, switch to waveform 1, switch to altimeter 2 = 3 Min.
  Altimeter 3
    For 4 Waveforms: (1.5 minutes*4) + (10 sec. waveform switch*3) = 6.5 Min.
    Turn + Descend, switch to waveform 1, switch to altimeter 2 = 3 Min.
  Total Time Per Altitude: 28.5 Min.
3 Altimeters over 5 Altitudes: 28.5 Min. x 5 altitudes = 142.5 Min.
Fly and settle to approach #1 position: ~10 Min.
Touch and go's (500 ft AGL): 10 minutes each x 3 = 30 Min.
Total time, 3 altimeters: 142.5 + 10 + 30 = 182.5 Min.
End

## Slide 21: Flight Test Area
R-2515, CORDS Road, north of Edwards Air Force Base.
40 NM legs, 3 NM either side of the center line.
  13.33 minute legs at 180 knots, 16.55 minute legs at 145 knots.
  3 minute turns for “dog-bone” flight path.
15 minutes flight to start point.

## Slide 22: Flight Test Profile

## Slide 23: Conclusions
Preliminary laboratory testing has begun at AVSI to characterize the interference of candidate WAIC signals on commercial radio altimeters.
This data, validated by planned flight testing, is critical to the development of the WAIC SARP
The AVSI WAIC team invites the ICAO FSMP – WG/4 to consider the suitability of the experimental method to develop an acceptable SARP.

## Slide 24: Comments?
Questions?
Dave Redman
  dredman@avsi.aero
  979-218-2272