## Slide 1: Interference Susceptibility Evaluations of Pulsed Radio Altimeters Due to 5G Mobile Base Station Signal
National Institute of Maritime, Port and Aviation Technology Electronic Navigation Research Institute
ICAO Frequency Spectrum Management Panel (FSMP) 12th Working Group Meeting, Virtual Meeting, October 2021 – IP/07
Electronic Navigation Research Institute
S. Futatsumori

## Slide 2: Contents
Summary
Interference test parameters
Interference test results of two pulsed radio altimeters due to 5G mobile base station signal
Interference test results
Out-band interference
Interference signal frequency conditions
In-band interference
Overview of the test set-up
Example of recorded data

## Slide 3: Interference susceptibility test
Summary
  The interference susceptibility of two pulsed radio altimeters with the same product number (PN) is investigated using DO-155 test protocols.
  The in-band and out-band interference signal are additive white Gaussian noise (AWGN) and 5G base station test signals, respectively.
Objectives
  The repeatability of the Japanese MIC test results is assessed. Furthermore, the interference susceptibility fluctuation of the identical PN radio altimeters is measured.
Radio altimeters for the test
  A pulsed radio altimeter identical to the one stated in the Japanese MIC test report (same serial number).
  For a pulsed radio altimeter, use the same PN as above.

## Slide 4: Test parameters
 | Parameters
Pulse radio altimeter for test | RT-300 (7001840-913, SN98056822, No. 1) RT-300 (7001840-913, SN90013302, No. 2)
Altitude (ft) | 50, 100, 500, 1000, 1500 (MIC test results: 50, 100, 500)
Interference signal | AWGN (In-band) 5GNR signal NR-FR1-TM1.1 (Out-band)
Interference signal bandwidth (MHz) | 200 (In-band) 100 x 2 (Out-band, both side) 100 (Out-band, single side)
Interference signal power | −130 dBm/MHz− −45 dBm/MHz (In-band) −80 dBm − −10 dBm (Out-band)
Interference signal power sweep step (dB) | 10 for the initial sweep, 1 for the detailed sweep
Interference signal configurations | 4.2 GHz−4.4 GHz (In-band) 4.0 GHz−4.1 GHz and 4.5 GHz−4.6 GHz (Out-band, guard band 100 MHz, both side) 4.0 GHz−4.1 GHz (Out-band, guard band 100 MHz, lower side band) 4.5 GHz−4.6 GHz (Out-band, guard band 100 MHz, upper side band) 3.9 GHz−4.0 GHz and 4.6 GHz−4.7 GHz (Out-band, guard band 200 MHz, both side) 3.8 GHz−3.9 GHz and 4.7 GHz−4.8 GHz (Out-band, guard band 300 MHz, both side)
Interference signal injection time | 10 s on, 10 s off
Band stop filter for RA band | ×(In-band) ○(Out-band)
Interference criteria | Altitude error exceed 0.5 % (cross-check for RTCA report) Altitude error exceed 2 % (cross-check for MIC report)

## Slide 5: Interference signal frequency configurations
4.2
4.4
RA band
AWGN
4.2
4.4
RA band
5GNR
5GNR
4.05
4.55
Guardband: 100MHz
4.2
4.4
RA band
5GNR
4.05
Guardband: 100MHz
4.2
4.4
RA band
5GNR
4.05
4.55
Guardband: 100MHz
4.2
4.4
RA band
5GNR
5GNR
3.95
4.65
Guardband: 200MHz
4.2
4.4
RA band
5GNR
5GNR
3.85
4.75
Guardband: 300MHz
Inband
(AWGN Bandwidth 200 MHz)
Outband
(5GNR Bandwidth 100 MHz)
(Guardband 100 MHz)
Outband
(5GNR Bandwidth 100 MHz)
(Guardband 200 MHz)
Outband
(5GNR Bandwidth 100 MHz)
(Guardband 300 MHz)
BW100 MHz on both side
BW100 MHz on both side
BW100 MHz on both side
BW100 MHz on LSB
BW100 MHz on USB

## Slide 6: Pulsed radio altimeter
RT-300(Model: 7001840-913)
RT-300 No.1
(SN: 98056822)
RT-300 No.2
(SN: 90013302)

## Slide 7: Block diagram
Anritsu MG3710E
Radio
altimeter
Step Attenuator
3 dB hybrid
Fixed Attenuator
Delay line
Signal generator
Keysight Technologies N9918B
Band stop filter
TX port
Precision out
20 dB
0 – 110 dB
Isolator
In-band test
Isolator
Isolator
Interference signal path
50, 100, 500, 1000, 1500 ft
3 dB hybrid
RX port
NI USB-6212
Experimental set-up based on DO-155 test procedures
Spectrum analyzer
Digitizer
Computer
Dual channel signal output
(Maximum bandwidth: 120 MHz for each channel)

## Slide 8: Overview of the set-up
Spectrum analyzer
(Recorded)
Dual channel Signal generator
Band stop filter for inband test
Delay line
Radio altimeter
Data recorder

## Slide 9: Example of the recorded data
Inband, AWGN 200 MHz bandwidth (4.2 GHz-4.4 GHz)
The altitude output voltage is measured and recorded using the digitizer.
Each data points stands for an average of 1000 pts of 10 kS/s

## Slide 10: In-band interference: Results
Criteria/Altitude | 50 ft | 100 ft | 500 ft | 1000 ft | 1500 ft
RT-300 No. 1 (7001840-913 SN98056822) | −77.8 | −80.8 | −82.8 | −85.8 | −86.8
RT-300 No. 2 (7001840-913 SN90013302) | −79.8 | −83.8 | −83.8 | −92.8 | −86.8
Interference power exceed 0.5 % error (dBm/MHz)
Criteria/Altitude | 50 ft | 100 ft | 500 ft | 1000 ft | 1500 ft
RT-300 No. 1 (7001840-913 SN98056822) | −72.8 | −73.8 | −78.8 | −84.8 | −86.8
RT-300 No. 2 (7001840-913 SN90013302) | −72.8 | −77.8 | −78.8 | −86.8 | −85.8
RT-300 No. 1 (7001840-913 SN98056822) (MIC report) | −70 | −70 | −76 | - | -
Interference power exceed 2 % error (dBm/MHz)
4.2
4.4
RA band
AWGN
AWGN 200 MHz bandwidth (4.2 GHz-4.4 GHz)
The maximum variation of interference threshold power is less than 7 dB.
The maximum difference between MIC report is 4 dB for RT-300 No. 1.

## Slide 11: Out-band interference: Results 1
Criteria/Altitude | 50 ft | 100 ft | 500 ft | 1000 ft | 1500 ft
RT-300 No. 1 (7001840-913 SN98056822) | −45.0 | −50.0 | −51.0 | −59.0 | −55.0
RT-300 No. 2 (7001840-913 SN90013302) | −35.0 | −39.0 | −42.0 | −47.0 | −46.0
Interference power exceed 0.5 % error (dBm/MHz)
Criteria/Altitude | 50 ft | 100 ft | 500 ft | 1000 ft | 1500 ft
RT-300 No. 1 (7001840-913 SN98056822) | −41.0 | −46.0 | −49.0 | −53.0 | −54.0
RT-300 No. 2 (7001840-913 SN90013302) | −31.0 | −36.0 | −39.0 | −45.0 | −45.0
RT-300 No. 1 (7001840-913 SN98056822) (MIC report) | −32 | −34 | −45 | - | -
Interference power exceed 2 % error (dBm/MHz)
5GNR 100 MHz+100 MHz bandwidth (Guardband 100 MHz)
4.2
4.4
RA band
5GNR
5GNR
4.05
4.55
Guardband: 100MHz
The maximum variation of interference threshold power is more than 10 dB. The maximum difference between MIC report is 12 dB for RT-300 No. 1.

## Slide 12: Out-band interference: Results 2
Criteria/Altitude | 50 ft | 100 ft | 500 ft | 1000 ft | 1500 ft
RT-300 No. 1 (7001840-913 SN98056822) | −47.7 | −52.7 | −53.7 | −57.7 | −57.7
RT-300 No. 2 (7001840-913 SN90013302) | −38.7 | −41.7 | −44.7 | −49.7 | −50.7
Interference power exceed 0.5 % error (dBm/MHz)
Criteria/Altitude | 50 ft | 100 ft | 500 ft | 1000 ft | 1500 ft
RT-300 No. 1 (7001840-913 SN98056822) | −43.7 | −48.7 | −50.7 | −55.7 | −57.7
RT-300 No. 2 (7001840-913 SN90013302) | −34.7 | −38.7 | −41.7 | −47.7 | −49.7
RT-300 No. 1 (7001840-913 SN98056822) (MIC report) | - | - | - | - | -
Interference power exceed 2 % error (dBm/MHz)
5GNR 100 MHz bandwidth LSB (Guardband 100 MHz)
4.2
4.4
RA band
5GNR
4.05
Guardband: 100MHz
The maximum variation of interference threshold values is more than 10 dB. The −57.7 dBm threshold is observed at 1500 ft due to the signal on LSB.

## Slide 13: Out-band interference: Results 3
Criteria/Altitude | 50 ft | 100 ft | 500 ft | 1000 ft | 1500 ft
RT-300 No. 1 (7001840-913 SN98056822) | −28.4 | −31.4 | −30.4 | −32.4 | −32.4
RT-300 No. 2 (7001840-913 SN90013302) | −24.4 | −26.4 | −27.4 | −31.4 | −31.4
Interference power exceed 0.5 % error (dBm/MHz)
Criteria/Altitude | 50 ft | 100 ft | 500 ft | 1000 ft | 1500 ft
RT-300 No. 1 (7001840-913 SN98056822) | −23.4 | −27.4 | −27.4 | −29.4 | −30.4
RT-300 No. 2 (7001840-913 SN90013302) | −20.4 | −23.4 | −24.4 | −29.4 | −31.4
RT-300 No. 1 (7001840-913 SN98056822) (MIC report) | - | - | - | - | -
Interference power exceed 2 % error (dBm/MHz)
5GNR 100 MHz bandwidth USB (Guardband 100 MHz)
4.2
4.4
RA band
5GNR
4.05
4.55
Guardband: 100MHz
The USB interference threshold values are almost 20 dB higher than those of LSB interference values. The variations are small values compared with LSB.

## Slide 14: Out-band interference: Results 4
Criteria/Altitude | 50 ft | 100 ft | 500 ft | 1000 ft | 1500 ft
RT-300 No. 1 (7001840-913 SN98056822) | −36.0 | −41.0 | −40.0 | −45.0 | −42.0
RT-300 No. 2 (7001840-913 SN90013302) | −23.0 | −25.0 | −26.0 | −29.0 | −28.0
Interference power exceed 0.5 % error (dBm/MHz)
Criteria/Altitude | 50 ft | 100 ft | 500 ft | 1000 ft | 1500 ft
RT-300 No. 1 (7001840-913 SN98056822) | −32.0 | −37.0 | −37.0 | −40.0 | −41.0
RT-300 No. 2 (7001840-913 SN90013302) | −19.0 | −22.0 | −23.0 | −27.0 | −28.0
RT-300 No. 1 (7001840-913 SN98056822) (MIC report) | −24 | −27 | −34 | - | -
Interference power exceed 2 % error (dBm/MHz)
5GNR 100 MHz+100 MHz bandwidth (Guardband 200 MHz)
The maximum variation of interference threshold values is more than 10 dB. The maximum difference between MIC report is 10 dB for RT-300 No. 1.
4.2
4.4
RA band
5GNR
5GNR
3.95
4.65
Guardband: 200MHz

## Slide 15: Out-band interference: Results 5
Criteria/Altitude | 50 ft | 100 ft | 500 ft | 1000 ft | 1500 ft
RT-300 No. 1 (7001840-913 SN98056822) | −29.0 | −31.0 | −30.0 | −32.0 | −34.0
RT-300 No. 2 (7001840-913 SN90013302) | N/A | N/A | -16.0 | −20.0 | −20.0
Interference power exceed 0.5 % error (dBm/MHz)
Criteria/Altitude | 50 ft | 100 ft | 500 ft | 1000 ft | 1500 ft
RT-300 No. 1 (7001840-913 SN98056822) | N/A | −21.0 | −29.0 | −31.0 | −32.0
RT-300 No. 2 (7001840-913 SN90013302) | N/A | N/A | -14.0 | −18.0 | −20.0
RT-300 No. 1 (7001840-913 SN98056822) (MIC report) | N/A | N/A | -27 | - | -
Interference power exceed 2 % error (dBm/MHz)
5GNR 100 MHz+100 MHz bandwidth (Guardband 300 MHz)
The maximum variation of interference threshold values is more than 10 dB. The difference between MIC report is observed for RT-300 No. 1.
4.2
4.4
RA band
5GNR
5GNR
3.85
4.75
Guardband: 300MHz

## Slide 16: Conclusions
The repeatability of the MIC report is evaluated by using the same radio altimeter. The threshold power is almost within 4 dB difference.
Conclusions
Future works
The interference threshold due to the 5G mobile base station is evaluated for two pulsed altimeters.
The variations of the interference threshold power is more than 10 dB at the same test conditions for the same PN radio altimeter.
We will take more measurements with the various PN pulsed radio altimeters as well as several FMCW radio altimeters.
The interference threshold power is reduced as the altitude is getting higher. The maximum measurement altitude is 1500 ft.
The minimum interference threshold values for the in-band and the out-band interference test are −57.7 dBm and −86.8 dBm/MHz, respectively