FREQUENCY SPECTRUM MANAGEMENT PANEL (FSMP)

Eleventh Working Group meeting

Web Meeting, 1 – 12 March 2021

Agenda Item 4:	Development of (planned) Material for ITU-R Studies on

a)	WRC-23 AI1.6 Suborbital Vehicles

Consideration of the use of MSS Frequency Bands at 1.6/1.5 GHz
to Support Communications for Sub-Orbital Vehicles

(Presented by Kamlesh Masrani, Inmarsat)

SUMMARY

This paper provides information on the benefits that may be gained in identifying MSS systems operating in the 1.6/1.5 GHz frequency bands to support safety and non-safety related voice and data communications (including the transmission of flight tracking data and other aeronautical telemetry information) by stations on sub-orbital vehicles (SoV) when they are operating their flight paths in space. Such provisions would complement the use of MSS by stations on SoV when operating their flight paths within the Earth’s atmosphere. The ICAO FSMP-WG/11 meeting is invited to review the proposals contained in this paper and to take them into account, as appropriate, in the development of any ITU-R studies on WRC-23 Agenda Item 1.6 within FSMP, and in any future update to the draft ICAO position for WRC-23. FSMP is also invited to provide comments on the proposals that may assist in progressing the discussions at WP 5B in identifying the radio communication services that may suitable for use by stations on sub-orbital vehicles.

INTRODUCTION

Inmarsat proposes the use of GSO MSS systems operating in the frequency bands: 1 518-1 544 & 1 545-1 559 MHz; 1 626.5-1 645.5 & 1 646.5-1 660.5 MHz; 1 670-1 675 MHz, be identified as one of the candidate radiocommunication services that may be used to support radiocommunications by stations to sub-orbital vehicles (SoV) during periods of their flight in space.   In making this proposal, Inmarsat recognises that other MSS systems operating in other parts of L-band also provide safety and non-safety related aeronautical communication services and may additionally be identified as candidate radiocommunication services for SoV communications.  It is also understood the operation of MSS systems on SoV is permissible under No. 1.63 and other RR provisions during periods of SoV flight within major portions of the Earth’s atmosphere.

DISCUSSION

Inmarsat submitted an input contribution to the February 2020 meeting of WP 4C (Document 4C/157) proposing the identification of the mobile-satellite service (MSS) as a potential candidate radiocommunication technology that may assist in the provision of safety and non-safety related voice and data communications by stations on sub-orbital vehicles.

In the WP 4C input contribution, Inmarsat noted that aeronautical MSS systems are routinely used to support safety and non-safety related radio communications to aircraft, particularly over remote and oceanic regions of the Earth, and thereby could be suitable for use for use on SoV when operating within the Earth’s atmosphere.

An extension in the operation of such aeronautical MSS systems on SoV to address cases when a SoV is operating in regions of near-Earth space is considered to be practicable, both from a technological and MSS satellite coverage perspective.

Inmarsat also considers the use of existing aeronautical MSS technology providing aviation messaging for Air Traffic Services and Emergency communications (via the ACARS and FANS 1/A) may also be suitable (with appropriate development and compliance with revised performance requirements) for use by stations on sub-orbital vehicles.

Inmarsat takes note of the text in the current draft ICAO position for ITU WRC-23 on Agenda Item 1.6, and particularly on the comment that the “introduction of sub-orbital vehicles will create numerous challenges for spectrum usage and frequency management”.

Comments are welcome from FSMP members on the various proposals that were contained in Inmarsat’s WP 4C contribution.  From brevity, these proposals are not repeated here but are listed in bullet points 1 to 6 in the Background Section of the WP 4C contribution.

During the WP 4C discussions comments made on aspects of the proposals including:

- there may be no need to identify any new category of MSS earth station class for operation on SoV, as the existing class identification may be sufficient to identify the frequency coordination requirements with other services and other MSS satellite networks;

- Similarly, there may be no need to identify any specific telemetry and telecommand service operation, as aeronautical telemetry data may be conveyed over MSS channels, following current practices in use of the MSS to support aeronautical telemetry; and

- to remove identification of the frequency band 1 668-1 670 MHz as a candidate frequency range, as it overlaps Radio Astronomy Service use and co-frequency sharing is likely to difficult under radio line-of-sight conditions.

WP 4C recommended Inmarsat re-submit the proposal to WP 5B for further discussion.

CONCLUSION

FSMP-WG/11 is invited to review and note the contents of this information paper.

Inmarsat plans to submit a revision of the attached WP 4C paper to WP 5B taking into account the comments made at WP 4C (listed in paragraph 2.7 above).

FSMP members are invited to provide any further comments on the proposals (looking to identify use of the MSS as a candidate radiocommunication service for use by stations on SoV) and which may assist in the on-going discussions at WP 5B on WRC-23 Agenda Item 1.6.

Attachment: 1

— END —