FREQUENCY SPECTRUM MANGEMENT PANEL (FSMP)

ELEVENTH MEETING

E-Meeting, 1 to 12 March 2021

Agenda Item 3c :	National efforts to implement broadband mobile near 4200-4400 MHz

Status on replanning the 3700–4200 MHz band in Australia

(Presented by Eddy D’Amico)

SUMMARY

The ACMA recently released an outcomes paper in response to submissions received to the July 2020 consultation looking at options to introduce wireless broadband in the 3700-4200 MHz band in Australia. The paper details outcomes of the review of the band, including the planning of wireless broadband up to 4000 MHz, and signals the progression of the 3700-4200 MHz band to the ‘implementation’ phase. The ACMA will convene a Technical Liaison Group in Q2 2021 to gather input into the technical frameworks for both spectrum licensed and apparatus licensed segments of the 3700-4200 MHz band to ensure an adequate level of protection to aeronautical systems and consider any necessary mitigations.

INTRODUCTION

In July 2020 the Australian spectrum regulator (the ACMA) released a consultation looking at options to introduce wireless broadband (WBB) in the 3700-4200 MHz band. The consultation closed in September 2020 and Airservices, along with 20 other stakeholders including Boeing Australia, provided submissions to the consultation. In January 2021 the ACMA released the Replanning the 3700–4200 MHz band: Outcomes paper describing the outcomes of the review of the band and detailing the way ahead.

DISCUSSION

The ACMA released an initial consultation in September 2019 on possible replanning of the 3700-4200 MHz band. Airservices responded to the initial consultation advising that any replanning must consider any potential impact on the safety critical radio altimeter (RA) and future wireless avionics intra-communication (WAIC) systems that operate in the neighbouring band. In July 2020 the ACMA released a further consultation looking at options to introduce WBB in the 3700-4200 MHz band (refer to document WG/10-IP03). The options consultation included a compatibility study between WBB and RA to show how WBB and RA can coexist in adjacent bands. The consultation considered three planning options, with each option providing a 200/300 MHz guard band between WBB and RA.

Airservices responded to the options consultation focusing on the compatibility studies between WBB systems in the 3700-4200 MHz band and RA systems operating in the adjacent band 4200-4400 MHz. Airservices preferred planning Option 3 with a frequency segment breakpoint at 3900 MHz. This option and segment breakpoint allowed for: 1) wide area (WA) WBB (i.e. mobile telecommunications) deployments in metropolitan and regional areas and local area (LA) WBB (i.e. internet service providers) deployments in rural areas in the band 3700-3800 MHz; and 2) LA WBB in the band 3800-3900 MHz Australia-wide. Airservices suggested that the frequency segment breakpoint could be reviewed once international compatibility studies between WBB and RA were agreed. Airservices also informed the ACMA about the work happening internationally and provided a copy of the RTCA Special Committee 239 (SC-239) report that concluded there’s a major risk that 5G systems in the 3600-3980 MHz band will cause harmful interference to RA on all types of civil aircraft.

In January 2021 the ACMA released the Replanning the 3700–4200 MHz band: Outcomes paper detailing the outcomes of the review of the band, and signalling the progression of the 3700–4200 MHz band to the ‘implementation’ phase under ACMA’s spectrum planning process. The ACMA has decided to implement Option 3 with a frequency segment breakpoint at 4000 MHz (i.e. WA WBB in metropolitan and regional areas and LA WBB in rural areas in the band 3700-3800 MHz, and LA WBB in the band 3800-4000 MHz Australia wide). Key outcomes of the planning process include: 1) introducing arrangements for WA WBB in 3700-3800 MHz in metropolitan and regional areas on an exclusive basis; and 2) introducing arrangements for LA WBB in 3700-3800 MHz in remote areas, and in 3800-4000 MHz Australia-wide on a shared basis with existing fixed satellite service and fixed point-to-point service.

As indicated on page 13 of the Outcomes paper, the ACMA acknowledged the RTCA SC-239 5G Report but view the report as conservative and consider that compatibility with RA can be successfully managed with WBB services introduced up to 4000 MHz. The ACMA made the following observations about the RTCA report: 1) the Interference Tolerance Masks (ITM) determined in the RTCA analysis uses a minimum ground reflectivity of 0.01, whereas the ACMA study used 3.16 based on representative conditions in Australia (a 25 dB difference); 2) the ITMs used the most conservative of each parameter from any of the set of RAs identified as being applicable for each specific scenario being analysed; 3) an extra margin of 6 dB is used in the RA laboratory tests to develop the ITMs, rather than testing multiple samples of each RA to obtain a parameter distribution; and 4) an additional 6 dB ‘aviation safety margin’ is also presented in the results, even though its application depends on the determined safety criticality of each analysed scenario.

The ACMA have indicated that it will work cooperatively with the aviation industry to develop technical frameworks for both spectrum licensed and apparatus licensed segments of the 3700-4200 MHz band to ensure an adequate level of protection and to consider any necessary mitigations, such as in-band or out-of-band emission limits and/or exclusion areas around aerodromes or identified heliports. The ACMA will convene a Technical Liaison Group (TLG) in Q2 2021 to gather input into the technical frameworks. Key to the success of this TLG will be the involvement of the aviation sector to be able to provide informed advice and views on how to manage the potential interference from WBB services to RA and WAIC in the adjacent 4200-4400 MHz band. It is expected that Boeing Australia, Virgin Australia, Qantas, CASA and Airservices will all be members of the TLG.

ACTION BY THE MEETING

The meeting is invited to:

note and review the contents of this working paper; and

provide material to support aviation efforts in the TLG activities in determining the technical framework for both spectrum licensed and apparatus licensed segments of the 3700–4200 MHz band to ensure RA is protected, and any mitigation necessary.

— END —

# Footnotes

Planning options for the 3700–4200 MHz band - consultation 22/2020 | ACMA