## Slide 1: Simplified explanation of II/SI code operations
Prepared for ICAO APAC Mode S and DAPS WG/6
28-30 March 2023
By HO Wee Sin
Civil Aviation Authority of Singapore

## Slide 2: Working principles of radar
Primary radar only provides position of aircraft
Secondary (mode A/C) radar provides the Mode A (i.e. ident code) and Mode C (barometric height), plus position
Secondary (mode S) radar provides other information (e.g. unique 24-bit Aircraft address, call-sign, vertical intent etc), plus what mode A/C radar can provide.
  Note that mode A/C is mandatory but not mode S
Pulse sent out
Pulse reflected
Radar measures position of aircraft
Interrogation (mode A or Mode C)
Transponder replies with height and identity (mode A), with other information
Primary radar
Secondary radar (Mode A/C)
*4096 mode A codes available
Secondary radar (Mode S)
Interrogation (all-call or roll-call)
Mode A (ident) and Mode C (height)

## Slide 3: Broad principle for mode S
Interrogation | Reply | Remark
All-call | 24-bit Aircraft address | Only non-locked out aircraft will reply
Roll-call (to only selected aircraft) | Aircraft address + height / Mode A with: Elementary Mode S Datalink capability report; Flight ID (aka call-sign); TCAS resolution advisory report; Enhanced Mode S Selected vertical intention; Track and turn; Heading and speed; | Only target aircraft will reply.
Interrogation (all-call or roll-call)
Appropriate reply
For purpose of locking out to all-call, each radar has its own identifier code (IC). Old scheme is the interrogator identifier (II) (15 combination). New scheme is the surveillance identifier (SI) (63 combination). Not all aircraft can recognize the SI code.

## Slide 4: Radar identifiers
II=1
II=2
II=3
II=4
II=5
II=6
II=7
II codes can be used if not too many overlapping radars
SI codes has to be used if too many overlapping radars

## Slide 5: All-call
24 bit aircraft address = 76ABCD
Locked out to II = 4, 7
Locked out to SI =21, 22
Radar with II=7
24 bit aircraft address = 34ABCE
Locked out to II = 4
Locked out to SI =21, 22
All call interrogation
All call interrogation
No reply to all call interrogation from radar with II=7
Reply with 24 bit address = 34ABCE and II=7
Currently acquired aircraft
24 bit aircraft address = 76ABCD
Newly acquired aircraft
24 bit aircraft address = 34ABCE

## Slide 6: Roll-call
Radar with II= 7
roll call interrogation to 76ABCD, with lock out command
Reply with 24 bit address with requested data
Reply with 24bit address and requested data
24 bit aircraft address = 76ABCD
Locked out to II = 4, 7
Locked out to SI =21, 22
24 bit aircraft address = 34ABCE
Locked out to II = 4
Locked out to SI =21, 22
Currently acquired aircraft
24 bit aircraft address = 76ABCD, 34ABCE
roll call interrogation to 34ABCE, with lock out command
Addition radar to lock out II = 7

## Slide 7: Coding of the II and SI number
4 bit IC field | 3 bit CL field
representing range of 0 to 15 decimal | 3 bit field to represent 0 to 5 decimal
Within the all-call interrogator message (UF=11), it contains 4 bit IC field and 3 bit CL field
CL field | how it affects interpretation of IC field
000 (or 0 dec) | IC field contains II code 0 to 15
001 (or 1 dec) | IC field contains SI codes 1 to 15
010 (or 2 dec) | IC field contains SI codes 16 to 31
011 (or 3 dec) | IC field contains SI codes 32 to 47
100 (or 4 dec) | IC field contains SI codes 48 to 63
Aircraft transponder need to be SI capable to interpret CL field, else it assume CL field is 0
SI code and II codes with same IC fields are ‘matching’
E.g. II = 7 is a ‘matching’ II code for SI = 23

## Slide 8: All-call (effects of aircraft with non-SI capable transponders)
24 bit aircraft address = 76ABCD
SI capable transponder
Radar with SI=23 (does not support II/SI code operations)
24 bit aircraft address = 34ABCE
Non-SI capable transponder
All call interrogation
SI=23
All call interrogation
SI = 23
Reply with 24 bit address = 34ABCE and II=7
Newly acquired aircraft
24 bit aircraft address = 76ABCD
Failed to acquire 24 bit aircraft address = 34ABCE
Reply with 24 bit address = 76ABCD and SI=23
CL = 010, IC=0111,
Its SI = 23
CL = 000, IC=0111,
Its II = 7

## Slide 9: Work-around available (II/SI code operations) using SI codes
All-call interrogations with SI codes
If transponder replies with SI code, to subsequently roll-call with SI code and issue lockout command
If any transponder replies with ‘matching’ II code, to subsequently roll-call with ‘matching’ II code and not issue lockout command

## Slide 10: All-call (SI radars with II/SI code operations)
24 bit aircraft address = 76ABCD
SI capable transponder
Radar with SI=23 (radar supports II/SI code operations)
24 bit aircraft address = 34ABCE
Non-SI capable transponder
All call interrogation
SI=23
All call interrogation
SI = 23
Reply with 24 bit address = 34ABCE and II=7
Newly acquired aircraft
24 bit aircraft address = 76ABCD
Newly acquired aircraft
24 bit aircraft address = 34ABCE,
Noted that it is non-SI capable transponder
Reply with 24 bit address = 76ABCD and SI=23
CL = 010, IC=0111,
Its SI = 23
CL = 000, IC=0111,
Its II = 7

## Slide 11: Roll-call (SI radar with II/SI code operations)
roll call interrogation to 76ABCD, SI=23 with lock out command
Reply with 24 bit address with requested data
Reply with 24bit address and requested data
24 bit aircraft address = 76ABCD
SI code capable
24 bit aircraft address = 34ABCE
Non-SI capable
Currently acquired SI transponder
24 bit aircraft address = 76ABCD
Currently acquired II transponder
24 bit aircraft address= 34ABCE
roll call interrogation to 34ABCE, II=7, without lock out command
Not locked out to II = 7
Locked out to SI=23 for future all-calls
Radar with SI=23 (radar supports II/SI code operations)
Other radars with II=7 and matching SI codes
Aircraft can respond to the all-calls
All call by other radars

## Slide 12: Work-around available (II/SI code operations) using II codes
All-call interrogations with II codes
Roll-call to ascertain whether transponder is SI capable by requesting for BDS 1,0
If BDS 1,0 indicates that transponder is SI capable, to subsequently roll-call with II code and issue lockout command
If BDS 1,0 indicates that transponder is not SI capable, to subsequently roll-call with II code and not issue lockout command
Currently practised in Europe

## Slide 13: All-call (II radars with II/SI code operations)
24 bit aircraft address = 76ABCD
SI capable transponder
Radar with II=7 (radar supports II/SI code operations)
24 bit aircraft address = 34ABCE
Non-SI capable transponder
All call interrogation
II=7
All call interrogation
II = 7
Reply with 24 bit address = 34ABCE and II=7
Newly acquired aircraft
24 bit aircraft address = 76ABCD,
unknown whether its SI capable transponder
Newly acquired aircraft
24 bit aircraft address = 34ABCE,
Unknown whether it is SI capable transponder
Reply with 24 bit address = 76ABCD and II=7
CL = 000, IC=0111,
Its II = 7
CL = 000, IC=0111,
Its II = 7

## Slide 14: Initial Roll-call (II radar with II/SI code operations)
roll call interrogation to 76ABCD, II=7 without lock out command, request for BDS 1,0
Reply with 24 bit address and BDS 1,0 indicating its SI capable
Reply with 24bit address and BDS 1,0 indicating its not SI capable
24 bit aircraft address = 76ABCD
SI code capable
24 bit aircraft address = 34ABCE
Non-SI capable
Currently acquired transponder
24 bit aircraft address = 76ABCD
roll call interrogation to 34ABCE, II=7, without lock out command, request for BDS 1,0
Radar with II=7 (radar supports II/SI code operations)
Currently acquired transponder
24 bit aircraft address = 34ABCE
Unknown whether 76ABCD is SI capable
Unknown whether 34BCE is SI capable
Note that 76ABCD is SI capable
Noted that 34BCE is not SI capable

## Slide 15: Subsequent Roll-call (II radar with II/SI code operations)
roll call interrogation to 76ABCD, II=7 with lock out command
Reply with 24 bit address with requested data
Reply with 24bit address and requested data
24 bit aircraft address = 76ABCD
SI code capable
24 bit aircraft address = 34ABCE
Non-SI capable
Currently acquired SI transponder
24 bit aircraft address = 76ABCD
Currently acquired II transponder
24 bit aircraft address= 34ABCE
roll call interrogation to 34ABCE, II=7, without lock out command
Not locked out to II = 7
Locked out to II=7 for future all-calls
Radar with II=7 (radar supports II/SI code operations)
Other radars with matching SI codes to II=7
Aircraft can respond to the all-calls
All call by other radars

## Slide 16: General strategy in migration from II to SI
II=7
SI=7
SI=23
SI=55
SI=39
Existing
New (remove one II code, replace with 4 SI codes, ensuring that all radars supports II/SI code operations)

## Slide 17: General strategy in migration from II to SI
II=7
SI=7
SI=23
SI=55
SI=39
Existing
New (there will be risk to add radars with matching SI codes without first removing the out matching II code) –see next slide
II=7
Unknown whether the radar supports II/SI code operations

## Slide 18: All-call (effects when radar with II/SI code operations overlaps with radar having match II code)
24 bit aircraft address = 76ABCD
SI capable transponder
Radar with SI=23 (radar supports II/SI code operations)
24 bit aircraft address = 34ABCE
Non-SI capable transponder, locked out to II=7 by another radar
All call interrogation
SI=23
All call interrogation
SI = 23
No reply
Newly acquired aircraft
24 bit aircraft address = 76ABCD
Could not acquired aircraft
24 bit aircraft address = 34ABCE,
Reply with 24 bit address = 76ABCD and SI=23
CL = 010, IC=0111,
Its SI = 23
CL = 000, IC=0111,
Its II = 7

## Slide 19: Conclusion
These slides are meant for simple explanation of II/SI code operations.
For mode details, please refer to Doc 9924 Appendix H and J.