## Slide 2
ATM Contingency
Arrangements and Procedures
They should provide for a timely response to a Contingency event
They should be established collaboratively
between adjacent ATS Units
Control is not enough
Management is mandatory.

## Slide 3: The ATM Contingency Management (CM) Cycle
Respond
Review
& improve
Prepare/Plan
Be Ready
Recover

## Slide 4: Some fundamentals to be considered for CM
Development of the Contingency Plan:
  How the plan is developed, agreed to and authorized
  Is it developed in collaboration with airspace users, military authorities, and adjacent FIRs.
Airspace arrangements:
  Utilizing existing ATS routes during disruptions, or contingency routes, FLAS, ATFM measures, etc. ?
ATS Contingency Procedures:
  Specific procedures for ATS during disruptions (e.g., volcanic ash, severe weather, military activity).
Pilots and Operator Procedures:
  Guidance for pilots and operators during contingency situations.
Communication Procedures:
  How information is disseminated to relevant parties.
Aeronautical Support Services:
  Support services available during contingencies (AIS, CNS, MET, SAR, etc).
TRAINING and more TRAINING and EXERCISES
Notes: ITOP

## Slide 5
ATS authorities shall develop contingency plans in the event of disruption or potential disruption of ATS and related services to ensure the continuity of the safe and orderly flow of international air traffic.
Scope of contingency management: ATS vs ATM?
Agreement with CM Cycle (Prepare, respond, recover, review)
CM in the context of crisis ad disaster relief
Resources should be allocated for CM
Crisis/contingency response must be timely.
Contingency Procedures and Arrangements should be established collaboratively
Include Contingency Procedures and Arrangements in Training
CCT and its role ensure collaboration between all parties concerned

## Slide 6: ATM Contingency Plan – ATM includes ATS, ATFM and ASM Contingency to refer to airspace disruption Crisis to refer to something bigger or the major events impacting traffic flows Contingency Events ACG: ATM Contingency Group CCC: Contingency Coordination Committee CCT: Contingency Coordination Teams
Terms
Framework vs Plan Level 1, 2 and 3 refer to the scale of a contingency event. Categories A to F identify the scope of the event and its potential impact on traffic flows. ATM Contingency Planning Principles Basic Plan Elements

## Slide 7
New [Region name] Region ATM Contingency Framework (RACF)
[Region Name] Region ATM Contingency Framework
Regional Level
National Level
[Region Name] Region ATM Contingency arrangements and procedures
National ATM Contingency Plan
Contingency Coordination Team (CCT)
ATM Contingency Group (ACG)
Contingency Coordination Committee (CCC)
PB2
Airspace
Limited
ATS
Normal
Playbooks (PBs)
PB6
Airspace
Not Available
PB5
Airspace
Available
/Limited
No ATS
PB4
Airspace
Available
/Limited
No ATC
PB3
Airspace
Limited
ATS Degraded
PB1
Airspace
Available
ATS
Degraded

## Slide 8
ATM system failure
GNSS spoofing
Industrial action
Pandemic
Facility incidents
Military activity
Contingency Events:
Earthquake
Nuclear emergency
Adverse weather
Volcanic Ash

## Slide 9: Two main conditions defining the scope, scale, and impact of contingency events: 1- ATS (Normal, Degraded, or Not Provided) 2- Airspace (Available, Limited, Not available)
The following are the three levels describing the management scale of a contingency event in the ICAO APAC Region:
Level 1: contingency within the State’s delineated FIR(s) that can be managed locally;
Level 2: cross-border contingency requiring collaboration between two adjacent States; and
Level 3: sub-regional or regional contingency requiring collaboration of more than two States.
Levels of Contingency Response

## Slide 10
The following are the categories of contingency events that identify the scope of the event and its potential impact on traffic flows. These categories are based on combinations of airspace availability and status of air traffic services:
Category A – events that would affect to some extent the provision of ATS. In this kind of events traffic will have access to the whole FIR, however, ACC will have a limitation in providing services as normal.
Category B – events that would limit access to a portion of the airspace, accordingly, ATS will have to accommodate the traffic in the available airspace through the introduction of changes to the ATS route structure.
Category C– events that will have major limitation on the airspace availability. This kind of event require procedures to circumnavigate traffic away from the affected airspace taking into consideration the limitation of the ATS..
Category D – events impacting the provision of air traffic control service but other ATS will remain available or arranged for. i.e. One of the contingency measures would be changing the airspace to class G.
Category E – events that result in no ATS could be provided, however, traffic might still have access or operate within, to or from the affected airspace. This will require arrangements by neighboring ACCs to reroute traffic avoiding the affected airspace.
Category F –events render the whole FIR not available.
Categories

## Slide 11
PB1: Airspace is available as usual, but ATS are degraded due to a Category A event such as industrial action, pandemic, earthquake, nuclear emergency, adverse weather, ATM system failure, GNSS spoofing that would affect to some extent the provision of ATS In this kind of events traffic will have access to the whole FIR, however, ACC will have a limitation in providing services as normal.
PB2: Airspace is limited due to a Category B event such as Volcanic Ash, nuclear emergencies, military activity, and weather, but ATS are normal. In this kind of events traffic would not have access to the affected portion of the airspace, accordingly, ATS will have to accommodate the traffic in the available airspace through the introduction of changes to the ATS route structure.
PB3: Airspace is limited, and ATS are degraded due to Category A events such as Volcanic Ash, nuclear emergencies, military activity, ATM system failure and adverse weather. This kind of event require procedures to circumnavigate traffic away from the affected airspace taking into consideration the limitation of the ATS.
PB4: Airspace is available or limited but no air traffic control (ATC), only flight information services can be provided, due to a Category C event such as a pandemic, national security, industrial action ATM system failure. In this kind of events provision of air traffic control is affected but other ATS will remain available or arranged for. One of the contingency measures would be changing the airspace to class G.
PB5: Airspace is available or limited, but no ATS due to a Category D event such as complete loss of facility operational capability, total loss of manpower, and security. In this kind of events no ATS could be provided, however, traffic might still have access or operate within, to or from the affected FIR. This will require arrangements by neighboring ACCs to reroute traffic avoiding the affected FIR.
PB6: Airspace is not available or avoided due to a Category E event such as airspace closure by the State or airlines avoiding the airspace due adverse weather, military activities, natural disaster despite the status of ATS. This might look similar to PB5, however, in this is the kind of event when full access to the FIR is not available.
6. Playbooks

## Slide 12: Matrix between Conditions and CAT
 | ATS Normal | ATS Degraded | NO ATC (FIS) | NO ATS
Airspace Available | Normal situation | CAT A PB1 | CAT C PB4 | CAT D PB5
Airspace Limited | CAT B PB2 | CAT A PB3 | CAT C PB4 | CAT D PB5
Airspace NOT Available | CAT E PB6 | CAT E PB6 | CAT E PB6 | CAT E PB6

## Slide 13
Group A (Meeting room 2)
List of Members:
Presenter on behalf of the Group:
Ex 1: Review the RACF and provide comments for improvement
Ex 2: Populate the relevant the Playbook Table using the scenario where ACC Charlee received information of military activities in a portion of the airspace within their FIR requesting them to deviate all traffic from that area.

## Slide 14
FIR Charlee
FIR Delta
FIR Golf
FIR Alpha
FIR Echo
FIR Bravo
FIR Foxtrot
FIR Hotel
MIL OPS
High Seas

## Slide 15
Group B (Meeting room 2)
List of Members:
Presenter on behalf of the Group:
Ex 1: Review the RACF and provide comments for improvement
Ex 2: Populate the relevant the Playbook Table using the scenario where it was reported that the earthquake in FIR Alpha damaged the CNS/ATM infrastructure and destroyed all ATS facilities.

## Slide 16
FIR Charlee
FIR Delta
FIR Golf
FIR Alpha
FIR Echo
FIR Bravo
FIR Foxtrot
FIR Hotel
High Seas

## Slide 17
Group C (Conference room)
List of Members:
Presenter on behalf of the Group:
Ex 1: Review the RACF and provide comments for improvement
Ex 2: Populate the relevant the Playbook Table using the scenario where it was reported that the earthquake in FIR Alpha damaged the CNS/ATM infrastructure but some flight information officers having been able to provide services from a back up facility.

## Slide 18
FIR Charlee
FIR Delta
FIR Golf
FIR Alpha
FIR Echo
FIR Bravo
FIR Foxtrot
FIR Hotel
High Seas

## Slide 19
Group D (Conference room)
List of Members:
Presenter on behalf of the Group:
Ex 1: Review the RACF and provide comments for improvement
Ex 2: Populate the relevant the Playbook Table using the scenario where it was reported high number of GNSS jamming/spoofing to ACC Charlee in part of the airspace they control.

## Slide 20
FIR Charlee
FIR Delta
FIR Golf
FIR Alpha
FIR Echo
FIR Bravo
FIR Foxtrot
FIR Hotel
GNSS Spoofing
High Seas

## Slide 21
Group E (Conference room)
List of Members:
Presenter on behalf of the Group:
Ex 1: Review the RACF and provide comments for improvement
Ex 2: Populate the relevant the Playbook Table using the scenario where 50% of ACC Charlee controllers went on strike for 72 hours.

## Slide 22
FIR Charlee
FIR Delta
FIR Golf
FIR Alpha
FIR Echo
FIR Bravo
FIR Foxtrot
FIR Hotel
High Seas

## Slide 23
Group F (Conference room)
List of Members:
Presenter on behalf of the Group:
Ex 1: Review the RACF and provide comments for improvement
Ex 2: Populate the relevant Playbook Table using the scenario where airlines decided to circumnavigate FIR Alpha and Charlee due to Volcanic Ash.

## Slide 24
FIR Charlee
FIR Delta
FIR Golf
FIR Alpha
FIR Echo
FIR Bravo
FIR Foxtrot
FIR Hotel
High Seas