## Slide 2: Saudia Arabia Experience in Managing GNSS Radio Frequency Interference (RFI)
ICAO MID GNSS/PBN Workshop
29th Sep – 1st Oct 2026
Presented by: Saudi Arabia

## Slide 3
GNSS RFI Statistics
Airspace: Jeddah FIR.
The GNSS RFI events have been reported by Airspace users as follow:
  2024: 1019 GNSS RFI report.
  2025: 3196 GNSS RFI report.
  2026: 1532 GNSS RFI report (As of September 2026)
Chart: Based on flight Phase
| 2024 | 2025 | 2026
ACC | 756 | 672 | 448
APP | 215 | 358 | 285
TWR | 48 | 2165 | 790
Chart: 
| 2024 | 2025 | 2026
GNSS RFI Reports | 1019 | 3196 | 1532

## Slide 4
PBN Implementation
RNAV1 & RNP APCH Navigation Specifications are implemented for international and domestic aerodromes (More then 29 aerodromes)
RNAV5 Navigation Specification is established in all CTAs. moreover, a new airspace modernization project is in progress right now and that would upgrade specific portion in OEJD FIR to meet RNAV1 with support of alternative ground infrastructures (DME/DME) to provide multi-signal coverage. (DME/DME geometry/coverage assessment & Optimization and NAV MON study are both in the review phase by the ANSP).
For example, OEJN, OERK, OEMA and OEDF, a total of 17 RNP APCH procedures are currently in operation and more than 18 RNAV1 SIDs are implemented using GNSS as the navigation sensors.
PBN procedures are designed and implemented using the applicable ICAO PANS-OPS criteria specified in ICAO Doc 8168 and ICAO Doc 9613 ensuring standardized and safe procedure design.
Conventional IFPs, based on VOR/DME and DMD/DME, remain in operation as an alternative navigation capability in the event of GNSS RFI. However, the DME/DME Optimization will provide sufficient coverage to enable RNAV based navigate in a multi-signal coverage along flight path.

## Slide 5
Operational Impact of GNSS RFI
Potential Impact on flight operations
Degradation of onboard GNSS-based navigation capabilities.
losing RNAV/RNP IFPs.
Increased Pilots and ATCOs workload.
Delays, flight path deviations, and reduced operational efficiency.
Increased reliance on conventional navigation aids. and pilot monitoring.
Potential disruptions to IFR operations.
  2) Potential Impact on ground-based systems
Reduced performance of GNSS-dependent surveillance systems.
Impact on ADS-B integrity.
Time Synchronization issues for systems relying on GNSS.
Degraded performance of ATM automation systems using GNSS inputs.
Increased reliance on backup infrastructure and contingency procedures.
Additional monitoring and coordination requirements for CNS/ATM systems.

## Slide 6
Coordination and Stakeholder Engagement
Given the inherent uncertainty surrounding the origins and impacts of GNSS RFI, ANSPs worldwide may encounter challenges in anticipating such events and resolving the resulting issues. Nevertheless, since 2024, an effective national coordination framework has been established, bringing together all relevant competent authorities and the Communications, Space, and Technology Commission (CSTC) to address GNSS RFI incidents at the national level. This framework supports RFI detection, mitigation, and risk management.
1) Coordination with the national radio regulator

## Slide 7
Coordination and Stakeholder Engagement
Given the broad reach and consequences of GNSS RFI, coordination extended beyond civilian bodies to include all relevant military authorities. That also within the national coordination framework that has been established in 2024.
  2) Coordination with military authorities

## Slide 8
Coordination and Stakeholder Engagement
Neighboring states with support of ICAO MID office should cooperate to establish a regional framework to manage GNSS RFI by and limited the following:
GNSS RFI Guidance to unify and standardized the operational procedure;
Sharing the significant GNSS RFI;
Established a regional NAV MON/RON enhancement;
Engage MID airspace users;
other
3) Coordination with adjacent States and ANSPs

## Slide 9
GNSS RFI reports are immediately generated to the frequency management authorities once verified to identify the source of the interference.
NOTAMS are raised to inform airspace users of the outages.
Dedicated ground team trained in interference identification and location using specialized directional handheld antennas and spectrum analyzers.
GPMS records are reviewed and generated.
Reports from airspace users are recorded and escalated by ATCOs.
The GNSS Performance Monitoring System (GPMS) that has been in operation since 2013 automatically generates NOTAM templates if GNSS outages are identified. Although this system has its limitations and is currently in the process of being replaced with one that has more coverage and is specifically designed to detect Jamming and spoofing using more modern means of detection and reporting.
(1) Technical measures (1/2)
Mitigation Measures

## Slide 10
Once reported by airspace users and verified, GNSS RFI NOTAMs are issued manually. The primary difficulty in preparing these notices is defining the extent of the impact.
Automated detection systems often struggle to determine the impact’s location and extent, particularly in large states where GNSS RFI may originate from multiple intentional or unintntional sources.
Mitigation Measures
(1) Technical measures (2/2)

## Slide 11
(2) Operational Contingency Measures (1/2)
Activate contingency procedures in the event of GNSS degradation or service interruption.
Strengthen the monitoring and formal reporting of GNSS radio-frequency interference (RFI) incidents.
Promulgate NOTAMs and operational advisories when significant GNSS disruptions are identified.
Employ conventional navigation aids (VOR/DME, ILS, and NDB, where available) as alternative means of navigation.
Apply tactical ATC measures, including radar vectoring and the assignment of alternative routes.
Reinforce coordination among ATC units, air operators, military authorities, and adjacent FIRs.
Promote controller and pilot awareness through formal briefings and authoritative operational guidance.
Maintain contingency communication arrangements and backup CNS capabilities.
Continuously assess operational impacts and implement traffic management measures as necessary.
Mitigation Measures

## Slide 12
(3) Safety measures
GACA (CAA) has issued a safety bulletin in 2024 Safety Bulletin providing a safety information and recommended actions to ANSP & Airspace Users when experiencing a GNSS RFI within Jeddah FIR.
GACA leading the coordination with all relevant civil/military parties and Communication Authority (CSTC).
GACA adopted the NAV MON/RON in the NANP.
GACA categorized the GNSS RFI as high risk and established a daily monitoring procedure.
Mitigation Measures

## Slide 13
Challenges and Lessons Learned
After years of advocacy by numerous states and organizations for replacing conventional NAVAIDs with GNSS, the growing prevalence of electronic warfare and other emerging risks has prompted a reassessment in recent years.
While GNSS offers substantial operational benefits, each state should retain a secondary layer of conventional ground-based navigation infrastructure to preserve sovereignty, reduce dependence, and safeguard the safety and security of its airspace.
DME/DME navigation and other advanced technologies can provide the benefits of GNSS while enhancing reliability, redundancy, and operational independence.
NAV MON/RON should be implemented not merely to meet current requirements, but to anticipate and accommodate future demand. Capacity should consistently remain ahead of traffic growth; maintaining this margin represents the principal challenge.
Detection and response addressing only one dimension of the solution; coordinated action and sustained cooperation are equally essential to mitigating GNSS RFI.