## Slide 1: ASBU Methodology Summary of Block 0 Modules H. Sudarshan
SIP/2012/ASBU/Nairobi-WP/8
Workshop on preparations for ANConf/12 − ASBU methodology
(Nairobi, 13-17 August 2012)

## Slide 2: Outline
Block understanding
Block Maturity cycle
Block 0 perspective
Block 0 Modules
Block 0 implementation

## Slide 3: Understanding the Relationships
3
Optimum Capacity and Flexible Flights
Globally Interoperable Systems and Data
Efficient Flight Path
Airport Operations
Performance Improvement Areas
Block 0
(2013)
Block 1
(2018)
Block 2
(2023)
Block 3
(2028 & >)
B3-15
B2-15
B1-15
B0-15
Module
ICAO SIP 2012-ASBU workshops

## Slide 4
Block Maturity Lifecycle
SIMPLIFIED
LIFECYCLE
IOC
Initial Operational Capability
-
Feasibility
Operations
Deployment
Industrialisation
Decommissioning
V3
V2
V6
V5
V4
V7
V1
V0
V3
V2
V6
V5
V4
V7
V1
R&D
Implementation
Operations
B0
B3
B2
B1
Concept Definition
Identification of Needs
B0: Capabilities available in 2013
Standardisation activities
Pre-Industrial Development and Integration
Decision
Decision
Decision
Decision
Planning Decisions
based on business case and validation results as developed during the previous phase
ICAO SIP 2012-ASBU workshops
4
Notes: This will be an evolving set of solutions. Block 0 is based on existing, fielded capabilities and includes installed aircraft functionality. Within the Aviation System Block Upgrades it represents the Initial Operating Capability available for use in 2013.
The next capabilities to be introduced will be described as Block 1 in 2018. In the case of Block 1, one of several “readiness” characteristics have not been met. But it is expected that over the next 5 years those modules will mature to enable the next level of capabilities to ensure implementation.
Beyond that we expect that those capabilities that are maturing through a development phase will be moved to an operational capability in 2023.
And further in time we anticipate that many of the capabilities in the research phases will move through the life cycle for release in the 2028+ time period.
But back to Block 0.

## Slide 5: Focus on Block 0
5
Optimum Capacity and Flexible Flights
Globally Interoperable Systems and Data
Efficient Flight Path
Airport Operations
Performance Improvement Areas
Block 0
(2013)
ICAO SIP 2012-ASBU workshops
Notes: So what makes Block 0 unique?
For Block 0, no new airborne technologies are required. However, it may be necessary to increase the participating aircraft to improve the size of the benefit to ensure payback and the ability to close the business case.
Each of the Modules or capabilities included have are operational in at least two diverse operational areas. These are not trial programs, but are fully functional including procedures, approvals, certification, standards, etc. Each module has been evaluated against a “readiness checklist” to ensure that the operational criteria have been met.

## Slide 6: Global Readiness Checklist
Each Module is evaluated for its readiness
If any component is not found to be ready it moves to a future Block for implementation
Those Modules that are not specifically ready at a Block release are noted as “dates of readiness”
All Block 0 Modules Have Met the Readiness Criteria
ICAO SIP 2012-ASBU workshops
Notes: I mentioned the Global Readiness Checklist – this is a tool to assess if all the key components are in place to allow operational credit. It is much more than standards. Of course we want to ensure that all the necessary standards have been developed and released to make sure we have a stable system going forward.
But the overall readiness of a Module also depends on the avionics availability, the end to end infrastructure, and the automation necessary to take advantage of the airborne capabilities.
Further we also look to see if the procedures and approvals are in place. We have learned that it is more that technology or an installed capability to provide access to benefits.
Why this attention to detail? This process offers insight into the level of detail necessary to implement a capability. We want to manage the risk so that any member state can adopt a module with confidence. We want to bring forward a positive business demonstrated by those that adopted the solution referenced in a given Block Upgrade.

## Slide 7: Block 0
4 Main Performance improvement areas
  Airprot Operations (5 modules)
  Globally interoperable systems & data (3 modules)
  Optimum capacity & flexible flights (7 modules)
  Efficient flight path (3 modules)
  Block 0 will serve as the enabler and foundation for the envisioned future aviation systems.

## Slide 8: Block 0 in Perspective
Infrastructure
CTA
B0-65 – Optimisation of approach procedures including vertical guidance
B0-75 – Safety & Efficiency of Surface Operations (A-SMGCS 1-2 & cockpit moving map)
B0-80 - Improved Airport Operations through A-CDM
B0-15 - Improved Runway Traffic Flow through Sequencing (AMAN/DMAN)
B0-70 - Increased Runway Throughput through Wake Turbulence Separation
Information
B0-30 - Service Improvement through Digital Aeronautical Information Management
Network
ToD
B0-05 - Improved Flexibility & Efficiency in Descent Profiles (CDOs)
B0-20 - Improved Flexibility & Efficiency in Departure Profiles
B0-25 - Increased Interoperability, Efficiency & Capacity through Ground-Ground Integration
ToC
B0-101 – ACAS Improvements
B0-10 - Improved Operations through Enhanced En-Route Trajectories
B0-35 - Improved Flow Performance through Planning based on a Network-Wide view
B0-40 - Improved Safety & Efficiency through the initial application of Data Link En-Route
B0-85 – Air Traffic Situational Awareness (ATSA)
B0-84 – Initial surveillance capability ADS-B Out, MLAT)
B0-86 – Improved Access to optimum FL through climb/descent procedures using ADS-B)
B0-102 – Baseline Gound-based Safety Nets
Airport Operations
Optimum Capacity and Flexible Flights
Efficient Flight Path
Globally Interoperable Systems and Data
Performance Improvement Areas
B0-105 – Meteorological information supporting enhanced operational efficiency and safety

## Slide 9: Airport Operations (PIA 1)
B0-65 - Optimization of Approach Procedures including Vertical Guidance
This is the first step toward universal
implementation of GNSS-based approaches
B0-70
Increased Runway Throughput through
Wake Turbulence Separation
Improved throughput on departure and arrival runways through the revision of current ICAO wake vortex separation minima and procedures (re-categorisation, CSPR and WIDAO)
B0-75
Improved Runway Safety (A-SMGCS) Airport surface surveillance for ANSP
B0-80
Improved Airport Operations through ACDM
Airport operational improvements through the way operational partners at airports work together
B0-15
Improved Runway Traffic Flow through Sequencing (AMAN/DMAN)
Time-based metering to sequence departing and arriving flights
The combined Block 0 Modules reduce fuel consumption and noise by improving arrival efficiencies and improving information sharing
Notes: So let’s explore how the modules can be assembled to support the Performance Improvement Areas. First we need to recognize that each Module has its own positive business case. But by combining then into an integrated Performance Improvement Area we enhance the benefits. This is a case where the whole is greater than the sum of the parts. In the case of Greener Airports the combination of:
A policy shift to time-based metering
The application of initial space and ground based augmentation to GNSS
Changes in Wake Vortex separation minima
Improved surface surveillance using multilateration
And improved information sharing
Yield a more significant set of benefits than any single Module’s benefit. This is an example of why care must be taken if there is a desire to implement a subset of Blocks as opposed to the integrated family of Blocks. There is flexibility and scalability considered for each of these Performance Improvement Areas with the key being interoperability.

## Slide 10: Globally Interoperable Systems and Data (PIA 2)
B0-25
Increased Interoperability, Efficiency and
Capacity through Ground-Ground
Integration
Supports the coordination of ground-ground
data communication between ATSU based on ATS Inter-facility Data Communication (AIDC) defined by ICO Document 9694
B0-30
Service Improvement through Digital
Aeronautical Information Management
Initial introduction of digital processing and
management of information, by the
implementation of AIS/AIM making use of
AIXM, moving to electronic AIP and better
quality and availability of data
In Block 0 we improve overall operations and continue to enable Collaborative Decision Making through improved interfacilities communications using standard information formats and baseline Met Services
B0-105 – Meteorological information supporting enhanced operational efficiency and safety
This module includes meteorological information supporting automated decision processes or aids such as meteorological information translation, ATM decision support. This module enables the reliable identification of applicable ATM solutions when meteorological conditions are impacting (observed) or expected to impact (forecast) aerodromes or airspace
Notes: Similarly, we find by improving our ability to share information and to ensure that the best information at the time is available to the decision makers. Improvements in Interfacility Communications and the use of common information formats means that we can all make better decisions. This infrastructure enables global information sharing and common decision structures which improve our overall operations.

## Slide 11: Optimum Capacity and Flexible Flights (PIA 3)
Using procedural concepts (e.g. RNP, FUA, etc.) and Air Traffic Situational Awareness - combined with enhanced planning tools and information sharing, the enroute phase of flight supports additional capacity and flexibility using the Modules of Block 0
B0-10: Improved Operations through Enhanced En-Route Trajectories
Implementation of performance-based
navigation (PBN concept) and flex tracking to avoid significant weather and to offer greater fuel efficiency, flexible use of airspace (FUA) through special activity airspace allocation, airspace planning and time-based metering, and collaborative decision-making (CDM) for en-route airspace with increased information exchange among ATM stakeholders
B0-35:Improved Flow Performance through
Planning based on a Network-Wide view
Collaborative ATFM measure to regulate peak flows involving departure slots, managed rate of entry into a given piece of airspace for traffic along a certain axis, requested time at a waypoint or an FIR/sector boundary along the flight.
B0-85: Air Traffic Situational Awareness (ATSA)
ATSA provides a cockpit display of a graphical
depiction of traffic to assist the pilot in out-the-window visual acquisition of traffic:
B0-86: Improved access to Optimum Flight Levels through Climb/Descent Procedures using ADS-B
The use of In Trail Procedure (ITP) facilitates en-route climb or descent to enable better use of optimal flight levels in environments where a lack of ATC surveillance and/or the large separation minima currently implemented is a limiting factor.
B0-101 ACAS Improvements
This addresses short term improvements to the performance of the existing airborne collision avoidance systems (ACAS).
Notes: And to be sure it is not all about hardware. In assessing the Optimum Capacity and Flexible Flights Performance Improvement Area there are components of procedure development to build on RNP and Flexible Use of Airspace concepts and initial airborne situational awareness implementations we find that we have the formula to grow the system capabilities. Add to that improved information sharing, as noted in the Globally Interoperable Systems and Data area and we now can share the improved information and enable the airspace.

## Slide 12: Optimum Capacity and Flexible Flights (PIA 3) -Continued
Through ground based safety nets combined with ground surveillance the enroute phase of flight supports additional capacity, flexibility and safety
B0-84 – Initial surveillance capability ADS-B Out, MLAT
Ground surveillance supported by ADS-B OUT and/or wide area multilateration systems will improve safety, especially search and rescue and capacity through separation reductions.
B0-102 – Baseline Ground-based Safety Nets
To monitor the operational environment during airborne phases of flight, the alerts such as Short Term Conflict Alert, Area Proximity Warnings and Minimum Safe Altitude Warnings are proposed in this module. Ground-based safety nets make an essential contribution to safety and remain required as long as the operational concept remains human-centred.
Notes: And to be sure it is not all about hardware. In assessing the Optimum Capacity and Flexible Flights Performance Improvement Area there are components of procedure development to build on RNP and Flexible Use of Airspace concepts and initial airborne situational awareness implementations we find that we have the formula to grow the system capabilities. Add to that improved information sharing, as noted in the Globally Interoperable Systems and Data area and we now can share the improved information and enable the airspace.

## Slide 13: Efficient Flight Path (PIA 4)
B0-05
Improved Flexibility and Efficiency in
Descent Profiles (CDOs)
Deployment of performance-based airspace
and arrival procedures that allow the aircraft to fly their optimum aircraft profile taking account of airspace and traffic complexity with continuous descent operations (CDOs)
B0-20
Improved Flexibility and Efficiency in
Departure Profiles
Deployment of departure procedures that allow the aircraft to fly their optimum aircraft profile taking account of airspace and traffic complexity with continuous climb operations (CCOs)
B0-40
Improved Safety and Efficiency through the
initial application of Data Link En-Route
Implementation of an initial set of data link
applications for surveillance and
communications in ATC
The use of procedurally based Optimized Profile Climbs and Descents as well as an initial Data Link Capability helps to establish a Block 0 capability for improved operational efficiencies
Notes: For the Efficient Flight Path Performance Improvement Area we recognize the improvements for Optimized Profile Climb and Descent in B0-05 and B0-20. Today we initiate those operations with voice commands.
By introducing a Data Link capability for either the simple trigger message to begin the operation or to upload a revised clearance package consistent with the climb or descent, we further improve the flight path efficiency. B0-40 is a reflection of today’s oceanic and remote data link system.
We saw the initial application of these capabilities in Tailored Arrivals in the Pacific and Atlantic operating areas. Further we are now seeing revenue flights into Los Angeles using the modules as described on a day to day basis. Other regions like Sydney, Miami, Atlanta, and others are preparing for similar use.
While there are no dependencies these are clearly first steps to the follow-on capabilities contained in Block 1.
These Modules are know to work, provide access to definable benefits, and are proven and demonstrate complete readiness against the checklist. They can be deployed on a global basis with a clearly described implementation package. This package has been developed on a global basis based on the regions using the capabilities described.
But this is just the starting point for the future. Block 0 provides the foundation and enables Block 1 to build on those successes. Blocks 2 and 3 add additional capabilities for those that require additional capabilities.

## Slide 14: Block 0: Priority
Block 0 initiatives must leverage on existing
on-board avionics
3 Priorities have been agreed to by the Global community:
  Performance Based Navigation (PBN)
  Continuous Descent Operations (CDO)
  Continuous Climb Operations (CCO)
Notes: PBN:
Runway safety:
Main enabler to address CFIT and unstabilized approaches
Accessibility: due to flexibility and application of modern on-board avionics to its full extent, more rwys are accessible (previously not accessible, or by less safe circling, offset or steep angle approaches)
Efficiency: through application of modern on-board avionics to its full extent, positioning of routes, Sids and Stars is not constraint anymore by location of navaids, but can be put virtually anywhere (airspace optimization, less fuel burn, less delays, workload decrease). CDO and CCO’s reduce fuel burn and noise.
PBN is a prerequisite before starting next generation airspace concepts. Therefore a full commitment to PBN and education is a prerequisite before starting the next generation projects.
CCO and CDO:
Continuous Descent en Climb Operations are significant contributors to efficiency and environmental benefits, fuel burn, emission and noise reductions. These type of operations are very much linked to PBN. As these type of operations have a potential to consume a lot of airspace, the airspace design flexibility provided by PBN is indispensable.

## Slide 15: Challenges - How to Get There?
It is all about managing risk
Block 0 risks are minimum
  Global Readiness Checklist is complete
  The Modules are well understood and supported
But risks do exist
  States may not be capable of ensuring successful deployment of Block 0
  If Block 0 is not implemented as a foundation, certain functionalities may not be available as enablers for future blocks
  We must Identify and resolve policies necessary to enable the future blocks now
ASBU workshop, Mexico, 27 February-2 March 2012
ICAO SIP 2012-ASBU workshops
Notes: The future is in our hands. It is up to us to manage the risks associated with any change. The good news is that the Aviation System Block Upgrade program is the best approach to reach our goals:
Enables global interoperability (which is our goal)
Develops clear solutions (block upgrades)
Establishes a transition plan (it’s a well thought out way for going forward)
Support the development of a Global CNS/AIM and avionics roadmaps
Risks still exist – but together we can work to resolve them – just as we have worked as a global community to develop the Modules and Blocks. The proposed approach is not a one-size fits all:
Modules are organized into flexible and scalable building blocks
Can be introduced and implemented in a State or a region depending on the need and level of readiness
Recognizes that all the blocks/modules are not required in all airspaces (important for some regions), but some may need a global mandate and synchronisation

## Slide 16: Implementation – The Time is Now
The Modules of Block 0 are ready for implementation today
  Standards are ready – The Infrastructure is available
  Avionics are ready – Ground Automation is ready
  Procedures and Operational Approvals are in place
Establishing the foundation for the future is now
Care was taken to ensure that regional implementation of the Blocks or the Modules are well described and ready for implementation
ICAO SIP 2012- ASBU workshops
Notes: The deployment of block upgrades has been chosen to resolve many of these identified risks. The timing and sizing of these are in response to the need for mature standards, integrated air and ground solutions, and the establishment of positive business cases that bring identifiable benefits forward for ICAO Aviation System Block Upgrades a level of equipage and infrastructure cost. Those capabilities that lack specific maturity in content or described benefit are purposefully placed in the later block upgrades.
Block upgrades also respond to the issue of “non-homogeneous deployment across regions”. Each block and its underlying components are intended to interoperate seamlessly, independent of how they are implemented in neighboring States. This ensures that procedures, training, policy and other “infrastructure” are consistent, enabling a safe transition to more capable airspace.

## Slide 17
ICAO SIP 2012-ASBU workshops