## Slide 1: Global Guidance Key points Seychelles Feb 2012
Tom Brady
Air Navigation Bureau
2012 Flight plan implementation status

## Slide 2: Following the ICAO Implementation guidelines
Under the phased approach, States will not implement NEW capability before the commencement of the ANSPs external testing and implementation period on 1 April 2012
Expected to complete implementation of NEW capability by the end of the ANSPs external testing and implementation period on 30 June 2012.
Airspace users would be invited by AIC, AIP supplement and/or NOTAM to commence testing with ANSPs from 1 July 2012.

## Slide 3: 120 Hour filing of Flight Plans
Investigations by the APAC FPL&AM/TF have been unable to identify required operational circumstances in the Asia/Pacific Region where FPL lodgement earlier than 24 hours was necessary to meet the medium term needs of States. A similar situation is reported by IATA in respect to Asia/Pacific operators.
The FPL&AM/TF does not support a compulsion on all Asia/Pacific States to meet the 120 hour lodgement provision by 15 November 2012.
This is expected to mitigate the transition issues associated with DOF/ matters and reduce transmission of superfluous modification messages and the associated loading on messaging systems.

## Slide 4: Use of P1 – P9(reserved for RCP)
Even though there is no need for this information now, ANSPs should accept P1-P9 if filed in an FPL and pass the information in AIDC messages, but with no interpretation or processing required.
This will avoid transition issues and minimize necessary coordination when these items begin to be used in the future.

## Slide 5: Changed definition of “S” in Field 10a
Amendment 1 changes the definition of standard equipment in Field 10a (“S”) so that it no longer includes ADF
It is essential to know whether an FPL is in NEW or PRESENT format before interpreting an “S” filed in Field 10a.

## Slide 6: Consistency between Field 10a and PBN/ in Item 18
The Amendment introduces a relationship between PBN/ in Item 18 and Field 10a, and it is possible to file inconsistent data (i.e., capabilities in PBN/ that are not supported by data in Field 10a)
A consistency check should be coded into software to evaluate NEW FPLs per the guidelines specified in paragraph 5.5 of the APAC guidance.

## Slide 7: Consistency between Item 10a and STS/ in Item 18
Amendment 1 formalised flight plan filing of the mutually exclusive entries ‘W’ (in Item 10a) and “NONRVSM” (in Item 18 STS/).
The use of NONRVSM in STS is to signify intent to operate as a Non-RVSM flight in RVSM airspace.
To avoid contradictory RVSM indications and possible incorrect application of separation standards based on this, the following consistency check should be coded in the software to evaluate NEW FPL related messages.
If STS/NONRVSM is filed in Item 18 then ‘W’ should not exist in Item 10a.

## Slide 8: Validity Checking & Processing of Item 18 Indicators
Systems should not accept indicators in Item 18 which are not defined in the PANS-ATM. If internal requirements create the need to use a ‘local’ non-standard indicator, measures must be taken to ensure that airspace users filing with multiple FIRs are not impacted.
Airspace users should file indicators in the required order to ensure that systems applying truncation do not eliminate more important data. ANSPs should either enforce the required order, or ensure that AIDC messages contain the items in the required order regardless of the order filed.
Airspace users should only file a single instance of each indicator. If duplicate indicators are detected, their contents will be concatenated within a single occurrence of the indicator but with a space inserted between the two data streams.

## Slide 9: Allowable Indicators and mandated order in Item 18.
Standard indicators should be filed in the order promulgated in Amendment 1 and always appear at the beginning of Item 18.
A number of states have advised that they will continue to use legacy regional indicators such as RVR/ and RFP/.
It is therefore recommended that to avoid large scale automated rejections; ANSPs code their systems to accept non-standard indicators to be reordered at the end of Item 18 i.e. after the standard indicators.

## Slide 10: Other guidance items.
Processing location information in the DEP/, DEST/, ALTN/, RALT/ and TALT/ indicators in Item 18.
Use of the DLE/ indicator in Item 18.
Special handling (STS) indicator
Conversion from NEW format to PRESENT format
Differentiating between NEW format and PRESENT format
ATS Messages

## Slide 11: Regional aspects
States will be asked by ICAO to provide their exact cutover timing for promulgation on the FITS website. States should consider planning this timing in conjunction with neighbouring states.
Minimize State specific constraints and, if constraints are identified as necessary, implement such constraints on a regional or sub regional basis in preference to an individual State basis.
To mitigate Date Of Flight (DOF) complexities, adopt a regional approach that does not require processing of flight plans more than 24 hours prior to Estimated Off Blocks Time (EOBT) during the declared transition period.

## Slide 12: Questions Please!
Tom Brady