## Slide 1: SESSION 1 REGIONAL RADIO NAVIGATION AID PLAN
SAM NAVIGATION SYSTEM IMPLEMENTATION PLAN
ONOFRIO SMARRELLI
REGIONAL CNS EXPERT
ICAO SOUTH AMERICAN OFFICE
LIMA PERU
OSMARRELLI@LIMA.ICAO.INT
Phone No. 511 6118686

## Slide 2: CONTENTS
OBJECTIVE
CAR/SAM AIR NAVIGATION PLAN
AMENDMENTS TO NAVIGATION-RELATED SARPS OF ANNEX 10
FREQUENCY BAND FOR THE RADIO NAVIGATION SERVICE
NAVIGATION ASPECTS OF GREPECAS
IMPLEMENTATION OF NAVIGATION SYSTEMS IN THE SAM REGION
CONCLUSIONS

## Slide 3: OBJECTIVE
THE OBJECTIVE OF THIS PRESENTATION IS TO PROVIDE INFORMATION ON THE PLANNING AND IMPLEMENTATION OF NAVIGATION SYSTEMS IN THE SAM REGION, AS FOLLOW-UP TO THE CAR/SAM REGIONAL AIR NAVIGATION PLAN, GREPECAS CONCLUSIONS AND THE SAM PERFORMANCE-BASED AIR NAVIGATION IMPLEMENTATION PLAN

## Slide 4: CAR/SAM REGIONAL AIR NAVIGATION PLAN
AIR NAVIGATION PLANS PROVIDE A DETAILED DESCRIPTION OF FACILITIES AND PROCEDURES REQUIRED FOR INTERNATIONAL AIR NAVIGATION IN A GIVEN AREA.
THESE PLANS CONTAIN RECOMMENDATIONS THAT GOVERNMENTS MAY FOLLOW WHEN PLANNING FOR THE PROVISION OF AIR NAVIGATION FACILITIES, WITH THE ASSURANCE THAT THE FACILITIES THUS FORESEEN, TOGETHER WITH THOSE OF THE OTHER STATES, WILL FORM AN INTEGRATED SYSTEM SUITED FOR THE FORESEEABLE FUTURE.
ON 26 FEBRUARY 1997, THE ICAO COUNCIL DECIDED THAT REGIONAL AIR NAVIGATION PLANS (ANPs) WOULD BE PUBLISHED IN TWO VOLUMES: A BASIC ANP AND A FACILITIES AND SERVICES DOCUMENT (FASID) FOR THE CAR/SAM REGIONS. THE AIR NAVIGATION PLAN IS CONTAINED IN DOCUMENT 8733.
THE BASIC ANP CONTAINS THE UNCHANGING ELEMENTS OF THE PLAN, SUCH AS :
THE GEOGRAPHIC AREA THAT ENCOMPASSES THE FLIGHT INFORMATION REGIONS (FIRs) COVERED BY THE PLAN.
BASIC OPERATIONAL REQUIREMENTS AND PLANNING CRITERIA.
REGIONAL PLANNING AND IMPLEMENTATION GUIDELINES CONTAINED IN THE RECOMMENDATIONS ISSUED BY REGIONAL AIR NAVIGATION MEETINGS.

## Slide 5: CAR/SAM REGIONAL AIR NAVIGATION PLAN
THE FASID CONTAINS THE MOST DYNAMIC TEXTS OF THE PLAN, COVERING THE FACILITIES AND SERVICES REQUIRED BY INTERNATIONAL AIR NAVIGATION IN THE SPECIFIC AREA
THE CAR/SAM REGIONAL PLANNING AND IMPLEMENTATION GROUP (GREPECAS) CONTINUOUSLY REVIEWS THE BASIC ANP AND THE FASID IN ORDER TO MEET, INTER ALIA, THE REQUIREMENTS OF THE GLOBAL AIR NAVIGATION PLAN (DOCUMENT 9750)
IN ACCORDANCE WITH ARTICLE 28 OF THE CONVENTION, EACH CONTRACTING STATE IS RESPONSIBLE FOR THE PROVISION OF FACILITIES AND SERVICES IN ITS TERRITORY. THE COUNCIL HAS RECOMMENDED THAT THESE FACILITIES INCLUDE THOSE SPECIFIED IN THE AIR NAVIGATION PLANS

## Slide 6: CAR/SAM REGIONAL AIR NAVIGATION PLAN
NAVIGATION SYSTEMS
PART I, BASIC ANP
BASIC OPERATIONAL REQUIREMENTS AND PLANNING CRITERIA (BORPC)
COMMERCIAL AIR TRANSPORT OPERATIONS
EN-ROUTE AIDS (VOR/DME, GNSS)
TERMINAL AREA AIDS (GNSS, VOR/DME)
FINAL APPROACH AND LANDING NON-VISUAL AIDS
  SHALL MEET THE GENERAL PROVISIONS SPECIFIED IN ANNEX 10, VOLUME I, 2.1 AND ATTACHMENT B, VOLUME I
  AIRCRAFT AERODYNAMIC AND MANOEUVRING CHARACTERISTICS
  REGULAR APPROACHES WITH AUTOPILOT
NON-PRECISION INSTRUMENT APPROACH PROCEDURES
Notes: Ayudas en ruta
63.Las ayudas en ruta que han de recomendarse deberían proporcionar ayuda para la navegación que permita la navegación en ruta, con la precisión requerida, en la red de rutas acordada de los servicios de tránsito aéreo.
64.Se prevé que el GNSS permitirá finalmente satis-facer todos los requisitos para la navegación en ruta. En la planificación de otras ayudas en ruta debería tenerse en cuenta la necesidad de una transición gradual al uso del GNSS en lugar de las ayudas para la navegación en ruta basadas en tierra. Hasta la implantación del GNSS, deberían instalarse VOR complementados con DME en la medida necesaria, como ayuda primaria para ese fin.
65.Para fines de planificación, cuando se utilice VOR, complementado de ser necesario con un DME, debería considerarse un valor total de error de navegación del VOR de ±5 (95% de probabilidad). Sin embargo, el valor específico del error de la señal del radial VOR para instalaciones/radiales individuales, debería obtenerse por medio de verificación en vuelo, y si estos valores exceden de ±3, deberían tomarse las precauciones apropiadas con respecto a las rutas en cuestión.
66.Siguen facilitándose las radioayudas apropiadas para la navegación de larga distancia cuando se precisan.
Ayudas de área terminal
67.Se prevé que el GNSS permitirá finalmente satis-facer todos los requisitos para la navegación en el área terminal. En la planificación de otras ayudas en el área terminal debería tenerse en cuenta la necesidad de una transición gradual al uso del GNSS en lugar de las ayudas para la navegación de área terminal basadas en tierra.
68.Las ayudas de área terminal que han de recomen-darse deberían permitir la navegación de forma que la aproximación, la espera y la salida se lleven a cabo con la precisión requerida. Cuando el VOR se utilice como la ayuda primaria, debería estar emplazado de tal forma que permita la aproximación y los procedimientos de control de tránsito aéreo más eficaces, y proporcione al piloto la máxima ayuda para ajustarse a los circuitos requeridos. Siempre que sea posible, los VOR deberían emplazarse y utilizarse de forma que sirvan de guía tanto para la navegación en ruta como para la navegación terminal, incluida la espera. Cuando no es posible facilitar VOR para la espera, pueden utilizarse NDB con este fin. Debería tenerse en cuenta la posibilidad de emplazar DME en el mismo lugar que los VOR, siempre que sea preciso a fin de asegurar la flexibilidad necesaria del ATC para encaminar el tránsito aéreo en determinada TMA y cuando el mejoramiento de la precisión de la nave-gación sea un prerrequisito para contar con dicha flexibilidad.
Ayudas no visuales para la aproximación
final y el aterrizaje
69.Las ayudas no visuales normalizadas de la OACI para la aproximación final y el aterrizaje, utilizadas en apoyo de las operaciones de aproximación y aterrizaje de precisión, cumplirán con las disposiciones generales el Anexo 10, Volumen I, 2.1, y su introducción y aplicación deberán estar acordes con la estrategia contenida en el Adjunto B del Volumen I.
70.Al planificar la necesidad de instalar ayudas para la aproximación final y el aterrizaje, debería considerarse cada aeródromo en relación con su tránsito, sus condiciones meteorológicas y otros aspectos de su entorno. Además, también deberían tenerse en cuenta los dos aspectos siguientes, al determinar los requisitos específicos:
a) Las características aerodinámicas y de maniobra de las aeronaves. Los aviones turborreactores necesitan una guía de trayectoria de aproximación de precisión durante la aproximación y el aterrizaje, con independencia de las condiciones meteorológicas. Debería proporcionarse esta guía en las pistas destinadas a ser utilizadas por estos aviones, del modo siguiente:
1) En una pista con tránsito de importancia, las instala-ciones deberían ser una ayuda no visual normalizada de la OACI para la aproximación final y el aterrizaje, complementada por un sistema visual indicador de pendiente de aproximación. El hecho de que no pueda instalarse una ayuda no visual normalizada inicial-mente, no debería demorar la instalación del sistema visual indicador de pendiente de aproximación; y
2) En una pista sin tránsito de importancia, las instala-ciones deberían incluir, como mínimo, un sistema visual indicador de pendiente de aproximación.
b) Las aproximaciones ordinarias con piloto automático. Cuando haya que realizar aproximaciones con piloto automático con carácter rutinario, debería proporcionarse una ayuda no visual normalizada de la OACI para la aproximación final y el aterrizaje, es decir, ILS o MLS, apropiada para el tipo de operaciones que se prevea realizar en el aeródromo. Si se trata de una insta-lación ILS de Categoría I, debería tener una calidad de señal de Categoría II, sin tener que satisfacer necesa-riamente los correspondientes criterios de confiabilidad y disponibilidad en cuanto a equipo de reserva y tiempos de conexión automática de la Categoría II, pero debería ajustarse y mantenerse con el mayor cuidado y la mayor precisión posibles, y sus características de rendimiento deberían publicarse en las AIP o en otros documentos apropiados.
Procedimientos para aproximaciones por
instrumentos que no sean de precisión
71.Los procedimientos para aproximaciones por instrumentos que no sean de precisión pueden basarse en ayudas distintas a las ayudas no visuales normalizadas (véase 69) que deberían también apoyar las SID y STAR. Dichos procedimientos deberían construirse siempre que sea posible de conformidad con el concepto de aproximación estabilizada; prever una trayectoria de planeo de aproxi-mación final de 3; eliminar las aproximaciones con escalón de descenso; y proporcionar un punto de referencia de aproximación final.
72.Debería tenerse particularmente en cuenta lo indicado en 71 en el diseño de procedimientos para aproxi-maciones por instrumentos que no sean de precisión destinados a ser utilizados con el GNSS que deberían también apoyar las SID y STAR.
Aviación general internacional
Ayudas de corta distancia
73.Deberían proporcionarse ayudas apropiadas, tales como el GNSS, para la navegación de corta distancia para servir a los aeródromos adicionales a que se refiere el párrafo 22, en los casos en que la densidad de tránsito y las condiciones meteorológicas lo justifiquen, teniendo debida-mente en cuenta el equipo de a bordo de las aeronaves. Estas ayudas deberían ubicarse, según convenga, de modo que permitan efectuar aproximaciones por instrumentos.
Ensayos en vuelo de las ayudas visuales
y no visuales para la navegación
74.Debería recomendarse que se hagan arreglos cooperativos para los ensayos en vuelo de las ayudas visuales y no visuales para la navegación (Anexo 10, Volumen I, Capítulo 2, 2.7) cuando sea imposible o antieconómico llevar a cabo nacionalmente los ensayos en vuelo.
VIGILANCIA
75.Los sistemas de vigilancia deberían proporcionar un apoyo adecuado a la ATM y satisfacer las necesidades de ésta. Se considera que una tabla de instalaciones y servicios radar, junto con la carta correspondiente, constituye un instrumento útil de planificación e implantación de los sistemas de vigilancia, incluso la vigilancia dependiente automática (ADS).
76.Deberían proporcionarse servicios de vigilancia como parte integrante del control de tránsito aéreo cuando sean viables y convenientes o cuando sean necesarios en interés de la seguridad, de la eficiencia y de la economía de las operaciones, particularmente en aquellas áreas donde la densidad de tránsito o la multiplicidad o complejidad de las rutas ATS ocasionen restricciones. El radar primario o secundario de vigilancia son sistemas que cabría utilizar para cumplir este requisito. Cuando la tecnología lo permita y a condición de mantenerse el nivel de seguridad requerido, la vigilancia dependiente automática (ADS) podría utilizarse en el espacio aéreo en que no se disponga de vigilancia mediante radar.
77.También debería preverse la utilización de sistemas de vigilancia para supervisar el tránsito aéreo e identificar las aeronaves civiles en zonas en que de otra forma podrían ser interceptadas.
Nota.— Este requisito no constituye una justificación ni un requisito operacional para la instalación de nuevos radares. Como las interceptaciones sólo se producirían normalmente bajo la existencia de un control radar militar, esto debería interpretarse como un requisito de que un Estado haga mejor uso de las medidas existentes y perfec-cione la coordinación civil/militar.
Las ayudas no visuales normalizadas de la OACI para la aproximación final y aterrizaje utilizadas en apoyo de las operaciones de aproximación y aterrizaje de precisión cumplirá con lo especificado en el Anexo 10 Volumen I 2.1 y su introducción y aplicación deberian estar de acorde con la estrategia contenida en el adjunto B del volumen I.

## Slide 7: CAR/SAM REGIONAL AIR NAVIGATION PLAN
INTERNATIONAL GENERAL AVIATION
THE APPROPRIATE AIDS, LIKE GNSS, SHOULD BE PROVIDED FOR SHORT-DISTANCE NAVIGATION
FLIGHT TESTING OF VISUAL AND NON-VISUAL NAVIGATION AIDS
ARRANGEMENTS FOR JOINT FLIGHT TESTING OF VISUAL AND NON-VISUAL AIDS SHOULD BE RECOMMENDED (ANNEX 10, VOLUME I, CHAPTER 2, 2.7) WHEN THE CONDUCTION OF SUCH TESTS AT NATIONAL LEVEL IS IMPOSSIBLE OR NON-ECONOMICAL
NAVIGATION SYSTEMS
PART I, BASIC ANP
BASIC OPERATIONAL REQUIREMENTS AND PLANNING CRITERIA (BORPC)
Notes: Ayudas de corta distancia
73.Deberían proporcionarse ayudas apropiadas, tales como el GNSS, para la navegación de corta distancia para servir a los aeródromos adicionales a que se refiere el párrafo 22, en los casos en que la densidad de tránsito y las condiciones meteorológicas lo justifiquen, teniendo debida-mente en cuenta el equipo de a bordo de las aeronaves. Estas ayudas deberían ubicarse, según convenga, de modo que permitan efectuar aproximaciones por instrumentos.

## Slide 8: CAR/SAM REGIONAL AIR NAVIGATION PLAN
NDB
AN NDB SHOULD BE IMPLEMENTED WHEREVER A VOR CANNOT BE PROVIDED
NDB GUIDELINES ARE SHOWN IN ANNEX 10, VOLUME I, ATTACHMENT C, SECTION 6
VOR
FOR VORs IMPLEMENTED IN THE CAR/SAM REGIONS FOR THE PROVISION OF SERVICES REQUIRED FOR FLIGHTS UP TO FL 450, A GEOGRAPHICAL SEPARATION OF 550 NM SHOULD BE APPLIED FOR THE ASSIGNMENT OF CO-CHANNEL FREQUENCIES, AND 220 NM FOR THE ASSIGNMENT OF ADJACENT CHANNEL FREQUENCIES.
WHERE THERE IS CONGESTION OF VOR FACILITIES, SERVICE VOLUME SHOULD BE REDUCED TO THE LEVEL ACTUALLY REQUIRED BY OPERATIONS. IN SUCH CASES, SERVICE VOLUME REDUCTION AND GEOGRAPHICAL SEPARATION SHALL BE AS FOLLOWS:
Type of facility | Airspace volume with frequency protection | Co-channel separation minima | Adjacent channel separation minima
Terminal | 25 NM (46 km) radius up to 12 000 ft (3 658 m) above mean sea level (MSL) | 130 NM (241 km) | 30 NM (56 km)
Low | 40 NM (74 km) radius up to 18 000 ft (5 486 m) MSL | 185 NM (343 km) | 50 NM (83 km)
High | 130 NM (241 km) radius up to 45 000 ft (13 716 m) MSL | 390 NM (722 km) | 150 NM (275 km)
NAVIGATION SYSTEMS
PART IV, BASIC ANP
RADIO NAVIGATION AID PLANNING PRINCIPLES

## Slide 9: CAR/SAM REGIONAL AIR NAVIGATION PLAN
FINAL APPROACH AND LANDING NON-VISUAL AIDS
GEOGRAPHICAL SEPARATION MINIMA BETWEEN ILS WOULD BE 175 NM FOR CO-CHANNEL, AND 45 NM FOR ADJACENT CHANNEL. GUIDELINES ON THIS MATTER ARE CONTAINED IN ANNEX 10, VOLUME I, ATTACHMENT C, 2.6.
DME
THE SAME GEOGRAPHICAL SEPARATION CRITERIA ESTABLISHED FOR VORs SHALL APPLY FOR MOST DME FACILITIES ASSOCIATED TO VORs. GUIDELINES ON THE GEOGRAPHICAL SEPARATION FOR DIFFERENT TYPES OF DMEs ARE CONTAINED IN ANNEX 10, VOLUME I, ATTACHMENT C, 7.1.7.
GUIDELINES FOR THE TRANSITION TO SATELLITE NAVIGATION SYSTEMS
PART IV, BASIC ANP
RADIO NAVIGATION AID PLANNING PRINCIPLES
NAVIGATION SYSTEMS

## Slide 10: CAR/SAM REGIONAL AIR NAVIGATION PLAN
PART IV,BASIC ANP
MAINTENANCE OF ICAO LIST COM 1, LIST OF FACILITIES OPERATING IN THE LF/MF FREQUENCY BAND (190-1 750 KHZ), AND ICAO LIST COM 2, REGISTRY OF VHF FREQUENCIES ASSIGNED TO VOR AND ILS RADIO NAVIGATION AIDS IN THE CARIBBEAN AND SOUTH AMERICA [CAR/SAM/3, Rec. 10/3]
FLIGHT TESTING OF RADIO NAVIGATION AIDS [CAR/SAM/3, Rec. 10/4]
a) DO THE UTMOST TO KEEP RADIO NAVIGATION AIDS PERMANENTLY OPERATIONAL;
b) CONDUCT PERIODIC FLIGHT TESTS OF RADIO NAVIGATION AIDS PURSUANT TO ANNEX 10, AT THE INTERVALS INDICATED IN ICAO DOC 8071; AND
C) SIGN BILATERAL OR MULTILATERAL AGREEMENTS TO SHARE FLIGHT TESTING CAPABILITIES.
SUSPENSION OF USE OF BAND 1 559 - 1 610 MHZ (ALLOCATED TO RNSS) BY FIXED SERVICES [CAR/SAM/3, Rec. 10/6]
NAVIGATION SYSTEMS
Notes: General
29.The aeronautical radio navigation plan comprises all facilities that provide navigation support to en-route, terminal, approach, landing and surface movement operations.
30.The growing number of modern aircraft equipped with area navigation (RNAV) and the increasing emphasis on required navigation performance (RNP) result in more flexible route selection and less dependence on any particular type of navigation system. Nevertheless, every single radio navigation facility must operate in strict conformance with the applicable standards.
31.It is foreseen that the provision of radio navigation services will gradually change from a ground-based to a satellite-based system. The global navigation satellite system (GNSS) is the generic term used for the satellite-based aeronautical radio navigation system. Existing and/or emerging navigation satellite constellations and their associated satellite-based, aircraft-based and ground-based augmentation systems (SBAS, ABAS and GBAS, respect-ively) all form elements of the GNSS.
Planning principles for radio navigation aids
[CAR/SAM/3, Rec. 10/1]
32.States, in planning the implementation of radio navigation services, should consider the principles shown in Attachment A.
Maintenance of ICAO COM List No. 1 List of
Facilities Operating on Frequencies in the LF/MF
Band (190  1 750 kHz) and ICAO COM List No. 2
Record of VHF Frequencies Assignments to
Caribbean and South American VOR and
ILS Radio Navigation Aids
[CAR/SAM/3, Rec. 10/3]
33.States:
a) in order to support the frequency management functions of the ICAO Regional Offices (including the publication of the COM Lists Nos. 1 and 2), should notify the relevant Regional Office of all changes to their frequency assignments; and
b) should release any assigned frequency which is not included in firm plans for operational use in the near future and notify accordingly the relevant ICAO Regional Office.
Flight testing of radio navigation aids
[CAR/SAM/3, Rec. 10/4]
34.States should:
a) make every effort to maintain their radio navigation aids operational at all times;
b) perform flight test of navigation aids periodically in accordance with Annex 10 requirements and at intervals indicated in ICAO Doc 8071; and
c) be encouraged to establish bilateral and/or multilateral agreements on sharing of flight test capabilities.
Termination of the use of the band 1 559  1 610 MHz
(allocated to the RNSS) by fixed services
[CAR/SAM/3, Rec. 10/6]
35.Considering the incompatibility of sharing of the band 1 559  1 610 MHz allocated to the RNSS with the fixed services, States should coordinate with the corres­ponding national frequency management authority in order to:
a) determine if any fixed service stations operate in the band 1 559  1 610 MHz and, if so, either cease their operation or relocate them to other fixed-service bands before GNSS‑based operations are approved; and
b) establish plans to avoid any future implementation of fixed service stations to operate in the band 1 559  1 610 MHz.
Navigation systems implementation
and regional timelines
36.It is intended to include regional timelines for navigation systems implementation when planning material is sufficiently mature.

## Slide 11: CAR/SAM REGIONAL AIR NAVIGATION PLAN
FASID
THIS PART CONTAINS INFORMATION ON THE FACILITIES AND SERVICES TO BE PROVIDED IN ORDER TO MEET THE BASIC REQUIREMENTS OF THE PLAN, AS AGREED UPON BETWEEN THE PROVIDER STATES AND THE USERS CONCERNED. SUCH AGREEMENT REFLECTS THE COMMITMENT OF THE STATES CONCERNED TO MEET SUCH REQUIREMENTS. GREPECAS, IN ACCORDANCE WITH ITS MANAGEMENT PROGRAMME, IS CONSTANTLY REVIEWING THIS ELEMENT OF THE FASID AND THE CAR/SAM ANP, IN CONSULTATION WITH USER AND PROVIDER STATES, AND WITH THE ASSISTANCE OF THE ICAO NORTH AMERICAN, CENTRAL AMERICAN, AND CARIBBEAN (NACC) AND SOUTH AMERICAN (SAM) OFFICES.
TABLE CNS 3 LISTS THE FACILITIES FOR RADIO AID SYSTEMS. THIS TABLE WAS AMENDED IN MID 2009. UPDATED INFORMATION ON THE TABLE MAY BE FOUND AT WWW.LIMA.ICAO.INT (DOCUMENTATION).

## Slide 12: CAR/SAM REGIONAL AIR NAVIGATION PLAN
RADIO AID SYSTEMS – FASID TABLE CNS 3

## Slide 13: AMENDMENTS TO NAVIGATION-RELATED SARPS
AMENDMENT 84 TO ANNEX 10, VOLUME I (NOVEMBER 2009)
UPDATES AND REORGANISES GENERAL INFORMATION ON RADIO AIDS
AMENDS OBSOLETE OR AMBIGUOUS INFORMATION ON ILS
AMENDS OBSOLETE OR AMBIGUOUS INFORMATION ON VORs
DELETES MATERIAL ON NDB TRIALS, WHICH DUPLICATED MATERIAL CONTAINED IN DOC 8071, MANUAL ON TESTING OF RADIO NAVIGATION AIDS
REFLECTS THE RESULT OF THE REVIEW OF DME ASPECTS IDENTIFIED IN RECOMMENDATIONS 6/14 AND 6/15 OF THE ELEVENTH AIR NAVIGATION CONFERENCE
UPDATES PRECISION STANDARDS IN LIGHT OF CURRENT DME PERFORMANCE, AND CLARIFIES AND SIMPLIFIES EXISTING MATERIAL
PROVIDES GUIDANCE ON POTENTIAL SAFETY ASPECTS IDENTIFIED DURING THE CAT III MLS CERTIFICATION PROCESS

## Slide 14: AMENDMENTS TO NAVIGATION-RELATED SARPS
AMENDMENT 85 TO ANNEX 10, VOLUME I (NOVEMBER 2010)
QUALITY IMPROVEMENTS IN THE ILS LOCATOR SIGNAL AT AERODROMES WHERE THE REFLECTION OF BUILDINGS AND LAND CAUSES THE REFLECTED SIGNAL TO INTERFERE WITH THE DESIRED SIGNAL
APPLICATION EXTENDED TO GNSS CAT I APPROACHES (“LPV 200”)
EVOLUTION OF GLONASS
AMENDMENT 86 TO ANNEX 10, VOLUME I (NOVEMBER 2011)
GBAS CHANGES BASED ON EXPERIENCE GAINED IN THE IMPLEMENTATION
GBAS CAT I TECHNIQUE THAT TAKES INTO ACCOUNT FUTURE COMPATIBILITY WITH EXISTING SYSTEMS

## Slide 15: AMENDMENTS TO NAVIGATION-RELATED SARPS
AMENDMENT 87 (EFFECTIVE NOVEMBER 2012)
CHANGES TO SIGNAL RECEPTION POWER REQUIREMENTS
INTRODUCTION OF TWO NEW SBAS PROVIDERS
CHANGES IN THE RUNWAY FIELD NUMBER IN THE FINAL APPROACH SEGMENT (FAS) OF THE DATA BLOCK
CHANGES IN GNSS POWER REQUIREMENTS
WORK IN PROGRESS IN THE NSP
DEVELOPMENT OF SARPS ON NEW CONSTELLATIONS/SIGNALS
DRAFTING OF DOCUMENTS FOR AN 12 (NAVIGATION ROADMAP)
MULTI-CONSTELLATION OPERATION
NEW EDITION OF DOC 9849
MAINTENANCE OF EXISTING SARPS ON CONVENTION RADIO AIDS
MAINTENANCE OF DOC 8071

## Slide 16: FREQUENCY BAND FOR THE RADIO NAVIGATION SERVICE
BAND | SERVICE | AERONAUTICAL USE | ICAO POLICY
130- 535KHZ | SRNA | NDB/Localizer | Aeronautical requirements in this band can decrease as GNSS is implemented Existing allocations must be protected until all NDBs are withdrawn Allocation of 15khz in part of the 415-526.5Khz band to serve radio hams on a secondary basis (CMR 2012 1.23 Agenda)
74.8-75.2Mhz | SRNA | Beacon | Eliminate international allocations No modifications to existing allocation
108-117.955Mhz | SRNA SRNA (R ) | VOR/ILS localizer GBAS VDL 4 | Eliminate international allocations No modifications to existing allocation Compatibility between FM broadcasting service and ILS/VOR , GBAS.
960-1215Mhz | SRNA RNS AMS(R ) | DME GNSS UAT | No modifications to existing allocation
1215-1400Mhz | SRL SRNS and SRNA | GNSS | No modifications to existing allocation

## Slide 17: FREQUENCY BAND FOR THE RADIO NAVIGATION SERVICE
BAND | SERVICE | AERONAUTICAL USE | ICAO POLICY
1559-1626.5 Mhz | SRNA SRNS SMS | GNSS | No modifications to the allocation to the radio navigation satellite service 1559-1610 Mhz No modifications in the use of the 1559 1610 Mhz band for future GNSS elements, including GLONASS and GPS, which must be protected No new allocations to be made in the 1559-1610Mhz band Delete notes
4200-4400Mhz | SRNA | Radio altimeter | No modifications in the allocation to the radio navigation satellite service
5000 5250 Mhz | SRNA | MLS | 

## Slide 18: NAVIGATION ASPECTS OF GREPECAS
CONCLUSI0N 12/45 – AMENDMENT TO THE “REGIONAL GUIDELINES FOR THE TRANSITION TO NAVIGATION SATELLITE SYSTEMS (GNSS)” AND TO THE “REGIONAL STRATEGY FOR THE INTRODUCTION AND APPLICATION OF NON-VISUAL AIDS TO APPROACH, LANDING AND DEPARTURE”
THAT:
A) CAR/SAM STATES/TERRITORIES/INTERNATIONAL ORGANIZATIONS TAKE INTO ACCOUNT THE NEW “REGIONAL GUIDELINES FOR THE TRANSITION TO NAVIGATION SATELLITE SYSTEMS (GNSS)” AND THE “REGIONAL STRATEGY FOR THE INTRODUCTION AND APPLICATION OF NON-VISUAL AIDS TO APPROACH, LANDING AND DEPARTURE”,
B) ICAO AMEND ATTACHMENTS H AND I TO PART IV OF VOLUME I, BASIC ANP (DOC 8733) IN CONFORMITY WITH THE AFOREMENTIONED NEW GUIDELINES AND STRATEGY.

## Slide 19: NAVIGATION ASPECTS OF GREPECAS

## Slide 20: NAVIGATION ASPECTS OF GREPECAS
GUIDELINES FOR THE TRANSITION TO NAVIGATION SATELLITE SYSTEMS IN THE CAR/SAM REGIONS
WHEN PLANNING THE TRANSITION TO THE GNSS, THE FOLLOWING ITEMS SHOULD BE TAKEN INTO ACCOUNT :
MAINTAIN OR IMPROVE THE EXISTING LEVEL OF SAFETY
PROGRAMME THE PROVISION OR ADOPTION OF A GNSS SERVICE, INCLUDING AIRCRAFT AND OPERATOR APPROVAL PROCESSES
SCOPE OF EXISTING GROUND-BASED RADIO NAVIGATION SERVICES
STRATEGY OF THE PLAN FOR THE TRANSITION TO GNSS FUNCTIONS (i.e., BENEFIT-DRIVEN OR MANDATORY)
APPROPRIATE LEVEL OF GNSS CAPABILITY AMONGST USERS
PROVISION OF OTHER AIR TRAFFIC SERVICES (i.e., SURVEILLANCE AND COMMUNICATIONS)
TRAFFIC DENSITY AND FREQUENCY OF OPERATIONS
MITIGATION OF RISKS CAUSED BY RADIO FREQUENCY INTERFERENCE AND IONOSPHERE ISSUES

## Slide 21: NAVIGATION ASPECTS OF GREPECAS
STRATEGY FOR THE INTRODUCTION AND USE OF NON-VISUAL AIDS FOR APPROACH, LANDING AND DEPARTURE IN THE CAR/SAM REGIONS
CONTINUE CONDUCTING ILS OPERATIONS WITH THE HIGHEST LEVEL OF SERVICE, PROVIDED THEY ARE OPERATIONALLY ACCEPTABLE AND COST-EFFECTIVE, TRYING NOT TO DENY AIRPORT ACCESS TO AIRCRAFT ONLY EQUIPPED WITH ILS
IMPLEMENT GNSS WITH AUGMENTATION FOR APV AND CAT I OPERATIONS IF OPERATIONALLY REQUIRED AND COST-EFFECTIVE
ENCOURAGE THE DEVELOPMENT AND USE OF A MULTIMODAL ON-BOARD LANDING CAPACITY
DEVELOP AND USE A MULTIMODAL ON-BOARD LANDING CAPACITY
PROMOTE THE IMPLEMENTATION OF APV OPERATIONS, ESPECIALLY WITH GNSS VERTICAL GUIDANCE, TO IMPROVE SAFETY AND ACCESS
IDENTIFY AND RESOLVE OPERATIONAL AND TECHNICAL FEASIBILITY ISSUES RELATED TO THE GNSS WITH GROUND-BASED AUGMENTATION SYSTEMS (GBAS) AND SUPPORT CAT II AND II OPERATIONS. IMPLEMENT GNSS FOR CAT II AND III OPERATIONS IF OPERATIONALLY REQUIRED AND COST-EFFECTIVE

## Slide 22: NAVIGATION ASPECTS OF GREPECAS
PHASING-OUT OF NDB STATIONS
CONCLUSION 14/56 – PHASING-OUT OF NDB STATIONS
THAT, IN ORDER TO DEVELOP A PLAN FOR PHASING-OUT NDB STATIONS WITHOUT AFFECTING SAFETY, THE STATES, TERRITORIES, INTERNATIONAL ORGANISATIONS AND AIRSPACE USERS:
ANALYSE THE SERVICE PROVIDED BY EACH NDB STATION, ITS FUNCTION, EXISTENCE OF PROCEDURES WITH OTHER AIDS SUCH AS VOR/DME, GNSS-RNAV, AS WELL AS THE CAPACITY/DEVELOPMENT OF AIRCRAFT OPERATING IN THE SERVICED AIRSPACE
DEVELOP A PLAN FOR THE PHASING-OUT OF NDB STATIONS
INTRODUCTION OF ABAS TABLE CNS 3
CONCLUSION 15/41 – AMENDMENT OFTHE REGIONAL AIR NAVIGATION PLAN – FASID TABLE CNS/3
THAT ICAO CONSIDER AMENDING THE FORMAT OF FASID TABLE CNS 3 OF THE REGIONAL AIR NAVIGATION PLAN, ADDING A NEW COLUMN UNDER GNSS REQUIREMENTS TO REFLECT THE PLANNING OF ABAS REQUIREMENTS.

## Slide 23: NAVIGATION ASPECTS OF GREPECAS
EVOLUTION OF AIR NAVIGATION INFRASTRUCTURE
SHORT TERM (UP TO 2010)
INITIAL DEACTIVATION OF NDBs
DEFINITION OF GNSS BACKUP INFRASTRUCTURE
MODIFICATION OF DME INFRASTRUCTURE TO MEET ICAO RNAV (DME/DME) REQUIREMENTS IN SELECTED TMAs
INITIAL IMPLEMENTATION OF ABAS FOR EN-ROUTE, TMA AND NPA OPERATIONS
MEDIUM TERM (2011-2015)
IMPLEMENTATION OF CAT I GBAS STATIONS AT AIRPORTS WITH SUFFICIENT OPERATIONAL DEMAND TO IMPROVE EN-ROUTE AND TMA OPERATIONS (SIDs AND STARs) ON ILS-LIKE PATHS
AT SOME AIRPORTS, ILS SYSTEMS WILL BE KEPT AS BACKUP FOR GNSS/GBAS
INITIAL DEACTIVATION OF VORs FOR EN-ROUTE OPERATIONS

## Slide 24: NAVIGATION ASPECTS OF GREPECAS
LONG TERM (2016-2025)
CONTINUE DEACTIVATION OF CONVENTIONAL AIDS, MAINTAINING THE BACKUP STRUCTURE, IF NECESSARY
IMPLEMENTATION OF CAT II/III GBAS AT SELECTED AIRPORTS
        IMPLEMENTATION OF CAT I GBAS-BASED APPROACHES AT OTHER AIRPORTS IN THE CAR/SAM REGIONS, AS WARRANTED BY OPERATIONAL DEMAND
        POSSIBLE IMPLEMENTATION OF SBAS, DEPENDING ON FEASIBILITY STUDIES CONDUCTED AND BEING CONDUCTED BY ICAO PROJECTS, TAKING INTO ACCOUNT EXISTING SINGLE-FREQUENCY SYSTEMS, THE EVOLUTION OF IONOSPHERE ALGORITHMS, AND THE FUTURE AVAILABILITY OF THE MULTI-FREQUENCY AND MULTI-CONSTELLATION SATELLITE STRUCTURE
EVOLUTION OF AIR NAVIGATION INFRASTRUCTURE

## Slide 25: NAVIGATION ASPECTS OF GREPECAS
Notes: Con el fin de alinear el GREPECAS a los objetivos estratégicos de la OACI , el Plan Mundial de Navegación Aerea , el Concepto Operacional ATM y Planes regionales de implantación de la navegación aérea basados en la performance para las Regiones CAR y SAM se ha considerado necesario
aumentar su efectividad, mejorar su eficiencia , mejorar la coordinación entre los diferentes órganos del GREPECAS, incrementar la participación y responsabilidad de los Estados, reducir los costos y trabajar bajo la metodología de gestión de proyecto .
Por tal motivo GREPECAS 16 a través de las Decisión 16/45 y 16/47 modifica la Organización del GREPECAS fundamentándola en una organización basada en programa y proyecto y eliminado los Subgrupos .

## Slide 26: NAVIGATION ASPECTS OF GREPECAS
PROJECT: AIR NAVIGATION SYSTEM IN SUPPORT OF PBN IN THE SAM REGION

## Slide 27: IMPLEMENTATION OF AIR NAVIGATION SYSTEMS IN THE SAM REGION
ATM/SAR
CNS
AIS
AGA
MET
SAM/IG MEETINGS
RLA/06/901

## Slide 28: IMPLEMENTATION OF AIR NAVIGATION SYSTEMS IN THE SAM REGION
Performance-based navigation (PBN)
Air traffic flow management (ATFM)
ATS automation
Improvement of CNS systems

## Slide 29: IMPLEMENTATION OF AIR NAVIGATION SYSTEMS IN THE SAM REGION
PLAN FOR THE IMPLEMENTATION OF PERFORMANCE-BASED AIR NAVIGATION IN THE SAM REGION
CURRENT SITUATION
RADIO AIDS: ALL CONVENTIONAL RADIO NAVIGATION AID SYSTEMS (NDB, VOR, DME AND ILS) HAVE BEEN FULLY IMPLEMENTED AND INSTALLED AS SPECIFIED IN TABLE CNS 3 (TABLE OF RADIO NAVIGATION AIDS). WITH REGARD TO NDBs, A DEACTIVATION PROCESS IS UNDER WAY, STARTING WITH THOSE STATIONS WHERE THE NDB IS INSTALLED NEXT TO A VOR/DME
THE USE OF ABAS FOR EN-ROUTE, TERMINAL AREA AND NPA OPERATIONS HAS STARTED IN SELECTED AIRSPACES

## Slide 30: IMPLEMENTATION OF AIR NAVIGATION SYSTEMS IN THE SAM REGION
PLAN FOR THE IMPLEMENTATION OF PERFORMANCE-BASED AIR NAVIGATION IN THE SAM REGION
IMPROVEMENTS TO NAVIGATION SYSTEMS (2012 - 2018)
STATES MUST CONTINUE WITH THE NDB DEACTIVATION PLAN AS DEFINED BY GREPECAS/14 (APRIL 2007). IT IS FORESEEN THAT MOST NDBs WILL BE DEACTIVATED AS SCHEDULED
VOR/DME: IT IS FELT THAT, AS PART OF THE TRANSITION TO GNSS, VOR/DME SYSTEMS SHOULD BE KEPT IN SELECTED TMAs, AND THAT EN-ROUTE VOR SYSTEMS SHOULD START BEING PHASED OUT
DME/DME: TAKING INTO ACCOUNT THE IMPLEMENTATION OF PBN EN-ROUTE AND IN TMAs, AND THE USE OF DME/DME NAVIGATION TO SUPPORT GNSS, STATES MUST MAINTAIN THE EXISTING DME COVERAGE AND, IF NECESSARY, CONDUCT STUDIES TO EXTEND COVERAGE IN SELECTED AIRSPACES

## Slide 31: IMPLEMENTATION OF AIR NAVIGATION SYSTEMS IN THE SAM REGION
ILS: IT IS FORESEEN THAT ILS SYSTEMS WILL REMAIN OPERATIONAL DURING THE RESPECTIVE PLANNING PERIOD
GBAS CAT I: WILL START AT AIRPORTS WHERE WARRANTED BY OPERATIONAL DEMAND
FLIGHT TESTING SUPPORT SYSTEMS: STATES MUST CONSIDER MODERNISING THEIR FLIGHT AND GROUND RADIO NAVIGATION AID TESTING ELEMENTS, INCLUDING RADIO NAVIGATION SATELLITE SYSTEMS (GNSS), SO AS TO BE READY FOR A PBN ENVIRONMENT
PROTECTION OF THE RADIO FREQUENCY SPECTRUM: STATES MUST STRIVE TO ENSURE THE PROTECTION AND PROPER USE OF THE RADIO FREQUENCY SPECTRUM ASSIGNED TO AVIATION FOR RADIO NAVIGATION SERVICES
PLAN FOR THE IMPLEMENTATION OF PERFORMANCE-BASED AIR NAVIGATION IN THE SAM REGION

## Slide 32: IMPLEMENTATION OF AIR NAVIGATION SYSTEMS IN THE SAM REGION
PLAN FOR THE IMPLEMENTATION OF PERFORMANCE-BASED AIR NAVIGATION IN THE SAM REGION

## Slide 33: CONCLUSIONS
THE STATES OF THE REGION, WHEN IMPLEMENTING THEIR NAVIGATION SYSTEMS, SHOULD TAKE INTO ACCOUNT:
THE BASIC OPERATIONAL REQUIREMENTS AND PLANNING CRITERIA (BORPC) (Doc 8733, Volume I, Part I)
THE AERONAUTICAL RADIO NAVIGATION AID PLANNING PRINCIPLES (Doc 8733, Volume I, Part IV)
THE RADIO AID PLAN (FASID TABLE CNS 3, Doc 8733, Volume II)
ICAO LISTS COM 1 AND COM 2
ICAO SARPS AND DOCUMENTS
THE STRATEGY FOR THE EVOLUTION OF AIR NAVIGATION SYSTEMS IN THE CAR/SAM REGIONS
PLAN FOR THE IMPLEMENTATION OF THE PERFORMANCE-BASED AIR NAVIGATION SYSTEM IN THE SAM REGION
THEIR ACTIVE PARTICIPATION IN ICAO REGIONAL EVENTS (SAM/IG MEETINGS, COURSES, SEMINARS/WORKSHOPS)