## Slide 1: SESSION 2 TESTING OF RADIO NAVIGATION AIDS AND INSTRUMENT FLIGHT PROCEDURES
STATUS OF ICAO DOC 8071 - MANUAL ON TESTING OF RADIO NAVIGATION AIDS
ONOFRIO SMARRELLI
REGIONAL CNS SPECIALIST
ICAO SOUTH AMERICAN REGIONAL OFFICE
LIMA PERU
OSMARRELLI@LIMA.ICAO.INT
Phone 511 6118686

## Slide 2: CONTENTS
OBJECTIVE
ICAO STANDARDS AND RECOMMENDATIONS
TESTING OF RADIO NAVIGATION SATELLITE SYSTEMS
INTERFERENCE WITH NAVIGATION SYSTEMS AND MITIGATION
PROPOSALS OF AMENDMENT TO DOC 8071
IN-FLIGHT VALIDATION OF PROCEDURES
CONCLUSIONS

## Slide 3: OBJECTIVE
THIS PRESENTATION IS AIMED AT PRESENTING RELEVANT ASPECTS OF DOC 8071, MANUAL ON TESTING OF RADIO NAVIGATION AIDS, MAINLY WITH RESPECT TO FLIGHT TESTING OF RADIO NAVIGATION SATELLITE SYSTEMS AND INSTRUMENT FLIGHT PROCEDURES, AND THE CHANGES FORESEEN IN ICAO DOC 8071.

## Slide 4: ICAO STANDARDS AND RECOMMENDATIONS
ANNEX 10, VOLUME I, CHAPTER 2, SECTION 2.7 STATES THAT RADIO NAVIGATION AIDS OF THE TYPES SPECIFIED IN CHAPTER 3 OF ANNEX 10, VOLUME I AND THAT CAN BE USED BY AIRCRAFT INTENDED FOR INTERNATIONAL AIR NAVIGATION WILL BE SUBJECT TO PERIODIC GROUND AND FLIGHT TESTING.
ICAO GUIDELINES ON GROUND AND FLIGHT TESTING OF FACILITIES STANDARDISED BY ICAO AND ON THE FREQUENCY OF SUCH TESTS ARE CONTAINED IN ATTACHMENT C TO ANNEX 10, VOLUME I, AND IN DOC 8071, MANUAL ON TESTING OF RADIO NAVIGATION AIDS

## Slide 5: ICAO STANDARDS AND RECOMMENDATIONS
PURSUANT TO RECOMMENDATION 10/4 OF THE CAR/SAM/3 MEETING, VOLUME I (BASIC ANP) OF THE CAR/SAM AIR NAVIGATION PLAN STIPULATES THAT STATES SHOULD:
MAKE EVERY EFFORT TO KEEP THEIR RADIO NAVIGATION AIDS OPERATIONAL AT ALL TIMES;
CONDUCT FLIGHT TESTS OF NAVIGATION AIDS PERIODICALLY IN ACCORDANCE WITH ANNEX 10 REQUIREMENTS AND AT THE INTERVALS INDICATED IN ICAO DOC 8071; AND
BE ENCOURAGED TO ENTER INTO BILATERAL AND/OR MULTILATERAL AGREEMENTS FOR SHARING FLIGHT TEST CAPABILITIES.

## Slide 6: ICAO STANDARDS AND RECOMMENDATIONS
ICAO DOC 8071 CONTAINS INFORMATION ON MEASURING PRACTICES AND SPECIAL TESTING EQUIPMENT.
SYSTEMS ARE NORMALLY TESTED AS PART OF THE ACTIVITIES RELATED TO:
THE DESIGN AND DEVELOPMENT PRIOR TO MASS PRODUCTION (CERTIFICATION)
SPECIFIC FACILITIES IN EACH LOCATION AND ACCEPTANCE TESTS(COMMISSIONING)
THE PERIODIC OPERATIONAL ASSESSMENT OF THE RADIO NAVIGATION AID (MAINTENANCE)

## Slide 7: ICAO STANDARDS AND RECOMMENDATIONS
CURRENTLY, DOC 8071 HAS THREE VOLUMES
VOLUME I : TESTING OF GROUND-BASED RADIO NAVIGATION SYSTEMS (Fourth edition, 2000, last amendment 31/10/02)
VOLUME II : TESTING OF SATELLITE-BASED RADIO NAVIGATION SYSTEMS (Fifth edition, 2007 , Corrigendum 30/4/2008)
VOLUME III : TESTING OF SURVEILLANCE RADAR SYSTEMS (Fifth edition, 1998 Amendments 09 /10/ 2002 and 31/12/06 )
Available in electronic version on the ICAO NET; in the electronic version, only Volume II is available in Spanish; in the printed version, the three volumes are available in Spanish.
Notes: Colocar caratulas de los tres volumenes

## Slide 8: ICAO STANDARDS AND RECOMMENDATIONS
DOC 8071 DEFINES THE TERMS “TESTING”, “INSPECTION”, AND “VALIDATION” AS FOLLOWS:
TESTING: A SPECIFIC MEASUREMENT OR CHECK OF FACILITY PERFORMANCE THAT MAY FORM A PART OF AN INSPECTION WHEN INTEGRATED WITH OTHER TESTS.
INSPECTION: A SERIES OF TESTS CARRIED OUT BY A STATE AUTHORITY OR AN ORGANISATION AS AUTHORISED BY THE STATE TO ESTABLISH THE OPERATIONAL CLASSIFICATION OF THE FACILITY.
VALIDATION: INCLUDES A CHECK OF ALL NAVIGATION AND OBSTACLE DATA, A CHECK OF THE REQUIRED INFRASTRUCTURE, A CHART ASSESSMENT, AND THE POSSIBILITY OF FLYING THE PROCEDURE.

## Slide 9: TESTING OF RADIO NAVIGATION SATELLITE SYSTEMS
THE STATE OR THE DESIGNATED AUTHORITY THAT PROVIDES THE SERVICE IS RESPONSIBLE FOR THE FUNCTIONING OF THE ELEMENTS OF SATELLITE-BASED NAVIGATION SYSTEMS, SUCH AS THE GLOBAL POSITIONING SYSTEM (GPS) OR THE GLOBAL NAVIGATION SATELLITE SYSTEM (GLONASS).
NORMALLY, THESE ELEMENTS ARE NOT TESTED AS A PART OF GROUND OR FLIGHT TESTING OF A GIVEN PROCEDURE. AN EXCEPTION IS WHEN CONFIRMING THAT THE SPECTRUM IS FREE OF HARMFUL INTERFERENCE.
SATELLITE-BASED AUGMENTATION SYSTEMS (SBAS) AND THE GROUND-BASED AUGMENTATION SYSTEM (GBAS) ARE CHECKED WHEN SARPS STIPULATE A GIVEN PERFORMANCE. IN THIS REGARD, DOC 8071 DESCRIBES THE APPROPRIATE GROUND AND FLIGHT TESTS.
REGARDING TESTING OF THE AIRCRAFT-BASED AUGMENTATION SYSTEM (ABAS), DOC 8071 ONLY CONTEMPLATES TESTING OF ABAS-BASED PROCEDURES AND NOT TESTING OF THAT SYSTEM, SINCE THE LATTER IS SUBJECT TO AIRWORTHINESS CERTIFICATION.

## Slide 10: TESTING OF SATELLITE-BASED RADIO NAVIGATION SYSTEMS
FLIGHT INSPECTION OF THE GNSS DIFERS FROM AN ORDINARY INSPECTION OF RADIO NAVIGATION AIDS IN THAT THE INTENTION IS NOT TO CHECK THE ACCURACY OF THE UNMODULATED SIGNALS FROM THE SATELLITES.
IT IS MORE FOCUSED ON CHECKING THE ASSOCIATED PROCEDURES AND THE RADIO ENVIRONMENT IN WHICH NAVIGATION SIGNALS ARE RECEIVED.
THE ONLY EXCEPTION IS GBAS, WHERE AUGMENTATION SIGNAL COVERAGE IS CHECKED USING PROCEDURES SIMILAR TO THOSE USED FOR GROUND NAVIGATION AIDS.

## Slide 11: TESTING OF SATELLITE-BASED RADIO NAVIGATION SYSTEMS
PARAMETER | ANNEX 10, VOLUME I, REFERENCE | TEST
PROCEDURE DESIGN | (NONE) | F, G
INTERFERENCE | CHAPTER 3, 3.7.4 | F
SUMMARY OF REQUIREMENTS FOR TESTING
ABAS PROCEDURES

## Slide 12: TESTING OF SATELLITE-BASED RADIO NAVIGATION SYSTEMS
PARAMETER | ANNEX 10, VOLUME I, REFERENCE | DOC 8071, REFERENCE | MAGNITUDE MEASURED | TOLERANCE | UNCER-TAINTY | PERIODICITY
PROCEDURE DESIGN VALIDATION (ALL SEGMENTS) | NONE | SECTION 5 PAR. 5.3 |  |  |  | C COMMISSIONING
MAPT LOCATION AS PER THE GNSS | NONE | SECTION2 PAR. 2.3.5 SECTION 5 5.3.21 | DEVIATION | VISUAL CHECK | SUBJECTIVE | C COMMISSIONING SP ESPECIAL
INTERFERENCE | CHAPTER 3, PAR 3.7.4 | SECTION 2 PAR. 2.3.4 | RAIM ALERTS GUIDANCE INDICATION | NONE GUIDANCE ALERT CONTINUOUS | NONE | C COMMISSIONING SP ESPECIAL
GUIDANCE INDICATIONS | NONE | SECTION 2 PAR. 2.3.5 | NAV. INDICATOR | CONTINUOUS | NONE | C COMMISSIONING SP ESPECIAL
FLIGHT STATUS | NONE | SECTION 2 PAR. 2.3.5 SECTION 5 5.3.20 |  | APPROPRIATE | NONE | C COMMISSIONING SP ESPECIAL
SUMMARY OF MINIMUM REQUIREMENTS FOR FLIGHT TESTING OF ABAS PROCEDURES

## Slide 13: TESTING OF SATELLITE-BASED RADIO NAVIGATION SYSTEMS
PARAMETER | ANNEX 10, VOLUME I, REFERENCE | TEST
ACCURACY OF SURVEY DATA IN THE FAS | B 3.6.7.2.4.2 G | G
PROCEDURE DESIGN |  | F
INTERFERENCE |  | F
SUMMARY OF TESTING REQUIREMENTS — SBAS PROCEDURES

## Slide 14: TESTING OF SATELLITE-BASED RADIO NAVIGATION SYSTEMS
PARAMETER | ANNEX 10, VOLUME I, REFERENCE | TEST
Position accuracy (functional test) | 3.7.2.4.1 and Table 3.7.2.4-1 | F/G
Pseudo-range control accuracy | App. B 3.6.7.1.1 | G
Continuity (GBAS ground system) | App. B 3.6.7.1.3 | G
Integrity of the broadcasting signal in space Uncertainty of pseudo-range on the ground Tropospheric delay and residual tropospheric uncertainty GCID indication uncertainty Residual ionospheric uncertainty | App. B 3.6.7.2.2.4 App. B 3.6.7.2.3.1 App. B 3.6.7.2.3.2 App. B 3.6.7.2.3.5 | G G F/G G
Accuracy of the central phase position of the reference antenna | App. B 3.6.7.2.3.3 | G
Accuracy of FAS data points | App. B 3.6.7.2.4.1 | G
SUMMARY OF TESTING REQUIREMENTS — GBAS PROCEDURES, SYSTEM REQUIREMENTS

## Slide 15: TESTING OF SATELLITE-BASED RADIO NAVIGATION SYSTEMS
PARAMETER | ANNEX 10, VOLUME I, REFERENCE | TEST
INTEGRITY CONTROL OF GNSS RANGE MEASUREMENT SOURCES | App. B 3.6.7.2.6 | G
RESISTANCE TO INTERFERENCE (DISTANCE MEASURING SIGNAL) | App. B 3.7 | F/G
PROCEDURE VALIDATION (NONE) |  | F
SUMMARY OF TESTING REQUIREMENTS — GBAS PROCEDURES – SYSTEM REQUIREMENTS

## Slide 16: TESTING OF SATELLITE-BASED RADIO NAVIGATION SYSTEMS
PARAMETER | ANNEX 10, VOLUME I, REFERENCE | TEST
COVERAGE OF RUNWAY SURFACE (RECOMMENDATION) | 3.7.3.5.3.2 G | G
MESSAGE BLOCK HEADER (ONLY FOR GBAS IDENTIFICATION) | App. B 3.6.3.4.1 G | G
DATA CONTENTS | App. B 3.6.4 F/G | F/G
VDB COVERAGE GBAS/H FIELD STRENGTH GBAS/E FIELD STRENGTH (INCLUDES PHASE SHIFT) | 3.7.3.5.4.4 F | F
CARRIER FREQUENCY (ASSIGNED CHANNEL) | 3.7.3.5.4.1 G | G
CARRIER FREQUENCY STABILITY | App. B 3.6.2.1 G | G
SUMMARY OF TESTING REQUIREMENTS — GBAS PROCEDURES –
VHF DATA BROADCASTING SUBSYSTEM

## Slide 17: TESTING OF SATELLITE-BASED RADIO NAVIGATION SYSTEMS
PARAMETER | ANNEX 10, VOLUME I, REFERENCE | TEST
SURVEILLANCE -- TDMA INTERVAL SURVEILLANCE VDB TRANSMITTER POWER CONTROL | App. B 3.6.7.3 App. B 3.6.7.3.1.2 App. B 3.6.7.3.1.3 | G G
SQUITTER | 3.7.3.5.4.6 | G
POWER IN ADJACENT CHANNELS | 3.7.3.5.4.5 | G
SUMMARY OF TESTING REQUIREMENTS — GBAS PROCEDURES –
VHF DATA BROADCASTING SUBSYSTEM

## Slide 18: INTERFERENCE – NAVIGATION AND MITIGATION SYSTEMS
SOME SOURCES OF INTERFERENCE FOR AERONAUTICAL RADIO NAVIGATION SYSTEMS
AND MITIGATION TECHNIQUES
BAND ASSIGNED TO AERONAUTICAL RADIO NAVIGATION | BANDS ADJACENT TO THOSE ASSIGNED TO AERONAUTICAL RADIO NAVIGATION | MITIGATION TECHNIQUES
OPERATIONS OF THE PRIMARY AND SECONDARY AERONAUTICAL FIXED SERVICE IN THE BAND ASSIGNED TO THE GPS , GLONASS | FM BROADCAST TX | REGULATORY TECHNIQUES
TX MALFUNCTION | TV BROADCAST TX | INS COUPLING
FREQUENCY COORDINATION PROBLEMS | GROUND MOBILE TX | ADJUSTABLE ANTENNAE AND ADJUSTABLE SLOT RESPONSE FILTERS
USE OF RF GENERATORS WHEN TESTING AVIONICS | CABLE TV DISTRIBUTION SYSTEMS | CELL PROTECTION AND LOCATION OF ANTENNAE
 | ICM SYSTEMS | FM BROADCAST AND GBAS COMPATIBILITY ISSUES
 | POWER LINE DISTRIBUTION SYSTEMS | FLIGHT INSPECTION OF GNSS APPROACHES WITH RESPECT TO INTERFERENCE, COMBINED WITH THE USE OF GROUND-BASED SURVEILLANCE AND TIMELY SUPPLY OF STATUS NFORMATION TO ATC TO PROTECT GNSS USERS

## Slide 19: EXPECTED AMENDMENTS TO DOC 8071
Notes: The CNTSG Rapporteur reported on the activities of the CNTSG related to Agenda Item 5. The report of the CNTSG meeting is provided as Attachment JE.
6.1.12 WP22, RESTRUCTURE OF DOC 8071, explained how CNTSG proposes to revise structure of Doc 8071. This was already discussed at previous meetings. Once the flight validation material is taken out of Volume 2, the amount of material remaining will be too small to justify a separate volume. Therefore, CNTSG proposes to integrate the existing Volumes 1 and 2 into a single volume. Chapter 1 will be reviewed by July, and a complete review through the entire document will be completed by the next WGW meeting. It was noted that VOR is no longer used for radial navigation only; it is now also used as an area positioning system along with DME. CNTSG needs to address this use, which is currently not considered in Doc 8071.
6.1.23 The Secretary requested that the original location of material moved from one part of the document to another be clearly indicated (e.g., via an editorial note to be removed later) in order to facilitate the task of the translators. Use of the Word change tracking feature is strongly discouraged when text is being moved because the end result is a messy documentmoved text would be redlined as new text, and would therefore that may have to be re-translated in its entirety, potentially resulting in a significant delay in the production of the document. Any changes inside the moved text that was moved sshould also be clearly indicated. In this case the Word change tracking feature is as good a mechanism as any othercould be used.

## Slide 20: EXPECTED AMENDMENTS TO DOC 8071
OTHER EXPECTED AMENDMENTS – WORK BY ICAO NSP AND ASP PANEL
A CHAPTER RESERVED FOR MLS
GENERAL REVIEW OF THE MATERIAL CONTAINED IN CHAPTER 1, VOLUME I
REVIEW OF MATERIAL ON VOR IN CHAPTER 2, VOLUME I
VOR AS LOCATION FOR POSITIONING PURPOSES IN RNAV NAVIGATION
REVIEW OF GBAS SARPS AND THE CORRESPONDING TESTS
DEVELOPMENT OF GUIDANCE MATERIAL ON FLIGHT TESTING OF ADS-B AND MULTILATERATION
Notes: The CNTSG Rapporteur reported on the activities of the CNTSG related to Agenda Item 5. The report of the CNTSG meeting is provided as Attachment JE.
6.1.12 WP22, RESTRUCTURE OF DOC 8071, explained how CNTSG proposes to revise structure of Doc 8071. This was already discussed at previous meetings. Once the flight validation material is taken out of Volume 2, the amount of material remaining will be too small to justify a separate volume. Therefore, CNTSG proposes to integrate the existing Volumes 1 and 2 into a single volume. Chapter 1 will be reviewed by July, and a complete review through the entire document will be completed by the next WGW meeting. It was noted that VOR is no longer used for radial navigation only; it is now also used as an area positioning system along with DME. CNTSG needs to address this use, which is currently not considered in Doc 8071.
6.1.23 The Secretary requested that the original location of material moved from one part of the document to another be clearly indicated (e.g., via an editorial note to be removed later) in order to facilitate the task of the translators. Use of the Word change tracking feature is strongly discouraged when text is being moved because the end result is a messy documentmoved text would be redlined as new text, and would therefore that may have to be re-translated in its entirety, potentially resulting in a significant delay in the production of the document. Any changes inside the moved text that was moved sshould also be clearly indicated. In this case the Word change tracking feature is as good a mechanism as any othercould be used.

## Slide 21: VALIDATION OF FLIGHT PROCEDURES
QUALITY ASSURANCE MANUAL FOR FLIGHT PROCEDURE DESIGN (DOC 9906)
CURRENTLY COMPRISING FOUR VOLUMES:
VOLUME 1 —FLIGHT PROCEDURE DESIGN QUALITY ASSURANCE SYSTEM;
VOLUME 2 — FLIGHT PROCEDURE DESIGNER TRAINING;
VOLUME 3 — FLIGHT PROCEDURE DESIGN SOFTWARE VALIDATION; AND
VOLUME 4 — FLIGHT PROCEDURES DESIGN CONSTRUCTION
VOLUME 1 — THE FLIGHT PROCEDURE DESIGN QUALITY ASSURANCE SYSTEM PROVIDES GUIDANCE FOR QUALITY ASSURANCE IN THE PROCEDURE DESIGN PROCESSES, SUCH AS PROCEDURE DESIGN DOCUMENTATION, VERIFICATION AND VALIDATION METHODS, AND GUIDELINES ABOUT THE ACQUISITION/PROCESSING OF SOURCE INFORMATION/DATA. IT ALSO PROVIDES A GENERIC FLOW CHART DIAGRAM FOR THE DESIGN AND THE IMPLEMENTATION OF FLIGHT PROCEDURES.
VOLUME 2 — THE FLIGHT PROCEDURE DESIGNER TRAINING PROVIDES GUIDANCE FOR THE ESTABLISHMENT OF FLIGHT PROCEDURE DESIGNER TRAINING. TRAINING IS THE STARTING POINT FOR ANY QUALITY ASSURANCE PROGRAMME. THIS VOLUME PROVIDES GUIDANCE FOR THE ESTABLISHMENT OF A TRAINING PROGRAMME.
VOLUME 3 — FLIGHT PROCEDURE DESIGN SOFTWARE VALIDATION, WHICH PROVIDES GUIDANCE FOR THE VALIDATION (NOT CERTIFICATION) OF PROCEDURE DESIGN TOOLS, NOTABLY WITH REGARD TO CRITERIA.
VOLUME 4 — FLIGHT PROCEDURES DESIGN CONSTRUCTION (TO BE INCORPORATED LATER).

## Slide 22: VALIDATION OF FLIGHT PROCEDURES
TWO NEW VOLUMES ARE BEING DEVELOPED TO SUPPLEMENT DOC 9906
VOLUME 5 VALIDATION OF INSTRUMENT FLIGHT PROCEDURES
THIS VOLUME PROVIDES A DETAILED DESCRIPTION OF THE PROCESS FOR THE VALIDATION OF INSTRUMENT FLIGHT PROCEDURES. THE VALIDATION PROCESS IS DIVIDED INTO GROUND AND FLIGHT VALIDATION. VALIDATION SEEKS TO ENSURE THE SAFETY, DATA PRECISION, AND INTEGRITY AND FLYABILITY OF THE ISTRUMENT FLIGHT PROCEDURE. THE PROCEDURE VALIDATION PROCESS APPLIES TO INSTRUMENT FLIGHT PROCEDURES FOR FIXED-WING AIRCRAFT AND HELICOPTERS
VOLUME 6 FLIGHT VALIDATION PILOT TRAINING AND EVALUATION
VOLUME 6 CONTAINS INFORMATION ON THE QUALIFICATIONS, TRAINING, AND GUIDELINES ABOUT THE SKILLS, KNOWLEDGE, AND ATTRIBUTES (SKA) TO BE CONSIDERED IN THE TRAINING AND EVALUATION OF FLIGHT VALIDATION PILOTS

## Slide 23: VALIDATION OF FLIGHT PROCEDURES
IN ORDER TO SUPPORT STATES IN THE CONDUCTION OF GROUND AND FLIGHT VALIDATION OF INSTRUMENT FLIGHT PROCEDURES IN THE SAM REGION, THE SAM IG/6 MEETING (Lima, Peru, 19 to 22 October 2010) REVIEWED THE PROPOSED ADVISORY CIRCULAR IDENTIFIED AS CA 91-012 FOR ITS ADOPTION IN THE REGION, WHICH PROVIDES GUIDANCE ABOUT SATELLITE-SUPPORTED VALIDATION OF INSTRUMENT FLIGHT PROCEDURES (IFP) INVOLVED IN PERFORMANCE-BASED NAVIGATION (PBN).
THE ADVISORY CIRCULAR DEFINES THE POLICY AND GUIDANCE FOR SATELLITE-BASED FLIGHT VALIDATION OF INSTRUMENT FLIGHT PROCEDURES (IFP) INVOLVED IN PERFORMANCE-BASED NAVIGATION (PBN).
IT ALSO DESCRIBES THE REQUIREMENTS FOR SIMULATOR AND OBSTACLE ASSESSMENTS TO BE PERFORMED PRIOR TO FV. THIS VALIDATION WILL BE CONDUCTED PRIOR TO THE PROMULGATION OF AN IFP IN THE AERONAUTICAL INFORMATION PUBLICATION (AIP) OF THE STATE.
THE CIRCULAR WAS DRAFTED WITH THE SUPPORT OF PROJECT RLA/99/901, REGIONAL SAFETY OVERSIGHT SERVICE (SRVOP).
THE FLIGHT VALIDATION PROCESS WOULD BE ADAPTED TO THE INITIAL CERTIFICATION AND THE PERIODIC QUALITY ASSURANCE PROGRAMME ESTABLISHED BY EACH STATE FOR INSTRUMENT FLIGHT PROCEDURES.
VALIDATION OF FLIGHT PROCEDURES IN THE SAM REGION
Notes: Para la elaboracion de esta circular se tomo como referencia el siguiente material :
Annex 6 Operation of aircraft
Annex 10 Aeronautical telecommunications
Volume I: Radio navigation aids
Doc. 9613 Performance-based navigation (PBN) manual
Doc. 8168 Aircraft operations
Volume I: Flight procedures
Volume II: Construction of visual and instrument flight procedures
Doc. 8071 – V 2 Testing of satellite-based radio navigations systems
FAA Notice 8260.67 Flight validation (FV) of satellite-based performance-based navigation (PBN) instrument flight procedures (IFP) – Current guidance and criteria

## Slide 24: VALIDATION OF FLIGHT PROCEDURES
PROCEDURE DESIGN
PROCEDURE DOCUMENTATION
SIMULATOR EVALUATION
POSITIVE SIMULATOR EVALUATION
GROUND AND AIR OBSTACLE EVALUATION
POSITIVE EVALUATION
FLIGHT EVALUATION
POSITIVE FLIGHT EVALUATION
EVALUATION REPORT
PROCEDURE IMPLEMENTATION
No
No
No
VALIDATION OF FLIGHT PROCEDURES IN THE SAM REGION
Notes: a) La validación es el último paso de control de calidad en el proceso de diseño de los procedimientos para la PBN. El propósito de la validación es la comprobación de todos los datos sobre obstáculos y de navegación, y la evaluación de la capacidad de vuelo del procedimiento. La validación normalmente consiste de la validación en tierra y en vuelo. Los procedimientos de la PBN que contengan datos sobre el tramo de aproximación final (FAS) requieren un sistema aprobado para validar los elementos de los datos del FAS para la alineación del curso, ángulo, altura de franqueamiento del umbral (TCH) y la verificación por redundancia cíclica (CRC).
b) Exactitud de los datos. Los IFP PBN, RNAV (GNSS), RNAV (RNP), basados en satélites requieren datos muy precisos, basados en el sistema geodésico mundial WGS-84. Esto requiere una integridad muy alta de todos los datos de levantamiento topográfico utilizada en el procedimiento de vuelo y la base de datos de navegación utilizada por los aviones. Es obligatorio que se mantenga un sistema adecuado de garantía de calidad que abarque todos los ámbitos de la recopilación de datos, elaboración, publicación y desarrollo de las bases de datos de navegación (Ref. Anexos 4, 11, 14 y 15 al Convenio sobre Aviación Civil Internacional). Los errores de entrada, especialmente en la casilla de datos FAS, pueden resultar en cambios significativos en la trayectoria de vuelo en relación a la pista. La validación debe garantizar el uso de datos correctos para un análisis válido del procedimiento de vuelo.
c) Validación en tierra (GV). La GV es una revisión de todo el paquete de procedimientos de vuelo por instrumentos por una persona entrenada en el diseño de procedimientos y con conocimientos adecuados de validación en vuelo. Su objetivo es identificar las desviaciones de los criterios y la documentación, y evaluar sobre el terreno en la medida de lo posible, los elementos que serán evaluados en la fase de validación de vuelo. Los temas identificados durante la fase de validación en tierra deben de abordarse antes de la fase de validación en vuelo. La GV puede incluir tanto una evaluación en el simulador de vuelo y la evaluación de obstáculos.
d) Validación en vuelo (FV). La FV de los procedimientos de vuelo por instrumentos debe llevarse a cabo como parte de la certificación inicial. Debe ser realizada por un piloto de validación/evaluador de vuelo calificado y con experiencia y autorizado de conformidad con esta circular de asesoramiento. Los objetivos de la FV son:
1) realizar una evaluación de la capacidad de vuelo para determinar que el procedimiento de vuelo puede realizarse de forma segura;
2) proporcionar la garantía final de que se ha obtenido el adecuado franqueamiento de obstáculos (mediante el Doc 8071 de OACI o documento equivalente);
3) verificar que todos los datos de navegación que se publicarán son correctos;
4) verificar que los elementos de los datos FAS proveen guía de navegación, como se designó, al umbral físico de la pista o al punto en el espacio requerido.
5) verificar que todas las infraestructuras necesarias, tales como las marcas de pista, iluminación, comunicaciones y las fuentes de navegación, estén en su lugar y operativas;
6) evaluar los otros factores operacionales, tales como la cartografía, infraestructura necesaria, visibilidad, etc.
Nota.- La validación en vuelo no debe confundirse con inspección en vuelo. La inspección en vuelo de los procedimientos de vuelo por instrumentos es necesaria para asegurar que las radios ayudas de navegación apoyan adecuadamente el procedimiento. La inspección en vuelo se lleva a cabo como parte del programa detallado en el Doc 8071 – Manual sobre ensayos de radioayudas para la navegación y es realizado por un inspector de vuelo calificado que utiliza una aeronave apropiadamente equipada.
e) Diagrama de Flujo del proceso de validación (véase la Figura A-1). El diagrama de flujo identifica que la FV es el paso final en el proceso de desarrollo de IFP PBN. Los objetivos primarios de la validación en vuelo es el de garantizar que la trayectoria lateral y vertical definida logre el objetivo del diseño, y que la base de datos funcione en vuelo como se ha previsto. La tripulación de vuelo de la FV anotará la existencia de cualquiera anomalía en relación con el procedimiento de vuelo, el funcionamiento del sistema de gestión de vuelo (FMS), obstrucciones, comunicaciones, vigilancia, infraestructura aeroportuaria, etc. Las evaluaciones de obstáculos, como se indica en el Doc. 8071 pueden ser completadas antes o después de la evaluación en simulador. Esta sección describe el proceso de la FV, así como los eventos, que debe ocurrir antes de la FV. Los proveedores de servicios que conducen el desarrollo y/o la validación en vuelo del IFP deben tener un sistema aprobado por la AAC para evaluar y confirmar que la integridad de los datos del FAS; la alineación del curso, la altura de cruce del umbral, y ángulo de trayectoria de planeo están proporcionando orientación para la navegación, tal como está contemplado, al umbral físico de la pista o a un punto en el espacio.

## Slide 25: VALIDATION OF FLIGHT PROCEDURES
VALIDATION REGISTRATION
VALIDATION OF FLIGHT PROCEDURES IN THE SAM REGION
ORIGINAL FORM AC 91-012B (SEE APPENDIX 1) SIGNED AND COMPLETED.
ORIGINAL FORM AC 91-012C (SEE APPENDIX 1) SIGNED AND COMPLETED.
PROVIDE THE CAA WITH THE ELECTRONIC AGRS FILE OF BOTH THE OBSTACLE EVALUATION AND THE FLIGHT VALIDATION. SUBMIT THE REPORT, TOGETHER WITH THE PROCEDURE PACKAGE. THE REPORT MUST CONTAIN, AT LEAST, THE FOLLOWING ELEMENTS:
DATE AND TIME OF PROCESSING;
MAXIMUM NUMBER OF SATELLITES;
MINIMUM NUMBER OF SATELLITES;
AVERAGE POSITION DILUTION OF PRECISION (PDOP);
FOR EACH SEGMENT, MAXIMUM AND MINIMUM ALTITUDE, GROUND SPEED, RATE OF CLIMB, AND GRADIENT OF CLIMB
SUFFICIENTLY DETAILED PRINTED GRAPHS SHOWING THE PATH FLOWN IN
REFERENCE TO THE DESIRED PATH OF THE APPROACH PROCEDURE, INCLUDING PROCEDURE FIXES.

## Slide 26: VALIDATION OF FLIGHT PROCEDURES
CIVIL AVIATION ADMINISTRATION SIMULATOR EVALUATION |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1-DATE |  |  |  |  |  |  |  | 3-ORGANISATION |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 5-TYPE OF AIRCRAFT |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
7-PROCEDURE |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 9-FMS/SOFTWARE |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
10-PIC NAME/PHONE NO. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 11-NAME/PHONE NO. OF EVALUATOR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | SIMULATOR ASSESSMENT TASKS |  |  |  |  |  |  |  |  |  |  |  | YES |  |  |  | NO |  |  |  |  |  |  |  |  |  | LIST OF GRAPHS |  |  |  |  |  |  |  |  | YES |  |  | NO |  |  |  |  | 
 |  | 13-FMC NAV DATA AND ORIGIN COMPARISON |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 23-CHART HAS SUFFICIENT DETAILS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 15-PROCEDURE AT 100' BELOW THE DA/MDA |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 24-RNP <1.0 IN MISSED APPROACH |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 16-RECORD AND KEEP SIMULATION DATA |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 25- RF SEGMENT NOTES |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 17- PROCEDURE FASTER/SLOWER THAN IN THE CHART |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 27-NON-STANDARD CLIMB RATE |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 28- FLYABILITY |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 29-LIMIT TEMPERATURE NOTES |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 31-AIRCRAFT SIZE NOTES |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 33- TRACKS CONSISTENT WITH THE CHART |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SEGMENT VERIFICATION |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  | FEEDER |  |  |  |  |  |  |  | INITIAL |  |  |  |  |  |  | INTERMEDIATE |  |  |  |  |  | FINAL |  |  |  |  |  |  |  | MISSED |  |  |  |  | HOLDING |  |  |  |  |  | 
35- COURSE SEGMENT (S) |  |  |  |  | PASSED |  |  |  |  | FAILED |  |  | PASSED |  |  | FAILED |  |  |  | PASSED |  |  |  | FAILED |  | PASSED |  |  |  |  | FAILED |  |  | PASSED |  | FAILED |  |  | PASSED |  |  | FAILED |  |  | 
37- DISTANCE SEGMENT |  |  |  |  | PASSED |  |  |  |  | FAILED |  |  | PASSED |  |  | FAILED |  |  |  | PASSED |  |  |  | FAILED |  | PASSED |  |  |  |  | FAILED |  |  | PASSED |  | FAILED |  |  | PASSED |  |  | FAILED |  |  | 
39- FLIGHT PATH ANGLE FPA) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | PASSED |  |  |  |  | FAILED |  |  |  |  |  |  |  |  |  |  |  |  |  | 
41- SEGMENT LENGTH |  |  |  |  | PASSED |  |  |  |  | FAILED |  |  | PASSED |  |  | FAILED |  |  |  | PASSED |  |  |  | FAILED |  | PASSED |  |  |  |  | FAILED |  |  | PASSED |  | FAILED |  |  | PASSED |  |  | FAILED |  |  | 
43- EGPWS/TAWS ALERT |  |  |  |  | YES |  |  |  |  | NO |  |  | SI |  |  | NO |  |  |  | YES |  |  |  | NO |  | YES |  |  |  |  | NO |  |  | YES |  | NO |  |  | YES |  |  | NO |  |  | 
45- WIND COMPONENT |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
47- MAXIMUM BANKING ANGLE |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
49- PROCEDURE NOTES |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
51- PROCEDURE: SAT / INSAT |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 53-SIGNATURE OF EVALUATOR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Formulario CA 91-012A |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Form CA 91-012A
VALIDATION OF FLIGHT PROCEDURES IN THE SAM REGION

## Slide 27: VALIDATION OF FLIGHT PROCEDURES
CIVIL AVIATION ADMINISTRATION OBSTACLE EVALUATION |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1-DATE |  |  |  | 3-ORGANISATION |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 5-TYPE OF AIRCRAFT |  |  |  |  |  |  |  |  |  |  |  |  | 
7-PROCEDURE |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 9-FMS/SOFTWARE |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
10-PIC NAME/PHONE NO. |  |  |  |  |  |  |  |  |  |  |  |  | 11-NAME/PHONE NO. OF EVALUATOR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  | SIMULATOR ASSESSMENT TASKS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | YES |  |  |  | NO |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  | 14-GROUND AND IN-FLIGHT CALIBRATION OF EQUIPMENT |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  | 15- PROCEDURE AT 100’ BELOW THE DA/MDA |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  | 18- INITIAL/INTERMEDIATE ASSESSMENT AT ½ THE ROC |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  | 19- FLIGHT AT ALERT LIMITS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  | 20- CHECK THE APPROPRIATE RUNWAY MARKINGS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  | 21- GROUND/AIR COMMUNICATION |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  | 22- ADEQUATE RADAR COVERAGE |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  | 30- LOSS OF RAIM/RNP/RFI |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
VERIFICATION OF SEGMENTS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  | FEEDER |  |  |  |  |  |  |  | INITIAL |  |  |  |  | INTERMEDIATE |  |  |  |  |  | FINAL |  |  |  |  |  |  | MISSED |  |  |  |  |  | HOLDING |  |  | 
43- EGPWS/TAWS ALERT |  |  | YES |  |  |  |  | NO |  |  | YES |  |  | NO |  | YES |  |  |  | NO |  | YES |  |  |  | NO |  |  | YES |  | NO |  |  |  | YES |  | NO | 
49- PROCEDURE NOTES |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
51- PROCEDURE: SAT / INSAT |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 53-SIGNATURE OF EVALUATOR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Formulario CA 91-012B |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Form CA 91-012B
VALIDATION OF FLIGHT PROCEDURES IN THE SAM REGION

## Slide 28: VALIDATION OF FLIGHT PROCEDURES
Form CA 91-012C
VALIDATION OF FLIGHT PROCEDURES IN THE SAM REGION

## Slide 29: CONCLUSIONS
CONDUCT PERIODIC GROUND AND FLIGHT TESTS OF RADIO NAVIGATION AIDS OF THE TYPES SPECIFIED IN CHAPTER 3, ANNEX 10, VOLUME I, IN ACCORDANCE WITH THE RECOMMENDATIONS OF ICAO DOC 8071
FOLLOW UP ICAO ACTIVITIES CONCERNING AMENDMENTS TO DOCS 8071 AND 9906
NEED TO INCLUDE FLIGHT ASSESSMENT OF INSTRUMENT FLIGHT PROCEDURES IN FLIGHT INSPECTION UNITS, INSTALL AIRCRAFT AND GROUND EQUIPMENT, AND DEVELOP AND IMPLEMENT A TRAINING PLAN AS REQUIRED
ADOPT THE ADVISORY CIRCULAR IDENTIFIED AS CA 91-012, PROPOSED BY THE SAM/IG MEETING, CONTAINING GUIDANCE ABOUT SATELLITE-BASED VALIDATION OF INSTRUMENT FLIGHT PROCEDURES (IFP) INVOLVED IN PERFORMANCE-BASED NAVIGATION (PBN).
ENSURE THAT THE FREQUENCY BAND ASSIGNED TO RADIO AID AND SURVEILLANCE SYSTEMS ARE FREE OF HARMFUL INTERFERENCE

## Slide 30
THANK YOU