## Slide 1: Flight Validation of Instrument Flight Procedures
ICASC Draft Guidance Material for the Quality Assurance Manual For Procedure Design (Doc 9906)
Glenn Bissonnette
Fabrizio Maracich

## Slide 2: ICASC Introduction
Currently representing 12 countries with 20 members from the International Flight Inspection/Calibration Community comprising Regulatory Authorities, Service Providers, Equipment Manufacturers, Academia, Research Organizations and System Integrators
Established in 1995 to support the International Flight Inspection Symposium
ICASC has an established working relationship with ICAO and was recently listed as a recognized international organization to participate in suitable ICAO forums.

## Slide 3: ICAO Tasking - Wellington ICASC Meeting
ICASC Operations and Safety Work group tasked with creating draft guidance material for flight validation pilot training and certification requirements
First workgroup meeting held at ICAO Headquarters in June 2009
Recognized shortfall of flight validation guidance material
Recommended adding FV material to the Quality Assurance Manual for Flight Procedure Design Doc 9906
  Volume 5 Flight Validation of Instrument Flight Procedures
  Volume 6 Flight Validation Pilot Training and Evaluation

## Slide 4: Flight Inspection Vs Flight Validation
Flight Inspection evaluates signals in space to meet intended use.
Flight Validation is a flight assessment of a new or revised IFP to confirm it is operationally acceptable for safety, flyability, design accuracy, ARINC 424 coding and required infrastructure

## Slide 5: Need for Flight Validation
Connects Virtual to Real World
IFP data bases and System (FMS/Simulator) databases have varying degrees of accuracy
Flight Validation verifies:
  Course and Path clear of obstacles
  No interference experienced
  IFP delivers aircraft to proper aiming point
  All published data is correct

## Slide 6: Data Accuracy and Integrity
ARINC 424 leg path & terminators provide the desired ground track and vertical path
Requires accurate survey data
Types of Data Errors:
  Survey Data errors common
  Terrain and obstacle data may be incomplete
  Conversions between geographic datums
  Input errors to FAS data

## Slide 7
QA Doc 9906, Volume 5, Draft
Flight Validation of Instrument Flight Procedures
Procedures for Air Navigation Services-Aircraft Operations (PANS-OPS, Doc 8168) requires States to perform ground and flight validation of instrument procedures
Object of conducting FV is to ensure safety, procedure data integrity and flyability
Volume 5 attempts to provide the framework for the validation process
  Preflight Validation
  Simulator Evaluation as required
  In-Flight Validation
  Post Flight

## Slide 8: Validation Process Overview
Flight Validation encompasses both ground and flight elements
Includes Pre-Flight, In-Flight, Post-Flight activities required for evaluating IFP’s
FV must be conducted:
  For initial certification of IFP
  For recertification after flight path and database changes to an existing IFP
  By a qualified and experienced flight validation pilot

## Slide 9
Procedure Design
Ground Validation Quality Assurance
Conduct
Pre-Flight Validation
Outcome of Pre-Flight Validation
Sim Eval
Required?
Conduct Sim Eval
(recommended practises)
Outcome of
Sim Eval
Flight Validation Required?
Conduct Flight Validation
Outcome of
Flight Validation
Conduct Post-Flight Activities
Procedure Implementation
PASS
PASS
FAIL
FAIL
FAIL
FAIL
YES
YES
PASS
NO
NO
PRE
FLIGHT
FLIGHT
POST
FLIGHT

## Slide 10
Conduct
Pre-Flight Validation
Outcome of Pre-Flight Validation
PASS
FAIL
FAIL
PRE
FLIGHT

## Slide 11: Pre-Flight
Inventory and Review IFP package
Perform an electronic data review
Identify items that require flight inspection
Review special operational and training requirements
Review operational considerations
Document the results of the pre-flight evaluation

## Slide 12
Sim Eval
Required?
Conduct Sim Eval
(recommended practises)
Outcome of
Sim Eval
Flight Validation Required?
Conduct Flight Validation
PASS
FAIL
FAIL
YES
YES
PASS
NO
NO
FLIGHT

## Slide 13: Simulator Evaluation
Evaluate necessity for a sim eval
Conduct simulator evaluation
Document the results of the sim eval

## Slide 14: Flight Evaluation
Perform database verification
Assess obstacle and infrastructure
Conduct flyability and human factors assessment
Complete associated validation tasks (Comm, lighting, markings…)
Verify chart depiction and details
Perform the flight(s)
Record flight validation data

## Slide 15
Outcome of
Flight Validation
Conduct Post-Flight Activities
PASS
FAIL
FAIL
NO
POST
FLIGHT

## Slide 16: Post-Flight
Assess the results of flight evaluation
Document the results of the Flight Validation
For satisfactory Flight Validations, complete IFP Processing, including dissemination of information and documents to the proper Authority for publication
For unsatifactory Validations – return supporting documents to the procedure designer for correction

## Slide 17
The goal is to consistently validate IFP to the highest standard to ensure Safety, Efficiency and Ease of use
The Aiming Point

## Slide 18
?

## Slide 19
Thank you