## Slide 1: The Path to Operational AMHS Success
The Steps to AMHS Success
In Peru, Colombia, and with Ecuador
Services and Future Enhancements
Notes: Estimado Director Franklin Hoyer
Estimado Onofrio Smarrelli Especialista CNS regional
Estimados delegados
Estimados observadores
Señoras y señores
Es gusto tanto como honor …
de presentar esta charla …
en esta posición tan distinguida como la primera,…
muchas gracias.

## Slide 2: The Path to Operational AMHS Success - Overview
The Steps to AMHS Success
In Peru and Colombia – and with Ecuador
COMSOFT Services
What is next?
Notes: Congratulations to Peru and Ecuador
This presentation intends to focus on the steps recommended to follow by ICAO in order to achieve such success

## Slide 3: The Steps to AMHS Success
Training
Conformance tests
Link setup & connection tests
Interoperability tests
Pre-operational tests
Confidence period
Operational connection
Notes: Plan ahead your steps and meet your deadlines
Each step builds on the prior one:
Train in due time
Conformance testing
  At FAT time or
  At software delivery time
Network Level tests
  Test with ping, NAT, telnet, wireshark, …
  Over operational infrastructure but best done to a separate (from the operational) development application environment
Inter-Op tests
  Also easier and safer on a separate development AMHS
Pre-Operational tests
  Much safer on a separate development environment (data pollution)
Confidence/Stability period
  AMHS and AFTN connections in parallel
  Smooth, convenient – and safe – transition: easy & quick swing back to backup AFTN possible

## Slide 4: AMHS Background Training
X.400 Fundamentals
AFTN/AMHS Gateway
ATN Security
ATN Directory
Extended ATSMHS
ATN Overview
Basic ATSMHS
New technology requires background training
Modules of COMSOFT‘s AMHS Overview Training
Notes: Well-trained resources scarce but valuable
Plan and meet your dates
---> next page! --->

## Slide 5: AMHS Practical Training
Hands-on training of procedures specific to
  AMHS
  Migration from AFTN/CIDIN to AMHS
Notes: Benefit from COMSOFT expertise (pericia y habilidad)
Important but not core issue of this presentation

## Slide 6: AMHS Test Guidance
Guidance material for AMHS testing
  EUR AMHS Manual (Appendices) http://www.paris.icao.int/documents_open/files.php?subcategory_id=74
  ASIA/PAC AMHS Manual (Annexes) http://www.bangkok.icao.int/edocs/cnsatn/22Guidance_AMHS_Conformance.pdf
    Includes ATN Router tests
  SAM AMHS Guide (2009) http://www.lima.icao.int/eDocuments/CNS/AMHS/AMHS%20Guia.pdf
Mandatory in EUR and ASIA/PAC Regions
Notes: “Paperwork”
All required documentation is
Ready
Available
Straightforward
Do use it!
EUR AMHS Manual in the lead , V7.0 / April, 2012, current
SAM Guide from 2009 refers to V4.0 of EUR AMHS Manual at this time

## Slide 7: AMHS Conformance Tests
Conformance of Implementation under Test (IUT)
  Pre-defined test cases
AMHS Test Tool
  Simulate AFTN/CIDIN and AMHS communication partners
  Monitors external behaviour of IUT
  COMSOFT AMHS Test Suite (CATS)
Notes: First step in ICAO AMHS test recommendations
Each ANSP should insist their system be AMHS compliance certified
COMSOFT can help with CATS (and already does so for its customers for all software releases); reliable and repeatable, defined tests with detailed documentation of results
Highly recommended NOT to proceed to later stages without certified conformance from the supplier; anything else is likely to waste time & money
---> (next page!) ---->

## Slide 8: AMHS Conformance Certificate
AMHS Conformance Tests
  Factory Acceptance Tests (FAT)
  Dedicated tests (third parties)
COMSOFT issues certificate of conformance
Pre-condition to AMHS Interoperability Tests
  No further parties involved
  Identify issues at the earliest opportunity
Notes: In ‘good’ company – delays all over the place:
Bangkok - Singapore not up yet (conformance issues in Bangkok)
Numerous corrections on non-conformant messages required on the China end of the Hong Kong – Beijing connection
State of the region
COMSOFT follows the book hence the connections work (see later slide)

## Slide 9: Connectivity Tests
Connection tests after link setup
  Ensure basic end-to-end connectivity of systems
  Network dependent
  ASIA/PAC: Annex C of AMHS Manual (ATN/OSI Router)
First involvement of external communication partner
Pre-condition to AMHS Interoperability Tests
Notes: IP connections “mostly standard”
Usually done by ANSPs
Analyze with ping, telnet, etc.
Better diagnostics with tools like wireshark very helpful.
NAT usually required
Do secure your networks!
COMSOFT can help
Some issues seen
Unknown or not understandable configurations,
unclear terminology and
limited expert knowledge on-site during link setup and testing slow down progress
=> Do plan your progress and do train your staff in due time
Late setup of links not useful
=> Do plan your progress and do stick to the dates and the stages
NAT and security issues slow down progress

## Slide 10: AMHS Interoperability Tests
Bilateral interoperability tests
  Ensure communication between AMHS end systems
  Clean room environment
  Optionally trilateral
Scope
  All AMHS components incl. AFTN/AMHS Gateway
  Normal message flows
  Stress tests
Pre-condition to Pre-operational Tests
Notes: SAM regional documentation refers to EUR AMHS Manual V4.0; the EUR AMHS Manual already is at V7.0 now.
COMSOFT offers complete assistance during the testing
EUR AMHS Manual compatible parameterization of the COMSOFT’s systems and guidance with others
Test planning, scripts, records
Remote or on-site support during the tests as has been done for Peru and Colombia
Once compliance-certified, progress can be quick …
  (AMHS operational parallel operations stage …
  between Colombia and Peru was …
  well-prepared at both sites and …
  Achieved …
    from parameterization …
    via Inter-Op and …
    Pre-Op stages in the …
  record time of less than a week)

## Slide 11: AMHS Pre-Operational Tests
Pre-Operational tests
  Tests in operational environment
  Real addresses, operational conversion tables and full routing tables
  Duplicate AFTN traffic and compare AFTN to AMHS messages
Scope
  Integrity of message exchange
Be careful to prevent from interference!
Pre-condition to Operation
Notes: Approaching the final operational scenario
Watch out for contamination of operational with copied test data!
=> COMSOFT system has corresponding filter facilities.

## Slide 12: Confidence Period
Purpose of optional confidence period
  Final training – get familiar with the AMHS
  Ensure conveyance of all kind of operational messages in any situation
  Smooth transition from AFTN to AMHS
AMHS shadow phase
  Copy all operational AFTN traffic to the parallel AMHS link
  Check amount and consistency of received messages regularly
  Discard received AMHS traffic
AFTN shadow phase
  Put AMHS into operation – AFTN is no longer operationally used
  Process AFTN traffic as per above the AMHS traffic
Fallback phase
  Switch of AFTN traffic exchange, but maintain configuration as a fallback
Notes: Confidence phase easily achievable with COMSOFT system since the AFTN link terminates on the same system as the AMHS connection and which can be controlled by a few clicks (LA parallel delivery with filters)

## Slide 13: Summary of Stepwise Approach
Swift lift to AMHS success
Regional guidance material follows this approach
Step by step approach is proven all over the world
COMSOFT can give support at any stage
Notes: Migration to AMHS is done without service interruption on a COMSOFT system
The migration is safe, smooth and easy; one platform with consistent parameters and no misrouted messages
AMC tables import ensures that maintaining up-to-date conversion parameters is a breeze; no service interruption required at the effective date of changes.

## Slide 14: The Path to Operational AMHS Success - Overview
The Steps to AMHS Success
In Peru and Colombia – and with Ecuador
COMSOFT Services
What is next?

## Slide 15: AMHS Success Operational AMHS in Peru and Colombia
Fuente: http://www.aerocivil.gov.co/AIS/AIC/Documents/C17_A12_2010_EN%20OPERACI%C3%93N%20EL%20SISTEMA%20DE%20TRATAMIENTO%20DE%20MENSAJES%20ATS%20DE%20COLOMBIA%20-%20%20AMHS-CO.pdf
Fuente: Licitación
Redes Nacionales
P3
Conexión Internacional
P1
Notes: Redes nacionales a través de P3
~80 terminales en el Perú
~110 terminales en Colombia
Interconexión internacional AMHS a través de P1
Entre Lima y Bogotá
This first operational international AMHS connection in the region hums along quietly for almost 2 years now since November 2010 when Colombia was ready

## Slide 16: AMHS Success Operational AMHS between Peru and Ecuador
Notes: Ahora otra, nueva interconexión internacional AMHS a través de P1
Entre Lima y Guayaquil
Entre proveedores distintos
CORPAC comprueba su capacidad de actuar independientemente => buena capacitación previa
Comprueba la buena interoperabilidad del sistema de COMSOFT
Otra vez, felicitaciones al Ecuador y a Perú.
----> en ambos casos, siguiendo los pasos recomendados por la OACI…
-------->

## Slide 17: AMHS Success Operational AMHS between Peru and Colombia - Step By Step
Do establish AMHS conformance
Insist on your certification – and on detailed documentation
Notes: Recommended to establish AMHS conformance as a first and early step:
Insist on your certificate
Insist on test results to back up the claim
There are two conformance test tools to facilitate the conformance testing, one from ACB (few references known to us), and COMSOFT’s AMHS Test Suite (CATS) used at all of the numerous COMSOFT AMHS systems.
Here are some samples from CATS which show how such documentation may look like.
CATS ensures
reproducible tests,
comprehensive documentation of results, and can
reduce test time to a few hours.

## Slide 18: AMHS Success Operational AMHS between Peru and Colombia - Step By Step
Notes: AMHS conformance certified previously from both parties, Colombia and Peru at FAT, i. e. prior to SAT
AMHS Interoperability established in less than 2 days ...
Despite some delays due to network and configuration on the first day ...
AMHS Pre-operational passed at the end of the week
------> Hence we see that AMHS success... ------>

## Slide 19: … AMHS Success !
TestED
DocumentED
CERTIFIED
Notes: AMHS success is
Possible,
Plan’able, and
Achievable
…if you do your homework as recommended.

## Slide 20: The Path to Operational AMHS Success - Overview
The Steps to AMHS Success
In Peru and Colombia – and with Ecuador
COMSOFT Services
What is next?

## Slide 21: The Steps to AMHS Success with COMSOFT
Training
Conformance tests
Link setup & connection tests
Interoperability tests
Pre-operational tests
Confidence period
Operational connection
Notes: Summary:
Benefit from COMSOFT experience
COMSOFT is the solution provider with the most operational AMHS connections in the field
COMSOFT hence has excellent routine, expertise (pericia y habilidad) and experience
COMSOFT customers know how to and can repeat this success due to good training and an excellent user interface
Numerous connections to systems of other vendors prove excellent interoperability of the COMSOFT system
The excellent diagnostic facilities of the COMSOFT system
  permit to find errors in configuration and parameters quickly
  help to assist even in debugging also neighbor systems’ configuration from other vendors
  Hence assist in quickly identifying the source of an issue thus
  Ensuring a swift implementation progress of a connection
----> And the market confirms that this approach is correct…: --->

## Slide 22: COMSOFT Experience World Market Leader

## Slide 23: COMSOFT Experience Operational AMHS Connections Worldwide
State | Manufacturer | Connection to
EUR/NAT Region |  | 
Germany | COMSOFT | Spain
United Kingdom | COMSOFT | USA, Singapore
Bosnia Herzigowina | COMSOFT | Austria
Austria | Thales | Bosnia Herzigowina
Spain | AENA | Germany
ASIA/PAC Region |  | 
Singapore | COMSOFT | India, United Kingdom
India | COMSOFT | Singapore
China | AIT | Corea
Corea | AIT | China (Bejing)
Hongkong | COMSOFT | Macao
Macao | COMSOFT | Hongkong
Japan | MELCO | USA
MID Region |  | 
Oman | COMSOFT | United Arab Emirates
Qatar | COMSOFT | United Arab Emirates
United Arab Emirates | COMSOFT | Qatar, Oman, Jordan, Egypt
Egypt | COMSOFT | United Arab Emirates, Jordan
Jordan | Avitech | United Arab Emirates, Egypt
Saudi Arabia | COMSOFT | Egypt, Jordan
NAM Region |  | 
USA | FAA | Japan, United Kingdom
SAM Region |  | 
Peru | COMSOFT | Colombia
Colombia | COMSOFT | Peru
(May, 2012)
Notes: Experience
Some references to installations and connections
COMSOFT experience with a great variety of environmental conditions and parameters
According to the ICAO COM charts, COMSOFT also leads regarding the number of operational AMHS connections
COMSOFT can assist on-site during testing and link transition
COMSOFT can assist remotely during testing and link transition
Training prior to link transition hence enabling customers to do so by themselves
CATS easily and quickly establishes conformance and enables testing parties to decide whether to proceed
  COMSOFT can assist with detailed analysis of results, system diagnostics and observations
  Avoid delays such as…
    Bangkok - Singapore not up yet (conformance issues in Bangkok
    Numerous corrections on non-conformant messages required on the China end of the Hong Kong – China connection
    State of the SAM region

## Slide 24: The Path to Operational AMHS Success - Overview
The Steps to AMHS Success
In Peru and Colombia – and with Ecuador
COMSOFT Services
What is next?

## Slide 25: Extend the Service New Applications
General Aviation Flight Plan Filing e. g. http://www.peter2000.co.uk/aviation/online-flight-plan-filing/index.html
Digital NOTAM Office over AMHS http://www.aim.aero/demo/digital-notam.html
Digital Meteo (GRIB2) over AMHS
Operational Directory Service http://legacy.icao.int/anb/panels/acp/wg/w/wgw4/ip%2013%20ongoing%20european%20directory%20activities_v2.doc
OLDI/FMTP, AIDC and FPL 2012
ATC Systems Contingency
ATC Systems Hosting
Notes: Further use of the network to be expected, here are some sample applications which will make use of the IP and AMHS networks we currently set up in the region, and world-wide….:
(see above)
COMSOFT can also offer to host ATC services at COMSOFT facilities (two centres, full contingency, direct satellite interface, broad-band internet facilities (>20Mbps),…)
The same technology, COMSOFT can also implement these means at customer sites if required

## Slide 26: Extend the Service Inter-Networking, General Aviation
Services
  Regional Support COMSOFT Latinoamerica
  COMSOFT Aeronautical User Group http://www.caug.aero/
  Network and Network Security Consulting (National, REDDIG)
  Network Management and Operations Centre (NMC, NOC)
  Training – Shine with Excellence
  AMHS Testing Consultancy (Conformance, Interoperability, Pre-Operational) http://www.comsoft.aero/products-solutions/aeronautical-messaging-systems/cats/
International Networking
  Satellite Network Contingency http://www.comsoft-sat.com/company/teleport/
  SAM RADAR Network
    SDDS http://www.comsoft.aero/uploads/media/sdds_ng_02.pdf
    Sensors http://www.comsoft.aero/products-solutions/modern-surveillance-techniques/
  ATN G/G, A/G Communications
Notes: COMSOFT can assist with
Service,
Experience, and
Knowledge
On all network as well as on application levels.
Services, as above
Networking from
  lowest network (satellite, microwave) …
  up (IP, ATN protocols, etc.) to…
  application layers (RADAR distribution, sensors, ATN applications such as AMHS and Digital NOTAM)

## Slide 27: Summary We Can Walk to Operational AMHS Success
Operational AMHS connections are achievable
Following the steps which the ICAO recommends in the AMHS manuals
  Facilitates success, and
  Reduces the risk of uncontrollable delay
There are successful operational connections after following the ICAO recommendations
COMSOFT offers to assist you in the process
New AMHS applications are defined and coming
Notes: We have seen that the AMHS connections we all wait for can be established with relative ease
We have learnt that following the steps which the ICAO recommends in the AMHS Manuals does facilitate success and reduces the risk of uncontrollable delay
We have seen several examples of successful connections here and elsewhere in this workshop after following the ICAO recommendations
COMSOFT offers to assist the region with the steps to come, be it on regional level or nationally, be it with training, technical or other expertise
We also can see new applications on the horizon which will rely on the IP and AMHS networks which we are building now and which justify the effort.
Thank you very much.

## Slide 28
THANK YOU
Contact:
Manfred Schmid, Managing Director Manfred.Schmid@COMSOFT.aero
Peter Cornelius, Project Manager Peter.Cornelius@COMSOFT.aero
COMSOFT GmbH Wachhausstr. 5a 76227 Karlsruhe Germany
Phone: +49-721-9497-0 Fax: +49-721-9497-129 E-mail: info@comsoft.de
Notes: Any questions?