## Slide 1
2023 World Radiocommunication Conference Agenda Item 1.7
Space based VHF
AMS(R)S allocation in 117.975-137 MHz band
CAA Singapore
Preparatory Workshop to ITU WRC-23
21-22 February 2022

## Slide 2
Background
Air navigation services limited by line-of-sight coverage of terrestrial systems
Constrained by separation procedures between aircraft in oceanic and remote areas
Reduced airspace capacity and efficiency
Objective
VHF communications relay via satellite in oceanic and remote airspace Complement current aviation use of satellite-based navigation and surveillance technologies Ease implementation with no change in aircraft avionic equipment Minimal or no change to current operations and SARPs Backup terrestrial systems

## Slide 3: Agenda Item 1.7 – Resolution 428
  to define the relevant technical characteristics
  to study compatibility
  Earth-to-space and space-to-Earth directions
  existing primary services in band and in adjacent bands
  ensuring protection of systems using existing primary services
  not constraining planned usage of those systems;
  taking into consideration the responsibility of ICAO;
resolves to invite the ITU Radiocommunication Sector
  to provide aeronautical operational requirements and relevant available technical characteristics
  to take into account the sharing and compatibility conclusions at ITU-R in the SARPs to be developed for AMS(R)S
invites the International Civil Aviation Organization
Completed
Mostly Completed
In progress
In progress
Completed
Completed
Completed
Completed
Completed

## Slide 4: ICAO’s Position
To support ITU-R studies and the definition of relevant technical characteristics as called for by Resolution 428 (WRC-19).
To support a global allocation to the aeronautical mobile-satellite (route) service for both the Earth-to-space and space-to-Earth directions in the frequency band 117.975-137 MHz and that the use of the allocation be limited to the relaying of aeronautical VHF air traffic management communications.
To support that those systems shall operate in accordance with international Standards and Recommended Practices and procedures established in accordance with the Convention on International Civil Aviation.
To ensure that any change to the regulatory provisions and spectrum allocation resulting from this agenda item do not adversely impact the operation of existing VHF systems in the band 117.975-137 MHz operating in the AM(R)S, including regional usage of terrestrial VHF, nor require any changes to aircraft equipage or to existing installations.

## Slide 5: WD towards a PDN Report ITU-R M.[SPACE-VHF]
Aircraft VHF radio
Doppler shift and latency
Ionospheric scintillation
Polarization (Circular)
Satellite-aircraft range
Baseline link budgets
Feasible solution found using low-Earth orbit satellite
Payload antenna
Summary of technical & operational studies

## Slide 6: Coexistent and Compatibility
In-band services
Adjacent band
services
* Services in 137-138 MHz such as Space Operation, Meteorological satellite, Space Research, Mobile Satellite
ICAO
Non- ICAO
Voice
VDL-M2
Frequency coordination#
Compatibility study
Frequency coordination (bilateral/regional)
AM(OR)S, AOC
ICAO
Non- ICAO
Frequency coordination#
Compatibility study or
Guard band (136-137 MHz)
ARNS (below 117.975)
Space services* (above 137)
VDL-M2
Compatibility study
Frequency coordination (bilateral/regional)
Compatibility study or
Guard band (136-137 MHz)
Pending discussions and acceptance of studies
# Responsibility of ICAO
WD towards a PDN Report ITU-R M.[SPACE-VHF]

## Slide 7: Current Proposed Methods
*Further discussions are ongoing towards possible reconciliation of Methods B, C and D into a single method, depending on the results of the technical compatibility studies.
Method B
Method C
Method D
Limited to internationally standardized aeronautical systems
Limited to systems that operate in accordance to international SARPs and procedures established in accordance with the Convention on International Civil Aviation
Method A – “No Change” to the Radio Regulation i.e. frequency allocation NOT granted.
117.975-136 MHz
117.975-[136/137] MHz
Limited to internationally standardized aeronautical systems; and
Limit the maximum power flux density radiated over the Earth above 137 MHz to [-197.7 dB(W/(m2 · Hz))]
117.975-137 MHz
New AMS(R)S allocation in the band:
WD towards a Draft CPM Text for WRC-23 Agenda Item 1.7

## Slide 8: Summary
WP 5B has progressed in its studies and has amended its working document, taking into account all material provided by ICAO.
Currently the AMS(R)S allocations are being considered separately:
  117.975-136 MHz (voice application, and possibly data link under DSB AM modulation in accordance with SARPs with identical RF parameters)
  136-137 MHz (voice and VDL Mode 2 applications)
Pending confirmation of the representativeness of the parameters against international standardized system for VDL Mode 2, and further discussion required on information regarding protection criterion of adjacent space services.
Next WP5 meeting to be held in Mar/Apr 2022.

## Slide 9
Questions?

## Slide 10: Regulatory activities at ICAO and ITU
Meetings | 2021 |  | 2022 |  | 2023 | 
ITU-R WP 5B WRC-23 AI 1.7 |  |  |  |  |  | WRC-23 Agenda Item 1.7
International Discussions (Technical and Compatibility Studies) |  |  |  |  |  | 
ICAO FSMP |  |  |  |  |  | 
ICAO DCIWG WRC-23 AI 1.7 |  |  |  |  |  | 
ICAO FVSG Monthly Meetings or as required |  |  |  |  |  | 
ITU-R Regional Groups (e.g. CITEL, CEPT, APT, etc.) Frequency of Meetings varies for different regions |  |  |  |  |  | 
Multi-States collaboration on technical contributions
In-band and Adjacent bands compatibility studies
Develop draft CPM text, liaison statements with ICAO
Continue technical and sharing compatibility studies
Finalise draft CPM text
CPM 23-2
Final WP 5B
Finalise ICAO Positions
Discuss draft CPM text, develop liaison statements with ITU-R,
Continue technical and sharing compatibility studies
Develop Regional Positions for WRC-23 Agenda Items
Review draft SARPs PfAs
Review a matured version of SARPs PfA
Initiate ICAO SARPs Approval Process
As required, provide input to ICAO liaison statements with FSMP in coordination with CP-DCIWG
Draft SARPs PfAs
Finalise Regional Positions for WRC-23
Tentative Meeting