## Slide 1: Alignment of ITU and ICAO frequency databases

## Slide 2: Background
ITU Master Register is a worldwide frequency database for all services
Frequency Finder is worldwide database for aeronautical frequencies
In 2012 comparison between ITU and ICAO databases showed that ICAO data are more accurate and up-to-date
WRC-12 considered the matter and invited ICAO/ITU to align databases
WG-F discussed the issue in September 2012 and March 2014

## Slide 3: Problems and Solutions
Problem 1: the format, structure and parameters of ICAO database and the MIFR are different. Solution: development of a notice generation tool for converting data and generating ITU notifications. Status: completed.
Problem 2: aviation authorities are not permitted to update Master Register. ITU administrations have no access to the ICAO database. Solution: make ICAO data available for ITU through Web. Status: ongoing
Problem 3: ITU administrations may have difficulties to compare the MIFR and ICAO data to identify updates to Master Register. Solution: development of a comparison tool. Status: completed. Both tools are linked in TerRaNotices.
Problem 4: aeronautical data are sensitive and shall not be publically available. Solution: 2 levels of protection (discussed further in this presentation). Status: ongoing

## Slide 4: Update of ITU database (standard)
TerRaNotices
Preparation of notifications
BR IFIC*
Publishing
ITU Administrations
(Regulators)
Query data
* BR IFIC: BR International Frequency Information circular
ITU database (MIFR)
Notification
(T12, T13, etc.)
ITU Secured Web notification portal

## Slide 5: ITU Secured Web notification portal

## Slide 6: Proposed interface with ICAO database
Web
Secured data transfer`
every 2
weeks
ICAO global database (Web,
Frequency Finder)
ITU secured Web
ITU Administration
Password
Adm. A can access only to its own ICAO data
MIFR
TerRaNotices
Notes: To the date, the ICAO granted access to its database for the ITU. WE plan ITU intends to place the ICAO data on a secure ITU web service. There will be no possibility to consult the data directly. 2 levels of protection.
The ICAO data could be read only through ITU software TerRaNotices, which will have a link to this web service. Administrations will be permitted to work only with the data related to its country.
How telecom regulator learn about changes to ICAO database ? 2 ways: by regular running comparison tool. 2 there will be a unique key in the both fdatabases. Aviation authority could tell telecom regulator: please notify modifications to those keys.

## Slide 7: ITU Terrestrial System overview
BR IFIC*
ITU Administrations
(Regulators)
TerRaNotices
Notification
(T12, T13, etc.)
Publishing
Query data
ITU Web notification portal
ITU database + Web (ICAO data)
ICAO data via
ITU Secured Web
1. Cross-comparison of ICAO and ITU data.
2. Generation of the correct notifices
Notes: Role of aviation authorities
It will be fully up to the ITU administration to decide whether notify or not aeronautical frequencies. What we are doing is just to make available a mechanism and tools to enable such notifications. Recording in the MIFR could be helpful. For example, if there are sharing rules for aeronautical and PMSE are established how the telecom regulator will know about DME equipment? This could be through MIFR.

## Slide 8
T h a n k y o u, Robert !