## Slide 1
Spectrum Topics not on the specific agenda for WRC-19
Protection of Radio Altimeter and Wireless Avionics Intra-Communications systems
Joseph Cramer – Boeing Noppadol Pringvanich – IATA
Aeronautical Spectrum Seminar Preparation for WRC-19
Bangkok, Thailand March 2017

## Slide 2: Overview
Potential Interference to Radio Altimeters due to future WRC decisions and mitigation measures.
Wireless Avionics Intra-Communications (WAIC) Coexistence with Radio Altimeters
International Mobile Telecommunication (IMT)

## Slide 3
Essential component of an aircraft for precision approach, landing, ground proximity and collision avoidance.
  Safety critical to pilot and flight operations
  Being used in all phases of flight
Provides accurate height measurements over many types of surface (forest, water, buildings, flat).
This information is used by: Automatic flight control system; ground proximity warning system; terrain awareness and warning system; flight management guidance computer; flight control system; electronic centralized aircraft monitoring system; and engine-indicating and crew-alerting system.
Two types: Frequency Modulated Continuous Wave and Pulsed Modulation.
Typical usage is -6 meters up to 6000 meters.
Up to three are installed on a single commercial aircraft.
Importance of the Radio Altimeter

## Slide 4
As a result of WRC-15, Wireless Avionics Intra-Communications (WAIC) share the radio frequency band 4200-4400 MHz with radio altimeters.
The new allocation is:
The Aeronautical Mobile (R) service is limited to WAIC systems.
The Aeronautical Radionavigation service is limited to radio altimeters.
While aviation interests had the intention of prioritizing radio altimeters over WAIC systems, such language was opposed at the WRC. Aviation’s intent remains the same.
WAIC Coexistence with Radio Altimeters
2 700-4 800 MHz
Allocation to services |  | 
Region 1 | Region 2 | Region 3
4 200-4 400 AERONAUTICAL MOBILE (R) ADD 5.A117 AERONAUTICAL RADIONAVIGATION MOD 5.438 5.439 5.440 ADD 5.B117 |  | 

## Slide 5: WAIC Coexistence with Radio Altimeters
Efforts are currently underway to safely incorporate WAIC onto aircraft.
Minimum Operational Performance Standards (MOPS) are being developed by RTCA (SC-236) and EUROCAE (WG-96).
  EUROCAE exchanging information between WG-72 (Data security) and WG-99/SC-234 (PEDS).
  Discussions with WG-68 (“Altimetry”) as well.
Standards and Recommended Practices (SARPS) are being developed within the FSMP Working Group.

## Slide 6: International Mobile Telecommunication (IMT)
IMT applications are increasing very rapidly. More frequency allocations and identifications are required to support this expansion.
  Frequency bands adjacent to the radio altimeter frequency band.
  During WRC-2015, the IMT industry through some States requested frequency identification at 4 400 – 4 500 MHz for IMT applications.
  At least one State is proposing to permit IMT in the frequency band 3 700 – 4 200 MHz.
  Some States supported the IMT industry request. However, no ITU regional groups support such proposal.
Concerns were raised due to the lack of satisfactory adjacent-band compatibility testing.

## Slide 7: IMT
Due to the safety criticality of the aircraft radio altimeters, several States aviation regulators and airlines were directly requested to assist with lobbying with their Capitals during the WRC-2015.
  Competition between IMT and satellite users for limited frequency resources which impact aviation
Debates lasted until the last day of the WRC-2015.
The IMT proposal was eventually dropped due to collaborative efforts by ICAO, IATA, ITU regional groups, aviation/satellite stakeholders and States themselves.

## Slide 8: IMT
Lesson Learned:
  Preparation for WRCs is a global aviation effort. This was a close call.
  Doing nothing is not an option. IMT continues to push for more spectrum. If not at the ITU, then regionally and in individual countries.
  Early coordination and communication among State authorities are essential in developing and influencing States positions for WRCs.
  A clear technical definition for adjacent-band interference rejection should be developed under ICAO for radio altimeters and other equipment.

## Slide 9: IMT
What are being done?
  ICAO Frequency Spectrum Management Panel (FSMP) is defining an interference rejection criteria for radio altimeters to be included in future ICAO SARPs.
    Joint effort with the development of SARPs for WAIC.
    An industry-wide consultation will be needed noting many radio altimeters are already installed and being operated on aircraft.
  Continue global aviation efforts to protect avionics equipment and the safety of traveling public
    Your assistance is needed and necessary!