## Slide 1: 8.33kHz VCS Implementation
Implementation progress report
EUR/NAT MID Preparatory Workshop
Jacky Pouzet
HOU - CFC
Network Manager

## Slide 2: Summary
Regulatory framework
Implementation status and planning
Analysis supporting the Network Impact Assessment
8.33kHz VCS NM implementation support

## Slide 3: (EU) IR 1079/2012 - VCS Regulation

## Slide 4: Area concerned
IR

## Slide 5: Who is affected?
  General Air Traffic (GAT)
    All categories of aircraft operating below FL195 within ICAO EUR region where EU MS are responsible for providing ATS
  Exemptions possible under certain circumstances
  ANSPs
IR
State aircraft
  Transport/non-transport state aircraft operating below FL195 (Military, police, customs, civilian aircraft operating as military, police, etc.)
Ground vehicles
Aerodromes

## Slide 6: Equipment
IR
All radios on EU market (VHF band) past 2013 are 8.33VCS capable
All equipment put into service after 2013 is 8.33VCS capable
All new airworthiness certificate past 2013 requires 8.33VCS equipment

## Slide 7
Regulatory framework
Implementation status and planning
Analysis supporting the Network Impact Assessment
8.33kHz VCS NM implementation support

## Slide 8: 8.33VCS Implementation Status
Based on SAFIRE information April 2017 for Switzerland, Norway and EU MS
  Only operational and assigned frequency assignments
  Excluding frequencies excepted from conversion by VCS Regulation (CLIMAX, ACARS, VDL, EMG, SAR)
Service | 25kHz | 8.33kHz | Total Assignments
A/A | 16 | 6 | 22
A/G | 1560 | 290 | 1850
ACC | 696 | 506 | 1202
AFIS | 774 | 24 | 798
APP | 1020 | 54 | 1074
AS | 625 | 130 | 755
ATIS | 380 | 20 | 400
FIS | 117 |  | 117
GUARD |  | 1 | 1
OPC | 1092 | 774 | 1866
PAR | 128 | 2 | 130
TWR | 968 | 59 | 1027
VOLMET | 49 | 6 | 55
Grand Total | 7425 | 1873 | 9298

## Slide 9: 8.33VCS Implementation planning
 | 25kHz | Exemptions due to Offset carrier (CLIMAX) | Exemptions due to State aircraft accommodation | Exemptions due to safety requirements | Exemptions due to local measures | Total Exemptions | Convertible 25kHz
No. Assignments | 7425 | 505 | 830 | 233 | 421 | 1989 | 5436
Note: these figures are in continuous evolution while states are finalising their strategy for conversion

## Slide 10: 8.33VCS Implementation planning
 | during 2016 | during 2017 | during 2018 | no plan or beyond 2018
No Assignments planned for conversion | 11 | 222 | 3178 | 2025

## Slide 11: Summary
Regulatory framework
Implementation status and planning
Analysis supporting the Network Impact Assessment
8.33kHz VCS NM implementation support

## Slide 12: Assessment Objective
  Evaluate the impact of local measures granting exemptions on the VHF spectrum availability
    As an individual (isolated) effect (State level)
    Global effect (EU level)
  Analyse the availability of frequency assignments in the future considering:
    The forecasted frequency demand for all States
    Other known constraints (e.g. frequency demand in “non 8.33 States”)
The Network Impact is defined by the probability of success in the process of allocating new frequency assignments, taking into account the forecasted demand.
A limited Network Impact can be considered in the case in which the future frequency demand can be satisfied without significant delays.

## Slide 13: Data availability and assumptions
Assessment is performed based on frequency assignment allocation data:
  Available in SAFIRE
    VHF frequency
    Service
    Designated Operational Coverage (DOC)
    8.33 planning (i.e. conversion or exemption)
  For all states
    EU Member States (28+2)
    Non-EU Member States participating in SAFIRE
  Current frequency congestion & forecasted frequency demand
    For 25kHz assignments
    For 8.33kHz assignments
    In 3 separate areas (Area1, 2 and 3) based on current spectrum congestion
$e<Ref>
$em
$es
$d(DDMMYY)
$ec

## Slide 14: Frequency demand forecast data
The forecast of future demand is based on
  Analysis of past frequency demand evolution,
  Known planned developments of the ATM infrastructure as covered by the Network Operations Plan
  Validation and extrapolation of demand trends based on the current situation
  Agreed by the States
Specific distribution of the demand was considered depending on the geographical position
  Different trend
  Different demand
  Different ratio between 25kHz and 8.33kHz assignments demand*
*Normally a 80%-20% ratio between 8.33kHz/25kHz assignments demand is considered for all services in Area 1&2, while a 20%-80% ratio is considered for Area 3. This is due to States in Area 3 not being covered by the VCS Regulation

## Slide 15: Methodology(ies)
Based on frequency demand satisfaction over a period of years (up to 2036)
  Measured by assessing the rate of success in finding frequency assignments for the forecasted demand
    rate of success above 95%
    rate of success below 95%
  Dependent on the number of “shifts” allowed
Based on the number of frequencies available in a geographical location
  Analysing the contribution of a proposed exemption to the reduction of the number of frequency assignments available in a certain area
  Qualifying the impact based on the number of frequencies available at the geographical location where the loss takes place (i.e. a loss of 10 potential new assignments in a location where 100 frequencies are available has not the same impact as having a similar loss in a location where only 11 are available)
  for 2018 (conservative case: minimum conversions vs. maximum no of exemptions)
Global impact
Individual impact

## Slide 16: Frequency demand satisfaction
Nominal potential implementation scenario
  The forecasted frequency demand is satisfactory fulfilled (above 95% satisfaction rate) for Area 1 and 2 States
  A maximum of 2 frequency shifts are allowed in order to allocate a solution
  Until 2028 for Area 3 all the demand is satisfied above 95%

## Slide 17: Frequency Congestion - estimated for end of 2018
No. of available 8.33kHz channels based on an ACC 50NM radius/FL450 service

## Slide 18: Example of exemption spectrum contribution for end 2018
No. of 8.33kHz assignments contributing to the spectrum reduction, based on an ACC 50NM radius/FL450 service

## Slide 19: Frequency demand variations
Double frequency demand (2 shift)
  The satisfaction rate trend for the States in Area 1 is constantly below 95%
  The satisfaction rate for the States in Area 2, shows a tendency to decrease through the end of the considered time interval
  The satisfaction rate for the Area 3 is constantly below 95% and on a decreasing trend

## Slide 20: Frequency demand variations
Nominal Frequency demand (0 shift)
  The satisfaction rate trend for the States in Area 1 is constantly below 95%
  The satisfaction rate for the States in Area 2, while above 95% for the first 9 years of the assessment, decreases and remains below this threshold after 2027
  The satisfaction rate for the Area 3 States is constantly below 95% and on a decreasing trend

## Slide 21: Frequency congestion evolution forecast
Comparison of the 8.33kHz channel congestion in Europe
  Nominal potential implementation scenario in 2018 vs.
  2025 with the forecasted demand added
  Note: the reduction of the frequency congestion in core Europe is due to most of the local measures granting exemptions being lifted. The increase in congestion in the East European States is due to
  - the lack of complete planning information from Bulgaria, Greece, Cyprus,
  - numerous exemptions for State aircraft accommodation (e.g. Romania)
  - the demand in 25kHz assignments from the States not participating in 8.33 programme (e.g. Turkey)

## Slide 22: Frequency Congestion – estimated end 2018
No. of available 8.33kHz channels based on an ACC 50NM radius/FL450 service

## Slide 23: Frequency Congestion – estimated 2025
No. of available 8.33kHz channels based on an ACC 50NM radius/FL450 service

## Slide 24: Summary
Regulatory framework
Implementation status and planning
Analysis supporting the Network Impact Assessment
8.33kHz VCS NM implementation support

## Slide 25: NM Implementation Support Project
Monitoring & Steering implementation
  Data collection for conversion planning, exemption, equipment inventory and implementation status
    SAFIRE
    Direct reporting
  VHF Radio Testing Campaign
  GA aircraft and equipment repository (833radio.com)
Coordination of exemptions/derogations
  Network Impact Assessment analysis of exemptions
  Exemption strategy analysis
Awareness and support to implementation
  www.eurocontrol.int/833
  Information dissemination preparation
    833radio.com
    Aero Friedrichshafen briefing (industry, pilots, fight schools, etc.)
Notes: - there are 3 main directions of activities within the 8.33 Implementation Support Project:
- monitoring and steering
- Coordination of exemptions
- awareness and support to implementation
- note the tasks covered by each of the activities and note the new achievements:
- VHF radio testing campaign – KOM tomorrow in which it is intended to provide feedback to the industry on specific technical issues related to the available radio equipment (8.33)
- GA aircraft and equipment repository – a web based platform for voluntary registration of aircraft owners intended to increase the awareness of the pilots regarding the 8.33 deployment, obtain an up-to-date database of GA aircraft and equipment, provide a basis for eventual funding for retrofit
- Impact assessment simulation with the scope of assessment of planned exemptions by states and support the definition of coordinated, and harmonised exemption strategies

## Slide 26: Implementation progress below FL195 EU ATC sectors
https://ext.eurocontrol.int/833/Airspace_8.33kHz_Radio.html
Notes: - there are 3 main directions of activities within the 8.33 Implementation Support Project:
- monitoring and steering
- Coordination of exemptions
- awareness and support to implementation
- note the tasks covered by each of the activities and note the new achievements:
- VHF radio testing campaign – KOM tomorrow in which it is intended to provide feedback to the industry on specific technical issues related to the available radio equipment (8.33)
- GA aircraft and equipment repository – a web based platform for voluntary registration of aircraft owners intended to increase the awareness of the pilots regarding the 8.33 deployment, obtain an up-to-date database of GA aircraft and equipment, provide a basis for eventual funding for retrofit
- Impact assessment simulation with the scope of assessment of planned exemptions by states and support the definition of coordinated, and harmonised exemption strategies

## Slide 27: Questions?

## Slide 28: 8.33kHz VCS Implementation
EUR/NAT MID Preparatory Workshop
8.33VCS Implementation Support
www.eurocontrol.int/833
8.33@eurocontrol.int
Thank you!