## Slide 1: APANPIRG Conclusions Regarding Frequency Management
(Spectrum Review Working Group)
Presented by the Secretariat
28 March 2017

## Slide 2: Conclusion APANPIRG/26/47 – Strategic planning and tactical use of VHF frequencies in the APAC Region from 2015 onwards
That, the guidance on Strategic planning and tactical use of VHF frequencies in the APAC Region from 2015 onwards provided in Appendix 1D to the Report under Agenda Item 3.4 is adopted.

## Slide 3: STRATEGIC PLANNING AND TACTICAL USE OF VHF FREQUENCIES IN THE APAC REGION FROM 2015 ONWARDS
Considering that the simulations conducted by SRWG on the basis of the needs submitted, showed that congestion in the APAC region for VHF frequencies using a 25 kHz channel spacing was unlikely to happen until 2020, and considering the necessity to continue using 25 kHz channel spacing as long as possible,
  1/ All APAC States should contribute to the strategic planning by submitting number of VHF channel required based on the operational requirement (planned use and release) for a 5-years sliding window so as to detect and mitigate any spectrum congestion sufficiently beforehand and optimize the efficiency of the available spectrum, by submitting and updating their operational needs in terms of VHF frequencies (international and national) on a yearly basis to the ICAO Regional Office;
  2/ If the frequencies for the channels could be reserved for protection as a result of strategic planning, their effective use should start after tactical assignment coordinated with the ICAO Regional Office;
  3/ The tactical coordination of frequencies without any prior strategic planning should be avoided as much as possible in congested areas;
  4/ Both strategic planning and tactical assignments should be completed using the ICAO global tool Frequency Finder; and
  5/ Strategic planning should be revised on an annual basis; in case of detected congestion within a 3-year timeframe based on the latest simulations made, the decision to move to 8.33 KHz spacing would need to be made by APANPIRG and implemented in a coordinated manner, after due consultation of airspace users.

## Slide 4: Conclusion APANPIRG/26/48 – Transition to the new global database
That, considering that Frequency Finder and the global database were a necessary toolkit for efficient frequency management across ICAO Regions, and training on using it is needed,
  a) ICAO be invited to secure the resources to maintain the tool and organize a seminar/workshop on Frequency Finder in 2016,
  b) States secure the attendance of their Subject Matter experts to the Seminar/workshop

## Slide 5: Conclusion APANPIRG/26/49 – Assignment of back up frequencies in APAC Region
That, considering that the assigned number of backup frequencies should be kept to a minimum,
1) the guidance material placed at Appendix N to WP/9 is adopted as regional guidance;
2) States/Administrations requiring back up frequencies, where operationally feasible:
  share backup frequencies either between different services (at the same ATC center) or between different facilities (e.g. different aerodromes or different APP/ACC/FIS serves from different ATC centers);
  follow the regional guidance for the backup frequencies to be assigned; and
  re-coordinate the backup frequencies already assigned as necessary.

## Slide 6: Conclusion APANPIRG/26/50 – Amendment to the APAC frequency allotment plan
That, considering the effect of the reduction of the guard band around the frequency 121.500 MHz and the four new channels that can be used for ATC communications and the necessity to map services previously defined in APAC Region under ASIA/PAC/3 RAN meeting Recommendation 11/4,
    the frequency allotment plan for the APAC Region be modified as follows:
    b) coordination be undertaken with ICAO HQ to update the ICAO Doc 9718 Volume II accordingly.
    c) the mapping between the services and designated operational coverages previously defined in APAC Region under ASIA/PAC/3 RAN Meeting Recommendation 11/4 and those defined in the global Database as per Appendix O to WP/9 is adopted.