## Slide 1: COLLINS AEROSPACE Communication Modernization
Advanced VHF
January, 2019

## Slide 2: Communication Modernization - vhf
Agenda
Current VHF Concerns/ Modernization Options
Channel Utilization Analysis/Forecast
Advanced VHF Value Proposition

## Slide 3: Communication modernization - vhf
Concerns/options
Legacy VHF Concerns
Current VDL M2 waveform limited to 31.5 kbps on a 25 kHz channel
Channel capacity may not be sufficient for new data applications
Insufficient spectrum to increase number of frequencies for more sectors
8.33 kHz channels in Europe limited to voice
Europe pushing for alternative comm systems (e.g. LDACS) to achieve higher data rates
  Requires new ground infrastructure
  Requires operators install additional radios/antennas
  Creates interference with existing L-band avionics
Advanced VHF Options
Introduce highly efficient digital signal processing (e.g APSK, QAM)
Adjust waveform to support 31.5 kbps on a 8.33 kHz channel
Achieve rates ~100 kbps on a 25 kHz channel
Capable of bootstrapping to wider channels for even higher data rates
Support connectionless protocol
Implement digital voice
Provide dynamic power control to reduce spectral footprint

## Slide 4: Communication Modernization - vhf
Channel utilization analysis/forecast
Model current channel utilization
Analyze short range line of sight roadmap
  Demand changes
  Technology changes

## Slide 5: Communication Modernization - Vhf
Advanced VHF Value proposition
MIRs | Value
Capacity | 31.5 kbps on a 8.33 kHz channel could satisfy near term data demand and relieve frequency concerns by increasing number of available frequencies in Europe. 100 kbps on a 25 kHz channel could satisfy long term ATC data requirements, but even greater rates opportunity exist if channel bootstrapping is permitted
Infrastructure | Updates to protocol would be provided without licensing to all service providers and should be minor changes to ground stations in support of a new waveform. Further advancements in the protocol could be deployed with other desired changes to VHF Comm (i.e., connectionless)
Avionics | Most existing radios could be modified by a SW only update to reach almost 3X the number of channels. Incremental block point updates could be introduced over a reasonable timeframe to make changes required by Operators more affordable. Modernizing the existing radios eliminates the need for operators to install additional redundant radios to fly through various national airspace
Regulations | The objective is to minimize regulatory changes to the MOPS and few administrative updates
Compatibility | Many of these advanced techniques can be applied within the current MASPS to facilitate backward compatibility with current waveforms and interoperability across all regions globally which allows certain regions to implement these changes more aggressively while maintaining operational compatibility