## Slide 1: SARPs and Manual on C2 Links for RPAS - Status Update -
– RPAS Panel WG2 –
FSMP WG/12-IP/02 – Agenda 10
4-15th October 2021

## Slide 2: C2 Link SARPs and Manual - Background
    Because the C2 Link is, for several reasons, very different to other aeronautical communication systems the C2 Link SARPs are contained in their own volume (Volume VI) of Annex 10
    Part I of Annex 10, Volume VI, contains the already adopted Procedures associated with C2 Links
      Adopted during ICAO Council 222nd Session, in February 2021, Effectivity July 2021
      Many additions also to Annex 6 “Operation of Aircraft” in support of the C2 Link Procedures
    RPASP WG2 is now developing the Systems SARPs for, Volume VI, Part II and the accompanying Manual on C2 Links for RPAS
      Planning Informal and Formal coordination between WGWHL/2 (October 2021) and RPASP/18 (March 2022)
        CP, CP-DCIWG, CP-OPDWLG, FLIRECSWG, FSMP, NSP, SASP, SMP, SP
      Planning to request RPASP approval to send the SARPs and Manual to the ANC at RPASP/18 in March 2022
      Planning that the ANC will hold a Preliminary Review of these SARPs in Q4 2022
      Anticipated adoption of SARPs in Q1 2025

## Slide 3: C2 Link SARPs and Manual - Background
    The C2 Link is a “black box” connecting the RPS and the RPA
      Supports all remote pilot activities required to safely manage the RPA
      Supports external management of its operation by the RP/RPS and RPA
    Neither “end“ of the C2 Link needs to be standardized in SARPs
      The C2 Link is entirely inside the RPAS and does not need to directly connect with other standardized aeronautical systems
    Many technical solutions are possible some already know, some to be discovered
      Currently RPASP WG2 is considering six solutions, two in L Band (satellite), three in C Band (terrestrial, relay and satellite) and one in Ku/Ka band (satellite)
      No interoperability between solutions is required
      Compatibility between solutions sharing the same frequency band is required
Graphic from the SARPs

## Slide 4: C2 Link SARPs and Manual - Background
    RPASP WG2 and RTCA have developed the Required Link Performance (RLP) concept for the C2 Link User Data
      Same RLP for all RPAS/C2 Links operating in the same airspace/phase of flight
      All RPAS are equally “safe” irrespective of their design or their C2 Link design
    The C2 Link is Managed by the RP/RPS and RPA
      Currently only how and how well the C2 Link responds to C2 Link Control Data is part of the proposed SARPs and Manual on C2 Links for RPAS
      How the C2 Link itself is managed by the RP/RPS and RPA is outside the scope of the RPASP WG2
        Will be part of the Type Certification of the RPAS
Graphic from the SARPs

## Slide 5: C2 Link SARPs and Manual – RLP Context
    The required performance of a C2 Link is highly dependent on
      The Target Level of Safety in the airspace = RLP
      The phase of flight = RLP
      The pilot activity it is supporting = RLP
      The level of automatic capability in the RPA and RPS = C2 Link Specification
        Too many different levels of RPAS automatic capability to cover in the RLP/SARPs
    The RLP is developed by Aviation Safety Regulators
      The RPAS Designer then specifies the, RPAS design dependent, C2 Link Specification
      The RPAS Operator then contracts, through a Service Level Agreement with the C2CSP, for a QoSR for their planned operation

## Slide 6: C2 Link SARPs – Strategy
    The Annex 10, Volume VI, Part II Systems SARPs
      Contain high level technical requirements that can be applied to any current or future C2 Link technology
        SARPs will not need to change every time the technical solution changes or a new technology is introduced
        SARPs provide a framework for any new technology concept
      SARPs standardize any C2 Link’s
        Performance
          Performance based RLP, high level concept and process, actual values in Manual
        Management
          Performance based, response to commands to Establish/Terminate, Switchover, Handover and Report Status, actual values in Manual
        Compatibility
          Performance based, management of interference and protection of systems, actual values in Manual
        Security
          Performance based security controls, actual values in Manual

## Slide 7: SARPs on C2 Links for RPAS
Abbreviations
Publications
Foreword
Part I – C2 Link Procedures
  Chapter 1. Definitions
  Chapter 2. Specifications
  Chapter 3. Procedures
Part I I – C2 Link Systems
  Chapter 1 Definitions
  Chapter 2 Systems
  2.1 System description
  2.2 Interfaces
    2.3 Frequency Spectrum
    2.4 System Characteristics
    2.5 User Data Transmission Characteristics
    2.6 C2 Link User Data Performance Requirements
    2.7 C2 Link Control Data Response Characteristics and Performance Requirements
    2.8 Security
    2.9 Records
    2.10 C2 Link Communications Service Providers
SARPs already adopted/effective
Review to be completed by WGWHL/2 October 2021
Initial review completed in July 2021

## Slide 8: Manual on C2 Links for RPAS - Strategy
    The Manual on C2 Links for RPAS will evolve as ICAO, its member states, and the RPAS industry learn more about the certification and operation of C2 Links
      Regular updates to the Manual on C2 Links for RPAS are anticipated
    The first version of the Manual on C2 Links for RPAS will focus on setting up the foundations and methods that States will use to develop C2CSP certification and management as well as the development of specific RLP types (grouped values of RLP parameters for certain phases of flight and airspaces)
      Chapter 1. Introduction to C2 Links for RPAS
      Chapter 2. The C2 Link Service Provision and Communication Service Providers
      Chapter 3. RLP description, method to develop etc. with worked examples
        RLP values are not currently planned to be in the initial version of the Manual on C2 Links for RPAS, but it is anticipated that they will be added as they become available

## Slide 9: Manual on C2 Links for RPAS - Strategy
    WG2 has a challenge
      Without RLP, it is not possible to assess the suitability of a C2 Link technology
      Without C2 Link technologies it is not possible to gather experience and data to enable RLP to be determined and validated
    The Manual on C2 Links for RPAS will encourage States to contribute to the development of RLP at a national level and then bring their findings to ICAO
    Since specific RLP values are not available currently it is not possible to indicate the suitability of any technical solution in the first version of the Manual on C2 Links for RPAS
    To ensure States do get guidance and work towards international harmonization, the Manual on C2 Links for RPAS will describe the “Candidate” C2 Link technologies that are being considered at this time
    Future versions of the Manual on C2 Links for RPAS will contain RLP values for various airspaces and phases of flight
    Future versions of the the Manual on C2 Links for RPAS will contain suitable C2 Link technologies and the performance they can achieve

## Slide 10: Manual on C2 Links for RPAS – First Version
Glossary
Definitions
References
Chapter 1. Introduction to the Manual on C2 Links for RPAS
Chapter 2. The RPAS C2 Link
Chapter 3. RPAS C2 Link Performance
Chapter 4. Candidate C2 Link Technologies
  Chapter 4.1. C Band
  Chapter 4.1.1 Terrestrial Systems
  Chapter 4.1.2 Satellite Systems
  Chapter 4.1.3. High Altitude Relay Systems
  Chapter 4.2. Ku and Ka Band
Chapter 4.3 L Band
Chapter 4.3.1 Inmarsat
Chapter 4.3.2 Iridium

## Slide 11: Manual on C2 Links for RPAS - Chapter 4
    For the first version of the Manual on C2 Links for RPAS Chapter 4 will provide general information about C2 Links
      Explain that we do not know if the candidate technical solutions will be suitable, but we want to give guidance and request feedback on the technologies being considered
      Explain how a C2 Link technology will be assessed for suitability (based on the SARPs structure)
        Performance
        Management
        Compatibility
        Security
    Chapter 4 will include descriptive information on each candidate technical solution without discussing its suitability

## Slide 12: C2 Link SARPs and Manual – Next Steps
    RPASP WG2 plans to complete its review of the Draft proposed C2 Link related SARP amendment proposals during October 2021
    With the help of the RPAS Secretariat it will then circulate those SARPs for Informal coordination with various Panels, including the FSMP
    Feedback on those SARPs is requested during Q4 2021
    RPASP WG2 will then issue an update to the C2 Link SARP amendment proposals so that Formal coordination can be completed prior to RPAS Panel Meeting #18 in March 2022