## Slide 1
Performance Based Navigation Approval and Training

## Slide 2: Contents
PBN Background
Certification Basics
PBN Basics
Navigation Databases
GNSS in PBN
Navigation Specifications
CAO 20.91
Navigation authorisations

## Slide 3: PBN Terminology
Correct terminology is important for clarity:
  Area Navigation is the generic term used for area navigation and is never abbreviated.
  RNAV is used only in reference to RNAV specifications.
  RNP is used only in reference to RNP specifications.

## Slide 4: Airspace Fundamentals
Airspace capacity is determined by the separation standard applied.
Minimum separation is a function of the CNS and ATM system capabilities.
All four elements require a regulatory infrastructure defining requirements and standards.

## Slide 5: Operational Approvals
Operational Approvals are the key to the implementation of the emerging air navigation system.
  Without operational approvals, operators will not be able to take advantage of the emerging technologies.
An operational approval is about:
  An OPERATOR
  Conducting that OPERATION
  With that AIRCRAFT
  In that AIRSPACE

## Slide 6: Operational Approval Content
Operational Approval
Airworthiness
Continued Airworthiness
Flight Operations
Aircraft requirements:
Function & Performance
Installation
Design standards
Maintenance schedule
Configuration management
Maintenance procedures
Parts
Test equipment
Training
  Syllabus
Competency
Operating procedures
Route Guide
MEL
Training
  Syllabus
  Means of delivery
Competency
Continued competency
Certification procedures
Business systems
Training
Competency
Head of Power
Requirements
Standards
Authority
Regulator Infrastructure

## Slide 7: Airworthiness
Compliance with airworthiness requirements must be determined.
  Approval is at the aircraft level.
    Includes equipment and the aircraft installation.
New production aircraft have airworthiness approvals identified in the AFM and / or OEM Service Letter.
  Airworthiness approval is usually straightforward.
Legacy aircraft require more detailed analysis.
  Compliance with requirements may require detailed certification activity.
    Tier 3+ aircraft modification configuration can be a problem.
  Some approvals are addressed by OEM Service Bulletin.

## Slide 8: Continued Airworthiness
Each operator is responsible for ensuring that each aircraft is maintained compliant with its type design.
Continued airworthiness elements that must be addressed:
  Maintenance schedule.
  Configuration management, particularly software & electrical load analysis.
  Maintenance procedures.
  Parts.
  Test Equipment.
  Training & competency.

## Slide 9: Flight Operations
Flight operations element must address:
  Operating procedures.
  Route Guide.
  Minimum Equipment List.
  Crew training.
    Includes the syllabus and delivery methods.
    Training requirements are included in ACs.
  Simulator exercises.
  Crew competency.
  Continuation training and currency.

## Slide 10: PBN Regulatory Structure
CAO 20.91
Instructions and directions for PBN
AC 91.U-II-1(0)
Navigation Authorisations
CAO 20.18
Aircraft equipment – basic operational requirements
Assessors Handbook
Assessors Worksheet
Worksheet Line 75:
Crew operating procedures – perform gross error checks.
Handbook C3.2.2:
Crew training & competency
AC 91.U-II-1(0):
Training programme
CAO 20.91 App 4 para 12.2 (r):
Perform gross error checks.

## Slide 11: Navigation Authorisations Process
Australia is implementing a navigation authorisation system that addresses all authorisations required in a single application.
  Certification activity is focussed on operator first-of-type applications.
  An application can be revised for additional authorisations and aircraft.
  Authorisation changes focus on differences.
  The applicant must demonstrate compliance.
Installation design engineers need to consider the operational requirements in system installation designs.
  Flight Manual Supplements need to clearly state operational limitations in the Limitations section.
    AFMS commonly state that an aircraft is approved for an operation; this indicates an airworthiness approval only.

## Slide 12: Navigation Authorisation Process
Operator completes the application form 1307 to demonstrate compliance with the relevant requirements.
Application and substantiating data is submitted to the CASA for approval.
When approved, the operator Op Spec will be revised or an navigation authorisation instrument issued.

## Slide 13: Certification Basics

## Slide 14: Typical Navigation System

## Slide 15: Hierarchy of Requirements
Operational Requirements
System requirements
  Regulatory requirements
  Derived requirements
  Sub-system requirements
    Regulatory & derived requirements
      Hardware requirements
    Regulatory & derived requirements
      Software requirements
    Regulatory & derived requirements

## Slide 16: 4 C’s and 3 A’s
Configuration
Conformance
Compliance
Certification
Approved
Accepted
Authorised

## Slide 17: Similarity
Compliance can be demonstrated by similarity with other aircraft or installations.
To be acceptable, the basis of the similarity must be defined and be valid (relevance and applicability test):
  The subject being considered for similarity must be:
    Relevant to the aircraft / system / configuration under consideration.
    Applicable to the aircraft / system / configuration under consideration.

## Slide 18: Navigation databases

## Slide 19: Database Management
The PBN Manual requires operators to use current databases.
Operators should have processes for managing navigation databases to ensure aircraft are always using current data.

## Slide 20: Database Integrity
The PBN Manual requires navigation data to be obtained from sources that meet the regulatory requirements.
  Regulators issue database suppliers with a Letter of Acceptance (LOA) when compliance with data processing standards are met.
Operators should carry out validity checks on data and must report any defects found.

## Slide 21: Database Validity Checks
Operators should carry out checks on databases for each cycle to meet quality assurance requirements.
The extent and depth of checks made should reflect the criticality of the data.
  For most operators, sample comparison between the AIP charts and the database are adequate.
  Critical data e.g. RNP AR APCH should be checked against a standard before each cycle is released for fleet use.

## Slide 22: Navigation Specification Structure
Navigation Specification & Application
RNAV Specifications
RNP Specifications
RNAV 10
(RNP 10)
Application:
Oceanic / Remote Continental
RNAV 5
RNAV 2
RNAV 1
Application:
Continental en-route & terminal
RNP 4
Application:
Oceanic / Remote Continental
RNP 2
RNP 1
Advanced RNP
RNP APCH
RNP AR APCH
RNP 0.3
Application:
Various phases of flight
RNP with additional requirements:
RF legs
Baro VNAV
LP/LPV
FRT
TOAC
Application:
3D, 4D & advanced ATM

## Slide 23: Inspector training
Types:
  Flying Operations
    Need to understand all aspects
  Engineering and Airworthiness
  Air Traffic
    Application of PBN
  ATM Support
    Part 175
    Pans OPs

## Slide 24: Training Framework
Notes: INTRODUCE this slide by explaining that each job function sits within the R&TT Framework, which was signed off by the DAS in March 2015. Key points to share in relation to the framework are:
There are four components to the R&TT Framework:
  Foundation Regulatory Training;
  Advanced Regulatory Training;
  Specialist Regulatory & Technical Training; and
  Currency Training.
Each component has unique features as they apply to staff members; and
These are explained on upcoming slides.

## Slide 25: Basic Training
“Core Regulatory Training”
  Basis for all incoming inspectors
    Includes basic GNSS and PBN
Specialist training for individual inspectors
ICAO IKITS
  PBN
  GNSS
  http://www.icao.int/safety/pbn/PBNiKitV3/story.html

## Slide 26: Specialist Team?
Can you train all your inspectors in GNSS and PBN?
  Perhaps in longer term
  Will become basic knowledge for all inspectors
    Various levels for each inspector type
Consider forming a specialist team
  FOI
  ATC
  AWI
Provide ongoing training and updates
  ICAO meetings, industry training

## Slide 27: SOME LESSONS

## Slide 28
AI
ALT
Turn Coordinator
DI
VSI
BN-2A Original Configuration
ASI

## Slide 29
DI
EFD 1000
ASI
BN-2A Modified Configuration
AI
ALT

## Slide 30
AI
EFD 1000
ASI
BN-2A Final Configuration
DI
ALT

## Slide 31
IRS
IRS
FMS
CDU
CDU
Is this a dual installation?

## Slide 32
IRS
IRS
FMS
ANCDU
ANCDU

## Slide 33
RVSM or not RVSM? – Dents & Buckles

## Slide 34
ASI
AI
ALT
Turn Coordinator
DI
VSI
GNSS Annunciator View
ENG
ENG
ENG
RAD
GNSS
GNSS
Transponder
PFOV

## Slide 35
Visibility & Accessibility (Q300)

## Slide 37
Visibility & Accessibility (F50)

## Slide 38: Electrical Load Analysis
Many GA aircraft struggle to meet the ELA requirements.
CAR 3B has no 30 minute battery only requirement.
Some GA manufacturers use a 30 minute discharge rate for the ELA rather than the 1 hour rate of SAE F2490-05.
  This provides a 1.8 benefit over the 1 hour rate.
  Battery is flat after 10 – 15 minutes compared to SAE F2490-05.

## Slide 39: ELA Mitigation
10 minute generator recognition period reduced to 5 minutes with flashing annunciators in the PFOV.
No recognition period for automatically shed loads.
All non-essential loads turned off – AFM supplement may be needed for electrical power failure.
Manual control of high power loads to minimise consumption e.g. de-icers.
Lightest load of navigation lights and strobes used.
Landing lights limited to 2 minutes prior to landing.

## Slide 40: RNP AR Operations
Application received for RNP AR operations to Queenstown.
Aircraft owned by high wealth individual.
Aircraft is modified to equip it with the required systems – not OEM or STC approved.
No RNP AR approval in the AFM.
Flight test data is presented to demonstrate compliance:
  Flight test plans have not been reviewed or accepted by a Regulator.
No evidence RNP AR of crew training.

## Slide 41: Air Route and Aircraft
Nominated RNP X air route
What are the aircraft requirements?
Different aircraft have different default RNP
  Need for pilots to set required RNP level
Some are still RNP 12!

## Slide 42
QUESTIONS and DISCUSSION